## Slide 1
Automated Black-Box Detection of Side‑Channel Vulnerabilities in Web Applications
Peter Chapman
David Evans
University of Virginia
http://www.cs.virginia.edu/sca/
CCS '11
October 19, 2011

## Slide 2
Side-Channel Leaks in Web Apps
HTTPS over WPA2
Client
Google
748
674
d
755
681
da
Client
Google
762
679
dan
775
672
dang
Chen⁺, Oakland 2010

## Slide 3
Modern Web Apps
Dynamic and Responsive Browsing Experience
On-Demand Content
Traffic
Latency
Responsiveness
Traffic is now closely associated with the demanded content.

## Slide 4
Motivation: Detect Vulnerabilities

## Slide 5
Motivation: Evaluate Defenses
Packet Sizes
Transfer Control Flow
Requests and Responses
Inter-Packet Timings
Randomized or Uniform Communication Attributes
HTTPOS [Luo+, NDSS 2011]

## Slide 6: Approach
Attacker Builds a Classifier to Identify State Transitions

## Slide 7: A Black-Box Approach
Full Browser Analysis
Similar to Real Attack
Scenario
Applicable to Most Web Applications

## Slide 8: Black-Box Web Application Crawling

## Slide 9: Crawljax
Web crawling back-end drives Firefox
instance via Selenium
Designed to build Finite-State Machines of AJAX Applications
http://crawljax.com/

## Slide 10: Approach

## Slide 11: Threat Models and Assumptions
No disruptive traffic
Distinguish incoming and outgoing
ISP
Access to TCP header
WiFi
Both: Victim begins at root of application

## Slide 12: Nearest-Centroid Classifier
Given an unknown network trace, we want to determine to which state transition it belongs
Classify unknown trace as one with the closest centroid

## Slide 13: Distance Metrics
Metrics to determine similarity between two traces
192.168.1 -> 72.14.204 62 bytes
72.14.204 -> 192.168.1 62 bytes
192.168.1 -> 72.14.204 482 bytes
72.14.204 -> 192.168.1 693 bytes
192.168.1 -> 72.14.204 62 bytes
72.14.204 -> 192.168.1 62 bytes
192.168.1 -> 72.14.204 281 bytes
72.14.204 -> 192.168.1 1860 bytes
192.168.1 -> 72.14.204 294 bytes
72.14.204 -> 192.168.1 296 bytes
192.168.1 -> 72.14.204 453 bytes
72.14.204 -> 192.168.1 2828 bytes
Summed difference of bytes
transferred between each party
Total-Source-Destination
192.168.1 -> 72.14.204 62 bytes
72.14.204 -> 192.168.1 62 bytes
192.168.1 -> 72.14.204 482 bytes
72.14.204 -> 192.168.1 693 bytes
192.168.1 -> 72.14.204 62 bytes
72.14.204 -> 192.168.1 62 bytes
192.168.1 -> 72.14.204 281 bytes
72.14.204 -> 192.168.1 1860 bytes
192.168.1 -> 72.14.204 294 bytes
72.14.204 -> 192.168.1 296 bytes
192.168.1 -> 72.14.204 453 bytes
72.14.204 -> 192.168.1 2828 bytes
A 62 bytes
B 62 bytes
A 482 bytes
B 693 bytes
A 62 bytes
B 62 bytes
A 281 bytes
B 1860 bytes
A 294 bytes
B 296 bytes
A 453 bytes
B 2828 bytes
Convert to string, weighted edit
distance based on size
Size-Weighted-Edit-Distance
Edit-Distance
Unweighted edit
distance

## Slide 14: Classifier Performance – Google Search
First character typed, ISP threat model

## Slide 15: Quantifying Leaks
Leak quantification should be independent of a specific classifier implementation

## Slide 16: Entropy Measurements
Problems
The same network trace can be the result of multiple classifications
Every possible network trace is unknown
Entropy measurements are a function of the average size of an attacker's uncertainty set given a network trace
Use the centroids
Number of classes
Centroid for class
Size of uncertainty set
Traditional Entropy Measurement

## Slide 17: Determining Indistinguishability
At what point are two classes indistinguishable (same uncertainty sets)?

## Slide 18: Determining Indistinguishability
Same issue with individual points.
In practice the area can be very large due to high variance in network conditions
Compare points to centroids?

## Slide 19: Entropy Distinguishability Threshold
Threshold of 75%

## Slide 20: Google Search Entropy Calculations
(measured in bits of entropy)
Threshold
We'd rather not use something with an arbitrary parameter
 | 100% | 75% | 50%
Desired | 4.70 | 4.70 | 4.70
Total-Source-Destination | 2.95 | 2.40 | 0.44
Size-Weighted-Edit-Distance | 1.13 | 0.56 | 0.44
Edit-Distance | 4.70 | 4.70 | 4.70

## Slide 21: Fisher Criterion

## Slide 22: Fisher Criterion
Marred Arthur Guinness' daughter, secret wedding (she was 17) in 1917
Arthur Guinness (1835-1910)
Ronald Fisher (1890-1962)
Developed many statistical tools as a part of his prominent role in the eugenics community

## Slide 23: Fisher Criterion
Arthur Guinness (1725-1803)
Like all good stories, this one starts with a Guinness.
“Guinness is Good for You”

## Slide 24: Fisher Criterion

## Slide 25: Google Search Fisher Calculations
Entropy Calculations
Fisher Criterion Calculations | 
Total-Source-Destination | 4.13
Size-Weighted-Edit-Distance | 41.7
Edit-Distance | 0.00
 | 100% | 75% | 50%
Desired | 4.70 | 4.70 | 4.70
Total-Source-Destination | 2.95 | 2.40 | 0.44
Size-Weighted-Edit-Distance | 1.13 | 0.56 | 0.44
Edit-Distance | 4.70 | 4.70 | 4.70

## Slide 26: Other Applications
Bing Search Suggestions
Yahoo Search Suggestions

## Slide 27: Other Applications
NHS Symptom Checker
See paper for Google Health Find-A-Doctor
Seems like a lot on this slide, perhaps divide into two (one on the search sites, one others). Could make second slide just NHS (and just a note for Google Health is in the paper) to show a bit more including web site screenshot.

## Slide 28: Evaluating Defenses
NDSS 2011
With black-box approach, evaluating defenses is easy!

## Slide 29: HTTPOS Search Suggestions
Before HTTPOS
After HTTPOS
 | 1 | 10
Random | 2.9% | 35.6%
Total-Source-Destination | 46.1% | 100%
Size-Weighted-Edit-Distance | 46.1% | 100%
Edit-Distance | 3.8% | 39.5%
 | 1 | 10
Random | 2.9% | 35.6%
Total-Source-Destination | 3.4% | 38.0%
Size-Weighted-Edit-Distance | 3.8% | 38.0%
Edit-Distance | 3.4% | 35.5%
(matches)
(matches)

## Slide 30: HTTPOS Search Suggestions
Before HTTPOS
After HTTPOS
HTTPOS works well with search suggestions
Fisher Criterion Calculations | 
Total-Source-Destination | 4.13
Size-Weighted-Edit-Distance | 41.7
Edit-Distance | 0.00
Fisher Criterion Calculations | 
Total-Source-Destination | 0.28
Size-Weighted-Edit-Distance | 0.43
Edit-Distance | 0.14

## Slide 31: HTTPOS Google Instant
Before HTTPOS
(matches)
 | 1 | 10
Random | 2.9% | 35.6%
Total-Source-Destination | 47.5% | 88.3%
Size-Weighted-Edit-Distance | 7.3% | 52.6%
Edit-Distance | 7.7% | 56.0%
 | 1 | 10
Random | 2.9% | 35.6%
Total-Source-Destination | 43.7% | 87.6%
Size-Weighted-Edit-Distance | 8.2% | 51.4%
Edit-Distance | 8.7% | 55.0%
(matches)
After HTTPOS

## Slide 32: HTTPOS Google Instant
Before HTTPOS
After HTTPOS
Fisher Criterion Calculations | 
Total-Source-Destination | 1.13
Size-Weighted-Edit-Distance | 0.34
Edit-Distance | 0.22
Fisher Criterion Calculations | 
Total-Source-Destination | 0.60
Size-Weighted-Edit-Distance | 0.55
Edit-Distance | 0.47

## Slide 33: Summary
Built system to record network traffic of web apps
Developed Fisher Criterion as an alternative measurement for information leaks in this domain
Evaluated real web apps and a proposed defense system
Code available now: http://www.cs.virginia.edu/sca
With a tutorial