## Slide 1: CS6456: Graduate Operating Systems
Brad Campbell – bradjc@virginia.edu
https://www.cs.virginia.edu/~bjc8c/class/cs6456-f19/

## Slide 2: Embedded OS: Three Key Requirements
Sharing resources
Handling concurrency
Managing limited resources

## Slide 3: Embedded hardware characteristics
Resource constrained
  10s KB RAM
  100s KB flash
  50-100 MHz CPU
  Limited energy
Hardware
  Single core
  No MMU
  Heavily relies on interrupts
Deployment
  Unattended operation
  Many separate operations

## Slide 4: Today
Three embedded operating systems
  TinyOS
  Contiki
  Tock
Three questions
  How do they enable resource sharing?
  How do they manage concurrency?
  How do they manage limited resources?

## Slide 5: TinyOS

## Slide 6: TinyOS solution
Support concurrency
  event-driven architecture
Software modularity
  application = scheduler + graph of components
  A component contains commands, event handlers, internal storage, tasks
Efficiency: get done quickly and then sleep
Static memory allocation

## Slide 7: TinyOS computational concepts
Events
  Time critical
  Caused by interrupts (Timer, ADC, Sensors)
  Short duration
Commands
  Request to a component to perform service (e.g, start sensor reading)
  Non-blocking, need to return status
  Postpone time-consuming work by posting a task (split phase w/ callback event)
  Can call lower-level commands
Tasks
  Time flexible (delayed processing)
  Run sequentially by TOS Scheduler
  Run to completion with respect to other tasks
  Can be preempted by events

## Slide 8: TinyOS Execution Model

## Slide 9: Concurrency
Two threads of execution
  Tasks
    deferred execution
    tasks cannot preempt other tasks
  Hardware event handler: respond to interrupts
    Interrupts can preempt tasks
Scheduler
  Two level scheduling
    interrupts (vector) and tasks (queue)
  Task queue is FIFO
  Scheduler puts processor to sleep when no event/command is running and task queue is empty

## Slide 10: TinyOS Execution Model (revisited)

## Slide 11: TinyOS Theory of Execution: Events & Tasks
Consequences of an event
  Runs to completion
  Preempt tasks
What can an event do?
  signal events
  call commands
  post tasks
Consequences of a task
  No preemption mechanism
  Keep code as small execution pieces to not block other tasks too long
  To run a long operations, create a separate task for each operation, rather than using on big task
What can initiate (post) tasks?
  Command, event, or another task

## Slide 12: Interface : provides & uses
Provides: Exposes functionality to others
Uses: Requires another component
Interface provider must implement commands
Interface user must implement events
Interface_A
Interface_B
Interface_C
Frame
Functions
Uses
configuration|module
Commands
Event
Events
Command
Provides
Event
Commands

## Slide 13: Applications consist of components “wired” together
Application: graph of components
  Main component
    init, start, stop
    first component executed
  Other components
Components
  modules
  configurations
Interfaces: point of access to components
  uses
  provides
Component
A
Component
B
Component D
Component
C
Application
configuration
Component
E
Component F

## Slide 14: Example: Blink Configuration
configuration Blink {
}
implementation {
components Main, BlinkM, SingleTimer, LedsC;
Main.StdControl -> SingleTimer.StdControl;
Main.StdControl -> BlinkM.StdControl;
BlinkM.Timer -> SingleTimer.Timer;
BlinkM.Leds -> LedsC;
}

## Slide 15: Example: Blink Module
module BlinkM {
provides {
interface StdControl;
}
uses {
interface Timer;
interface Leds;
}
}
implementation {
command result_t StdControl.init() {
call Leds.init();
return SUCCESS;
}
command result_t StdControl.start() {
// Start a repeating timer that fires every 1000ms
return call Timer.start(TIMER_REPEAT, 1000);
}
command result_t StdControl.stop() {
return call Timer.stop();
}
event result_t Timer.fired() {
call Leds.yellowToggle();
return SUCCESS;
}
}

## Slide 16: TinyOS Compilation
Number of resource uses known at compile time
  Memory statically allocated
All TinyOS files merged into one .c file
  Existing C compilers then just have to compile one file
    More optimization possibilities

## Slide 17: TinyOS summary
Component-based architecture
  Provides reusable components
  Application: graph of components connected by “wiring”
Three computational concepts
  Event, command, task
Tasks and event-based concurrency
  Tasks: deferred computation, run to completion and do not preempt each other
  Tasks should be short, and used when timing is not strict
  Events: run to completion, may preempt tasks
  Events signify completion of a (split-phase) operation or events from the environment (e.g., hardware, receiving messages)
Today
  Not too much active development
  NesC too much overhead
  Hardware has improved

## Slide 18: Today
Three embedded operating systems
  TinyOS
  Contiki
  Tock
Three questions
  How do they enable resource sharing?
  How do they manage concurrency?
  How do they manage limited resources?

## Slide 19: Contiki

## Slide 20: Events vs. Threads
An old debate!
Why events?
Why threads?
Contiki chooses threads

## Slide 21: Protothreads
Programmers get a thread-like interface
Only one stack shared among all protothreads
Protothreads run until they either:
  Block
    Execution state is saved
    Scheduler is invoked
  Exit
Implemented in C
  Hack using C macros

## Slide 22: Hello World in Contiki
#include "contiki.h"
#include <stdio.h> /* For printf() */
PROCESS(hello_world_process, "Hello world process");
AUTOSTART_PROCESSES(&hello_world_process);
PROCESS_THREAD(hello_world_process, ev, data)
{
PROCESS_BEGIN(&wait); printf("Hello, world\n");
PROCESS_YIELD(&wait);
printf("Hello, world again\n");
PROCESS_END();
}

## Slide 23: Ad-hoc software libraries
Impressive implementation of embedded software
Networking
  IP and IPv6 stacks
  MAC layers
  TCP and UDP
  CoAP
Software
  FTP, HTTP, MQTT
Many sensor drivers
Tradeoff:
  Integration is more difficult

## Slide 24: Interfaces exist through function pointers
 | /*
 | * The structure of a network driver in Contiki.
 | */
 | struct network_driver {
 | char *name;
 | /** Initialize the network driver */
 | void (* init)(void);
 | /** Callback for getting notified of incoming packet. */
 | void (* input)(void);
 | };

## Slide 25: Contiki
Accessible as it is written in C
https://github.com/contiki-os/contiki
  Pretty much a ghost town these days
Fork: https://github.com/contiki-ng/contiki-ng
  Opportunity to prune old cruft

## Slide 26: Today
Three embedded operating systems
  TinyOS
  Contiki
  Tock
Three questions
  How do they enable resource sharing?
  How do they manage concurrency?
  How do they manage limited resources?

## Slide 28: Tock

## Slide 29: Tock: Embedded Devices are Multiprogrammed
Multiple users running applications concurrently
Applications updated dynamically
  Small payloads better
  Buggy updates shouldn’t brick devices
Security sensitive devices want least privilege

## Slide 30: Syscall interface allows kernel to manage application access to resources
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
yield, memop, IPC
6LoWPAN
SI7021
SD Card
Console
Syscall Interface
Processes
(Any Language)
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf

## Slide 31: Different isolation primitives for an embedded OS
Processes: Use the Memory Protection Unit
Capsules: Type-safe Rust API for safe driver development
Grants: Bind dynamic kernel resources to process lifetime

## Slide 32: Tock’s Isolation Mechanisms
Capsules
Rust code linked into kernel
Isolation enforced at compile-time
Lower overhead
Used for device drivers, protocols, timers...
Cooperatively scheduled
Processes
Standalone executable in any language
Isolation enforced at runtime
Higher overhead
Applications
Time sliced
Trusted for liveness, not safety
Totally untrusted

## Slide 33: Multiple capsules enable resource sharing
SPI
Virtual SPI
SI7021
RF233
UDP
Temperature
Syscall Interface

## Slide 34: Multiple applications presents a new challenge: resource exhaustion
How many userland processes will there be?
or
How much memory should we allocate for them?
  Or, should we do dynamic memory allocation?

## Slide 35: The kernel and processes have separate memory allocations. A kernel that allows allocations would have a heap, as shown.
Data
Stack
Code
Process
RAM
Allocation
Flash
Process
Accessible
Memory
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap

## Slide 36: Tock supports multiple applications, each with their own memory allocations.
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 37: Apps are allowed to use their memory region as they see fit. For example, one app may need more heap space, another may need more stack space.
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 38: If one app exhausts its memory space, for example by making its heap too large, it will fault and the kernel can terminate just that app.
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 39: However, what happens when the app requests services from the kernel? For example, if process #1 wants the kernel to schedule a timer for it, the kernel must allocate state for that.
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 timer allocation
Data
Stack
Code
Heap

## Slide 40: Allocating state for app requests in kernel memory works for a little while…
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 allocation
P2 allocation
Data
Stack
Code
Heap

## Slide 41: But what happens when the kernel no longer has room for all of the requests? What is the kernel’s recourse? Reboot and hope it doesn’t happen again?
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 allocation
P2 allocation
P2 allocation
P2 allocation
P2 allocation
P2 allocation
Data
Stack
Code
Heap

## Slide 42: To address this, Tock introduces grants, which are regions of application memory space that the kernel uses to store the app-specific kernel state. The grant region is not accessible to the process, and the kernel does not support dynamic memory allocation.
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Data
Stack
Code
Process
RAM
Allocation
Flash
Process
Accessible
Memory
Heap
Grant section
Kernel
Accessible
Memory

## Slide 43: As processes want to use kernel resources, the state for those resources is allocated from the grant region in each process.
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Data
Stack
Code
Heap
Grant section
Timer1 allocation
BLE allocation
Data
Stack
Code
Heap
Grant section
Timer1 allocation
Timer2 allocation

## Slide 44: If one process requests too many resources, its grant section will exhaust its available memory, and the kernel can safely terminate just that process.
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Data
Stack
Code
Heap
Grant section
Timer1 allocation
BLE allocation
Data
Stack
Code
Heap
Grant section
Timer1 allocation
Timer2 allocation
Timer3 allocation
Timer4 allocation
Timer5 allocation

## Slide 45: The Rust type system and closures prevents using the grant region of terminated processes.
fn enter<'a, F>(&'a self, pid: ProcId, f: F) → where
F: for<'b> FnOnce(&'b mut T)
// Can’t operate on timer data here
timer_grant.enter(process_id, |timer| {
// Can operate on timer data here
if timer.expiration > cur_time {
timer.fired = true;
}
});
// timer data can’t escape here

## Slide 46: Tock
Pushing towards a general purpose OS on embedded HW
“Users” not statically known at compile time
Grants enable dynamic memory without crashing the kernel

## Slide 47: Today
Three embedded operating systems
  TinyOS
  Contiki
  Tock
Three questions
  How do they enable resource sharing?
  How do they manage concurrency?
  How do they manage limited resources?