## Slide 1: CS6456: Graduate Operating Systems
Brad Campbell – bradjc@virginia.edu
https://www.cs.virginia.edu/~bjc8c/class/cs6456-f19/
Slides modified from CS162 at UCB

## Slide 2: I/O In a Picture
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
I/O
Controllers
Read / Write
Read / Write
wires
interrupts
DMA transfer

## Slide 3: I/O In a Picture
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
I/O
Controllers
Read / Write
Read / Write
wires
interrupts
DMA transfer
I/O Controllers – hardware to support communication between processor and HW
Processor accesses controller’s registers as if memory
  Using memory bus or (sometimes) separate bus
Controllers signal processor through interrupts

## Slide 4: I/O In a Picture
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
I/O
Controllers
Read / Write
Read / Write
wires
interrupts
DMA transfer
Controllers communicate results through registers or direct memory access to main memory

## Slide 5: I/O Requirements
Without I/O, computers are useless!
Thousands of devices, each slightly different
Devices unreliable: media failures and transmission errors
Devices unpredictable and/or slow

## Slide 6: I/O & Storage Layers
Application / Service
Disks, Flash, Controllers, DMA
Commands and Data Transfers
I/O Driver
descriptors
File System
registers
Syscall
handles
Low Level I/O
streams
High Level I/O

## Slide 7: Operational Parameters for I/O
Data Granularity: byte (e.g., keyboard) versus block (e.g., disks and network)
Access pattern: sequential (e.g., tape) versus random (e.g., hard drive)
Transfer Notification: Polling vs. Interrupts
Transfer Mechanism: Programmed I/O versus direct memory access

## Slide 8: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity

## Slide 9: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity
Sometimes a lot of (architecture-neutral) layers in front of actual device operations

## Slide 10: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity
Other times just providing relatively direct access to devices

## Slide 11: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity
Sometimes primary “users” are parts of the OS – not user programs – but similar interface

## Slide 12: POSIX I/O: Everything is a “File”
Identical interface for:
Devices (terminals, printers, etc.)
Regular files on disk
Networking (sockets)
Local interprocess communication (pipes, sockets)
Based on open(), read(), write(), and close()

## Slide 13: Goal of the I/O Subsystem
Provide uniform interfaces (“everything is a file”)
The following code works for many devices:
FILE *fh = fopen("/dev/something", "w"); for (int i = 0; i < 10; i++) { fprintf(fd, "Count %d\n", i); } fclose(fh);
Code that actually controls devices (device drivers) provides a standard interface to kernel I/O subsystem
Kernel handles I/O syscalls by dispatching to proper driver

## Slide 14: Options for User I/O Timing
read() and write() block calling thread
Might want other choices:
  Handle multiple I/O devices in one thread
  Read data as it is available
  Queue lots of work at once without using lots of buffering in the kernel

## Slide 15: Non-Blocking I/O “Don’t Wait”
read: Just return whatever data is available
write: Just write whatever the kernel can buffer in its memory for now
So read/write calls may not read or write anything
Makes sense for network/terminal/etc.
Questionable for regular files on disk
  How much space to allocate for kernel buffers?
  What starts a read or write?
On POSIX: fcntl(fd, F_SETFL, flags | O_NONBLOCK)

## Slide 16: I/O Multiplexing: select/poll
POSIX way to wait for one of several files to have data available
Supports event-loop style programming
Indicates which file descriptors can read or write data without the need to block
Mix with non-blocking I/O

## Slide 17: select() example
int main(void) {
fd_set rfds;
struct timeval tv;
int retval;
FD_ZERO(&rfds);
FD_SET(0, &rfds); // Watch stdin (fd 0) to see when it has input.
FD_SET(my_serial_port, &rfds); // Watch on some other file descriptor.
/* Wait up to five seconds. */
tv.tv_sec = 5; tv.tv_usec = 0;
retval = select(2, &rfds, NULL, NULL, &tv); // this blocks
if (retval == -1)
perror("select()");
else if (retval)
printf("Data is available now.\n");
else
printf("No data within five seconds.\n");
exit(EXIT_SUCCESS);
}

## Slide 18: Asynchronous I/O – “Tell Me Later”
Invoke callback function with I/O op completes
User makes a call to start I/O
  Specifies buffer in userspace – source of a write or destination for a read
  Program can run on CPU while I/O happens (once it is started)
Notification might be signal, system call to poll, …

## Slide 19: Basic event loop structure
void callback1 (...) { ... }
void callback2 (...) { ... }
int library () {
event_loop(button_fd, callback1, socket_fd, callback2);
}
int event_loop(int fd1, fn fn1, int fd2, fn fn2) {
struct pollfd poll_list[2];
int retval;
// Setup list of things to wait on.
poll_list[0].fd = fd1;
poll_list[1].fd = fd2;
while(1) {
retval = poll(poll_list, (unsigned long)2 , -1);
if(retval < 0) {
fprintf(stderr,"Error while polling: %s\n",strerror(errno));
return -1;
}
// Handle the event
if((poll_list[0].revents & POLLIN) == POLLIN)
fn1();
if((poll_list[1].revents & POLLIN) == POLLIN)
fn2();
}
}
User psuedocode:
wait_for_button_press(3, function () {
printf(“button press\n”);
});

## Slide 20: Streams vs. File Descriptors
Streams are buffered in user memory:
printf("Beginning of line ");
sleep(10); // sleep for 10 seconds
printf("and end of line\n");
Prints out everything at once
Operations on file descriptors are visible immediately
write(STDOUT_FILENO, "Beginning of line ", 18);
sleep(10);
write("and end of line \n", 16);
Outputs "Beginning of line" 10 seconds earlier

## Slide 21: Why Buffer in Userspace? Overhead!
Avoid system call overhead
  Time to copy registers, transition to kernel mode, jump to system call handler, etc.
Minimum syscall time: ~100s of nanoseconds
  Read/write a file byte by byte?
  Max throughput of ~10MB/second
  With fgetc? Keeps up with your SSD

## Slide 22: Why Buffer in Userspace? Functionality.
System call operations less capable
  Simplifies operating system
Example: No "read until new line" operation
  Solution: Make a big read syscall, find first new line in userspace
  Could simulate by one syscall per character, but we already know this is a bad idea

## Slide 24: Types of Devices
Block Devices: Hard Drives, Tape Drives, etc.
  Access data in blocks (e.g. 4KB)
  open(), read(), write(), seek()
  Raw I/O or file-system access
Character Devices: Keyboards, mice, serial ports, some USB devices
  Read/write one character at a time
  Commands include get(), put()
  Libraries layered on top to allow line editing

## Slide 25: Types of Devices
Network Devices: Ethernet, Wireless, Bluetooth
  Distinct enough from block/character devices to have its own interface
  Unix and Windows include socket interface
    Separates network protocol from network operation
    Includes select (multiplexing) functionality
  Usage: pipes, FIFOs, streams, queues, …

## Slide 26: Chip-scale Features of 2015 x86
Significant pieces:
  Four CPU cores
  Integrated GPU
  System Agent (Memory and Fast I/O)
  Shared L3 cache
Integrated I/O
  Integrated memory controller (IMC)
    Two independent channels of DRAM
  High-speed PCI-Express (for GPUs)
  Direct Media Interface (DMI) Connection to PCH (Platform Control Hub)

## Slide 27: Sky Lake I/O: PCH
Platform Controller Hub
  Connected to processor with proprietary bus
    Direct Media Interface
Types of I/O on PCH:
  USB
  Ethernet
  Audio
  BIOS support
  More PCI Express
  SATA (for Disks)
Sky Lake
System Configuration

## Slide 28: Modern I/O Systems
network

## Slide 29: Flashback: Range of Timescales
Jeff Dean: "Numbers Everyone Should Know"

## Slide 30: Challenge: Range of Device Data Transfer Rates
Spans over 12 orders of magnitude
OS Goal: Low overhead for fast and slow devices

## Slide 31: How does the processor talk to the device?
CPU interacts with a Controller
  Contains a set of registers that can be read and written
  May contain memory for request queues or bit-mapped images
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address +
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

## Slide 32
Processor accesses controller’s registers in two ways
  I/O-specific instructions: in/out
    Intel: out 0x21, AL
  Memory/mapped I/O: load or store
    Registers appear in physical address space
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address +
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses
How does the processor talk to the device?

## Slide 33: Ex: Memory-Mapped Display Controller
Hardware maps control registers and display memory into physical address space
Addresses set at boot time (on modern OSs)
Simply writing to display memory (“frame buffer”) changes image on screen
  Addr: 0x8000F000 — 0x8000FFFF
Writing graphics description to cmd queue
  Set of triangles describing some scene
  Addr: 0x80010000 — 0x8001FFFF
Writing to the command register may cause on-board graphics hardware to do something
    Process current command queue
    Addr: 0x0007F004
Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical
Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 34: Transferring Data to/from Controller
Programmed I/O: Processor reads/writes data from/to device registers
  Pro: Simple hardware (control and data interfaces are the same)
  Con: I/O can consume a lot of CPU time
Direct Memory Access (DMA): I/O controller reads/writes from/to RAM without CPU
  OS specifies physical address range to use via device controller registers
  Pro: CPU can now do other things during large I/O ops

## Slide 35: Transferring Data: DMA
1
2
3

## Slide 36: Transferring Data: DMA
4
5
6

## Slide 37: I/O Devices: Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O device has encountered an error
Two options:
  Interrupts
  Polling

## Slide 38: I/O Devices: Notifying the OS
Interrupt: Device generates an interrupt whenever it needs CPU’s attention
  Pro: Handles unpredictable events well
  Con: Handling each interrupt relatively high overhead
Polling: OS periodically checks a device-specific status register
  Pro: Low overhead to run this check
  Con: May waste cycles checking for infrequent events

## Slide 39: I/O Devices: Notifying the OS
Actual devices combine both interrupts and polling
Example: High-bandwidth network adapter
  Interrupt for first new incoming packet
  OS polls for any subsequent packets until hardware queues are emptied

## Slide 40: Basic Performance Concepts
Response Time or Latency: Time to perform an operation(s)
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: MB/s, Networks: Mb/s, Arithmetic: GFLOP/s
Startup or Overhead: time to initiate an operation
Most I/O operations are roughly linear in n bytes
  Latency(n) = Overhead + n/TransferCapacity

## Slide 41: Example: Fast Network
Consider a 1 Gb/s link (B = 125 MB/s)
  With a startup cost S = 1 ms

## Slide 42: Example: At 10ms startup (More Like a Disk)

## Slide 43: What determines peak bandwidth for I/O?
Bus Speed
  PCI-X: 1064 MB/s = 133MHz x 64 bit (per lane)
  Ultra Wide SCSI = 40 MB/s
  USB 3.0 = 5 GB/s
  Thunderbolt 3 = 40 Gb/s
Device Transfer Bandwidth
  Rotational speed of spinning metal hard drive
  Write/Read rate of NAND flash
  Signaling rate of network link

## Slide 44: Example driver in Linux
CC2520 IEEE 802.15.4 (ZigBee) radio
  https://github.com/torvalds/linux/blob/master/drivers/net/ieee802154/cc2520.c