## Slide 1: Wireless for the Internet of Things Introduction to Networking
CS/ECE 4501
Spring 2024
UVA
[Pannuto, Ghena, Campbell]

## Slide 3: pollev.com/wiot

## Slide 4: Today’s Goals
Introduce layered network architecture
Introduce internet structure and services
Provide enough general networking context for this class

## Slide 5: Short term road map
This week
  Today: introduction to networking
  Wed: Wireshark lab
    Make sure to do prelab!
    This will be the only individual lab
Next week
  Mon: introduction to wireless
  Wed: introduction to Bluetooth
Next next week
  Mon: Bluetooth continued
  Wed: Bluetooth lab part A

## Slide 6: Communication layers
Application
Transport
Network
Data Link
Physical
What goes on at each of these?

## Slide 7: Internet protocol stack
application: supporting network applications
  IMAP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 8: OSI model of communication layers
Application
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
Data Link
  How to send frames of data
  Ethernet, WiFi
Physical
  How to send individual bits
  Ethernet, WiFi
CS/ECE 4457
WIoT
ECE courses

## Slide 9: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
  Packet is wrapped with header for the link to make a frame
Encapsulation is a key concept
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 10: Analogy: Sending a letter
Application: Purpose/type of letter
Transport: Carrier service
Named recipient
Network: Street Address
Courier
Mailing/shipping infrastructure
Link: Transfer to post office
Physical: Moving tangible object

## Slide 11: Host: sends packets of data
host sending function:
takes application message (string of bits, really)
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 12: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
  Packet is wrapped with header for the link to make a frame
Internet Packet
Ethernet Frame

## Slide 13: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 14: Transmitting data between networks
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
(2)
internet packet
(7)
data
PH
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header
LAN1 frame

## Slide 15: Model is not always reality
Wireless protocols don’t always split between layers cleanly
  Usually explain parts of physical, data link, and possibly upper layers
Model still helps conceptualize stack-up though
  Layering of some type still occurs

## Slide 16: Layering for IoT (joke) (kind of)
MQTT
MQTT is a publish/subscribe message broker

## Slide 17: Outline
OSI Layers
Internet Architecture (“The Upper Layers”)

## Slide 18: Order the network layers
Pollev.com/wiot
application, link, network, physical, transport

## Slide 19: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video

## Slide 20: The global Internet
Most famous example of a network
Based on the TCP/IP protocol family
  Network Layer
    IP (Internet Protocol)
      Provides a naming scheme and unreliable delivery of packets from host-to-host
  Transport Layer
    UDP (Unreliable Datagram Protocol)
      Uses IP to provide unreliable data delivery from process-to-process
    TCP (Transmission Control Protocol)
      Uses IP to provide reliable data delivery from process-to-process
Accessed via a mix of Unix file I/O and the sockets interface

## Slide 21: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when message received, or other events
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 22: Hardware and software organization of an Internet application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 23: A programmer’s view of the internet
Hosts are mapped to a set of 32-bit IPv4 addresses
  52.87.65.167
The set of IP addresses is mapped to a set of identifiers called Internet domain names
  52.87.65.167 is mapped to linklab.virginia.edu
A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 24: IP addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian)
    Remember: most computers use little-endian 😭
  True in general for any integer transferred in a packet header from one machine to another
    E.g., the port number used to identify an Internet connection
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8169071E = 129.105.7.30
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 25: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries
  Each host entry defines the mapping between a set of domain names and IP addresses
A special name: localhost
  Refers back to the computer being used (IP address 127.0.0.1)

## Slide 26: Internet connections
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
    IP address identifies the computer
    Port identifies the process on the computer
Clients and servers communicate by sending streams of bytes over connections. Most connections are:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  [TCP adds] Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.

## Slide 27: Connection performance
Assume the maximum packet size is 128 bytes. You need to send 1 KB (1024 bytes). How long will this take on a 256 kbps link (ignoring other potential delays)?
  10 milliseconds
  32 milliseconds
  4 seconds
  32 seconds

## Slide 28: Ports are used to identify services to the kernel
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 29: How does the Internet route packets? (simplified…)
IP layer
  Describes the overall goal
    Packets from my computer <---> Google
Link layer (Ethernet)
  Describes individual links
    Packets from my computer <---> McCormick Router
Routing
  Get packets from one host to another

## Slide 30: Addressing
How to solve the routing problem?
  I need to know how to get data from me to you
How does the post office work?
  I know where you live (your address)
    Zip Code
    City
    Street
    House Number
    Name

## Slide 31: Addressing
Your computer moves all the time
  Home, school, Starbucks...

## Slide 32: Addressing - Intranet and Internet
In general, network operators don’t change that often
Solution:
  Tie IP addresses to network operators
  Assign computers IPs as they join networks
  Ex: When you move apartments, you get a new address
Key Point:
  Networks “own” a block of IP address space
  “The Internet” is a network of networks

## Slide 33: Getting an IP from your building’s network\
Rice hall router “owns” 128.143.67.0-255
  This is notated as 128.143.67.0/24
  The first 24 bits are fixed, remaining 8 bits assigned to devices
cs.virginia.edu “owns” 128.143.67.11
  128.143.67.11/32, usually omit the /32

## Slide 34: Identifying your computer?
Every network card has its own MAC address
  IPs are (somewhat) dynamic, “owned” by local networks
  MACs are hardware and static, “owned” by specific computers
    Manufacturers own blocks of MACs, use them each time they make a device
Connecting to a network
  Your computer leases an IP from the local network
  Only the local router knows your MAC, everyone else sees your IP
    [n.b. this overview ignores NATs, which are commonplace today]

## Slide 35: Routing
1.0.0.0/8
5.0.0.0/8
2.0.0.0/8
10.0.0.0/8
4.0.0.0/8

## Slide 36: Routing
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 37: Routing - Adaptive
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 38: Routing – Congestion + Time

## Slide 39: Routing – Congestion + Time

## Slide 40: Routing – Other considerations [pre-2010, hah!]
Most ethernet packets have a Maximum Transmission Unit (MTU) of 1500 bytes
The fastest routers run at 10 GB/s
A 1 GHz processor can only do ~1000 instructions / packet
Tables must fit in cache
  Memory accesses would cost ~100 instructions each

## Slide 41: Some Perspective: North America (in June, 1999)

## Slide 42: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Networks of ISPs connect to provide global connectivity
IXP
IXP
access
net
access
net
regional ISP
access
net
access
net
access
net

## Slide 43: Some Perspective: The Internet

## Slide 44: So how does the Internet of Things fit into the Internet?
“IP is the Narrow Waist of the Internet”
  IP is Dead, Long Live IP for Wireless Sensor Networks
A recurring theme in this class:
  How does this actually attach to the Internet
    Physically [hello Hue Hub, Wyze Hub, August Hub, …]
    Logically [are BLE devices really part of the internet?]

## Slide 45: In which layer is…
Reliable transfer, ensuring packets successfully get from host to host?
DNS (Domain Name System), the database of mappings from domains to IP addresses.
Scheduling when a wireless device is allowed to "talk" (i.e. transmit packets).
The decision to route using Router A rather than Router B when forwarding packets.

## Slide 46: What are the steps for viewing a website?
You enter a domain name for the website
Computer looks up domain name to get IP Address
Computer sends request to IP_address:80
Computer gets back data, which it renders into a website

## Slide 47: ALL the layers
A “famous” interview question
  “What happens when you type google.com into your browser’s address bar and press enter?”
  https://github.com/alex/what-happens-when (11 pages!)
    Keyboard events
    Parsing URL
    DNS lookup
    Opening socket
    HTTP protocol
    HTML parsing
    GPU rendering

## Slide 48: Lab 1: How does your Internet work?
What can you learn about the network around you?
Play with Wireshark
Protocol analysis, introspection