## Slide 1: Wireless for the Internet of Things IEEE 802.15.4 – Mesh and Low Power MAC
CS/ECE 4501
Spring 2024
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
Understand why IoT might want to use mesh networks
Describe one possible mesh network algorithm
Investigate a decade of low power MAC research

## Slide 3: Outline
Mesh motivation
Mesh protocol (AODV)
Low power MAC

## Slide 4: Enabling full mesh networks
All nodes:
  Can send and receive data
  Route and forward data in the network
Nodes connect with their neighbors
Gateway provides access to other networks/internet
We’re interested in meshes that
  Use low power nodes (battery powered)
  Are low data rate with small packets
802.15.4 provides foundation to build mesh on top
Contention Access Period

## Slide 5: Mesh network layers
PHY Layer
  802.15.4 physical layer
MAC Layer: 802.15.4
  802.15.4 spec gives us the option of implementing our own
  Technically this layer is here, but we generally ignore it
MAC Layer
  Need to allow to TWO low power devices to communicate
  Devices are off most (~99%) of the time
  No assumption of energy asymmetry (as with PAN coordinator or BLE)
Network Layer: Mesh
  Handles organizing the network
  How should packets travel from nodes to the gateway?
  How should packets travel from the gateway to nodes?
  How should packets travel from node to node?
PHY Layer O-QPSK - 2.4 GHz
MAC Layer Low Power
Network Layer Mesh Routing
802.15.4 Contention MAC

## Slide 6: Quantitative intuition of “why bother meshing?”
Free Space Path Loss (FSPL) and the Friis transmission equation
  Measure how RF signals travel through space
  , measured in dB
  , measured in W [Friis]
  , Friis, re-written in dB
Image: https://www.sciencedirect.com/topics/computer-science/transmitting-antenna
Traditionally written as transmit distance

## Slide 7: A hand-wavy quantitative analysis of “why bother meshing”?
D-wing to E-wing is ~40m wide; how to get from one side to the other?
0 dBm
1 mW
-72 dBm (6.3e-8 mW)
-68 dBm (1.6e-7 mW)
-5.2 dBm
0.3 mW
Multi-hop mesh…
Reduces TX power
  But adds RX, sync cost!
Improves aggregate network coverage
Can improve robustness
Reduces collision domain
”reference dipole”

## Slide 8: Outline
Mesh motivation
Mesh protocol (AODV)
Low power MAC

## Slide 9: Mesh Routing
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 10: Reactive routing
Build up a map of the routes through a network
  Hopefully the “optimal” routes
Map routes in reaction to a packet arrival
  Sensor devices are slow and limited
  Most likely to resend to same prior address
  Discover a route when it is needed, then cache for next time
B Neighbor Table | 
A | c7:e3:45:00:1f:e4
C | c7:e3:45:ab:44:c6
D | 54:99:10:aa:b1:c3
B Forwarding Table | 
DST | Next Hop
F | C
A | A
A
B
C
D
E
F

## Slide 11: Neighbor discovery
Which nodes are nearby to me?
  i.e. within one packet transmission range
General Techniques
  Periodically listen for nearby transmissions
    Overhear packets
    Source addresses indicate neighbors
  Periodically send neighbor discovery probes
    Announce your existence
    Ask for neighbors to respond
  Centrally collect neighbor information
    Gateway disseminates to nodes as needed
B Neighbor Table | 
A | c7:e3:45:00:1f:e4
C | c7:e3:45:ab:44:c6
D | 54:99:10:aa:b1:c3
A
B
C
D
E
F

## Slide 12: Ad-hoc On-demand Distance Vector Routing (AODV)
On-demand: Construct routes only when needed
Modern ZigBee routing approach (for Mesh topology)
Routing table
  Destination node -> Next hop (for all cached destinations)
  Store only next hop instead of full route
    All routers along the path must also have Destination->Next mappings
  Also keep hops-to-destination and last-seen-destination-sequence-number
Route discovery
  Upon demand: check table
  If not cached send Route Request (RREQ) via Flooding
    Route is unknown, so flooding is needed

## Slide 13: AODV Route Requests (RREQs)
Request ID identifies this RREQ
  Used to discard duplicates during flooding
Sequence Numbers are per-device, monotonically increasing
  Used as a notion of “how recently” device has been seen
  Source SeqNo is the source’s most recent sequence number
  Destination SeqNo is the most recently seen from the destination by the source. (Defaults to zero)
Hop Count is the number of hops this request has taken
  Starts at 1 and incremented by each transmitter along the path
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count

## Slide 14: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
A wants to find a route to F, so it sends out an RREQ

## Slide 15: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 1
B and D also opportunistically add a routing table entry for A

## Slide 16: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
B goes first via some access control protocol (D also in contention)
A and D ignore duplicate Request ID C opportunistically adds a routing table entry to A

## Slide 17: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
D goes next by some access control protocol (C also in contention)
A, B, and C ignore duplicate Request ID E and F opportunistically adds a routing table entry to A

## Slide 18: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 3
C and E repeat this process with Hop Count 3 (but everyone ignores them)
They go one-at-a-time, but I’m getting tired of drawing these
Actually, they’re in contention with the response from F

## Slide 19: AODV Route Response (RREP)
Reply is sent unicast back to the source via newly constructed route
  Each node along the way already knows the route back
Includes most recent destination sequence number as a sense of recency
  No need for source sequence number anymore
Source Address | Destination Address | Destination SeqNo | Hop Count

## Slide 20: Example AODV RREP (F to A)
A
B
C
D
E
F
Source Address | Destination Address | Destination SeqNo | Hop Count
F | A | 7 | 2
F sends response back to A via D
D opportunistically adds a routing table entry for F

## Slide 21: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
A
B
C
D
E
F

## Slide 22: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
    RREQs:
      C -> (B,D,F)
      (B or D) -> A
      (D or F) -> E
    RREPs:
      E -> (D or F) -> C
  Network could have multiple configurations
A
B
C
D
E
F

## Slide 23: Tradeoffs for reactive routing
Upside: no transmissions unless there is demand
  Routes might appear, disappear, reappear, but no need to update if no one actually wants to transmit anything
Downside: large, variable delay when actually sending a packet
  Full RREQ/RREP protocol before data can actually be sent
  Route might have broken at some point
    So data will be sent based on cached information
    RERR will occur
    RREQ/RREP will occur
    Then data will be sent again

## Slide 24: Reliability as a cost metric
Link quality can very from node to node
  Fewest hops might not be the “fastest” or “most reliable” path
ETX: minimize “expected transmissions”
  Measure link quality over time to determine each link’s reliability
A
B
C
D
E
F

## Slide 25: Outline
Mesh motivation
Mesh protocol (AODV)
Low power MAC

## Slide 26: Asynchronous MAC principles
Communication is possible if one device is receiving while other is transmitting
Both devices want to minimize the time they are receiving or transmitting (i.e. their radio is on) to reduce power draw
Devices can only coordinate using the data communication channel (i.e. no out-of-band communication)
  No global synchronization mechanism
Goal: scheme to schedule TX and RX to permit communication while minimizing energy
Energy is paramount, but additional metrics:
  Latency
  Throughput
  Reliability
  Network scale
A
B

## Slide 28
Early 2000s

## Slide 29: Early days of low power sensor nodes
WINSng [Pottie00]
Mica [Hill01]
Rene [Hill99]
Mica2 [Xbow03]
MicaZ [Xbow05]
PC/104 [Cerpa01]
PASTA [Bajura05]
mPlatform[Lymberopoulos07]
WeC [Hill98]
WINS [Rockwell]
Stargate [Intel]
Telos/Tmote
[Polastre05]
Iris [Xbow07]
Tmote Mini
[Sentilla07]
MicaZ Stamp
[Xbow06]
Iris OEM
[Xbow07]

## Slide 30: Low power: multiple year operation using batteries
Pnode = PCPU + PTX + PRX + PSLEEP
EBATT = Pnode * lifetime
Lifetime ⬆️, Pnode⬇️
  PCPU ≫ PSLEEP
  PTX ≫ PSLEEP
  PRX ≫ PSLEEP
  → Minimize compute, TX, RX
  → Maximize sleep

## Slide 31: Low power MAC principles
Communication is possible if one device is receiving while other is transmitting
Devices can only coordinate using the data communication channel (i.e. no out-of-band communication)
  No global synchronization mechanism
Goal: scheme to schedule TX and RX to permit communication while minimizing energy
Energy is paramount, but additional metrics:
  Latency
  Throughput
  Reliability
  Network scale
A
B
Both devices want to minimize the time they are receiving or transmitting (i.e. their radio is on) to reduce power draw

## Slide 32: Low Power Listening (LPL) - B-MAC (2004)
Method:
  Receiver periodically samples the channel
  Transmitter sends a preamble long enough to ensure receiver will detect it
  Upon detection, receiver stays awake to receive transmitted packet
  Receiver ACKs if packet received correctly
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004
CCA
TX ACK
RX ACK

## Slide 33: LPL performance
CCA check interval
  Too small: energy wasted on idle listening
  Too large: energy wasted on transmissions (long preambles)
In general, it’s better to have larger preambles than to check more often!
Sensor sample period – controls the packet rate
Time between listening
(checking if the channel is idle)
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 34: LPL Drawback
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
CCA
TX ACK
RX ACK
Spend time listening to packets for someone else!
A
B
C
CCA
Receiver
Sleep
Sleep
CCA
Sleep
RX
Sleep
CCA
Sleep
CCA
DROP
A
B
C
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 35: X-MAC: Shorter preambles and destination information
Method
  Transmitter sends a short “I have a packet for this address” packet
  Nodes periodically listen, and ACK if the packet is for them
  Upon receiving the ACK, the transmitter sends full packet
  Receiver successfully receives the full packet.
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
TX (DST ID)
TX (DST ID)
TX (DST ID)

## Slide 36: X-MAC: Overhearing node drops out early
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX (DST ID)
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
RX
Overhearer
Sleep
Sleep
RX
Sleep
C
TX (DST ID)
TX (DST ID)
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 37: X-MAC: lower power draw than LPL with multiple nearby transmitters
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 38: LPL (B-MAC) and X-MAC are transmitter initiated MAC protocols
Receiving nodes continuously periodically sample the wireless channel
  When they detect a transmission they listen to receive packets
Transmitting nodes are only active when they want to transmit
Receiving nodes prone to unnecessary wakeups
  Have to receive all nearby transmissions to see if the packet happens to be for them
  Unnecessary wakeups lead to increasing receive energy  shorter lifetime
  In general, difficult for receiver to know if it should stay awake or go back to sleep

## Slide 39: Low Power Probing (LPP) is receiver initiated
Method
  Receiver periodically transmits a probe, listens afterward
  Transmitter listens for probe packet from intended recipient
  Transmitter sends packet after receiving the correct probe packet
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX ACK
A
B
RX ACK
TX Probe
TX Probe
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.
RX
RX

## Slide 40: LPP introduces a new challenge for multiple nodes. What happens with multiple transmitters?
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX Probe
TX Probe
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.
If multiple transmitters receive a probe, they both transmit, leading to a collision and a lost packet
Receiver is unsure if there actually was a packet, or just noise/interference on the channel
Transmitter
Sleep
TX
Sleep
RX
Collision!!

## Slide 41: A-MAC resolves this with backcast constructive interference
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
RX
TX ACK
TX Probe
RX ACK
TX Probe
Method
  Transmitters send an ACK in response to a probe packet
  With multiple transmitters, the ACKs collide, but interfere non-destructively, so the receiver still receives an ACK
  The receiver stays awake to receive a packet, but the packet collides
  The receiver sends a new probe, informing transmitters there was a collision
  Transmitters use CSMA/CA to send packets
Transmitter
Sleep
TX
Sleep
RX
TX ACK
Collision!!
Design and Evaluation of a Versatile and Efficient Receiver-Initiated Link Layer for Low-Power Wireless. Prabal Dutta, Stephen Dawson-Haggerty, Yin Chen, Chieh-Jan Mike Liang, and Andreas Terzis. SenSys 2010.
TX Probe
CCA
TX
CCA
RX
Listen
TX ACK
CCA
RX
TX ACK
TX
RX ACK
RX ACK
Sleep
RX
RX
Listen

## Slide 42: Summary: asynchronous low power MAC protocols
Transmitter initiated protocols
  Receivers periodically sample the channel
  Transmitters transmit sufficiently to ensure recipients heard
  Examples: LPL, X-MAC
  Pros:
    Simple, intuitive
    Can balance TX and RX energy with sample interval
  Cons:
    Receivers prone to false wake-ups
    High idle listening energy costs
Receiver initiated protocols
  Receivers periodically transmit probes
  Transmitters listen for a probe before sending a packet
  Examples: RI-MAC, Koala, A-MAC
  Pros:
    Fixed, small listening energy cost for receivers
  Cons:
    Multiple transmitters leads to collisions

## Slide 43: Mesh network layers
PHY Layer
  802.15.4 physical layer
MAC Layer: 802.15.4
  802.15.4 spec gives us the option of implementing our own
  Technically this layer is here, but we generally ignore it
MAC Layer
  Need to allow to TWO low power devices to communicate
  Devices are off most (~99%) of the time
  No assumption of energy asymmetry (as with PAN coordinator or BLE)
Network Layer: Mesh
  Handles organizing the network
  How should packets travel from nodes to the gateway?
  How should packets travel from the gateway to nodes?
  How should packets travel from node to node?
PHY Layer O-QPSK - 2.4 GHz
MAC Layer Low Power
Network Layer Mesh Routing
802.15.4 Contention MAC