## Slide 1: Wireless for the Internet of Things NFC
CS/ECE 4501
Spring 2024
UVA
[Pannuto, Ghena, Campbell]
No quiz, kinda.

## Slide 2: Protocols explored so far
BLE Advertisements
BLE Connections
IEEE 802.15.4 (raw)
Thread (based on 802.15.4)

## Slide 3: Throughput vs. Range
Data
Throughput
Range

## Slide 4: Complexity vs. Power
Sensor/Device Complexity
Power

## Slide 5: Latency vs. Network Type
Time until first byte transferred
Network Type
One-to-one
Many-to-many

## Slide 6: Comparing protocols
What protocol should I use?
  I have two IoT devices: CO2 sensor and fan. I want the fan to turn on when CO2 rises above a threshold.
  I have a sensor on a bus to measure bus occupancy and want to track bus use in real time.
  I have a restaurant and I want my customers to be able to quickly load today’s menu.
Data
Throughput
Range
Sensor/Device Complexity
Power
Time until first byte transferred
Network Type
One-to-one
Many-to-many
BLE Advertisements
BLE Connections
IEEE 802.15.4 (raw)
Thread (based on 802.15.4)

## Slide 7: Outline
Comparing networks
Backscatter and RFID
NFC

## Slide 8: Resources
This Bell Labs instructional video from 1959 is excellent background:
  https://www.youtube.com/watch?v=DovunOxlY1k

## Slide 9: What does an antenna do?
Loosely: Converts between electric and magnetic waves
Animation by Chetvorno - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=40789783

## Slide 10: What generates electric waves?
RF front end
  can be done with high-speed digital components (e.g. fast DACs)

## Slide 11: What receives electric waves?
Could be a high-speed ADC, more often with analog pieces in front:
Graphics from Analog Devices whitepaper: https://www.analog.com/media/en/technical-documentation/tech-articles/480501640radio101.pdf — significantly more detail here

## Slide 12: What happens if nothing ‘receives’ the wave?
From: https://www.flippingphysics.com/standing-waves.html

## Slide 13: “Fixed end” and “Free end” in electronic transmission
~
~
Short Circuit = “Free End”
- Reflects wave
Open Circuit = “Fixed End”
- Inverts wave
~
Matched Load
- Absorbs wave (no reflection)

## Slide 14: Backscatter systems reflect waves rather than generate waves — significant (10,000x or more) power savings
Simple versions just ‘reflect or don’t reflect’
Modern designs can do more advanced modulation as well
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=8368232

## Slide 15: Backscatter is an old idea — history in spycraft!
1945: Leon Theremin* creates “The Thing” (aka Great Seal Bug)
  *Yes, same guy who invented the instrument
  Discovered when a British embassy radio operator heard recorded conversations

## Slide 16: Outline
Comparing networks
Backscatter and RFID
NFC

## Slide 17: RFID is everywhere nowadays
Fundamental design principle is asymmetry
  Extremely simple, cheap tags
  Complex readers

## Slide 18: A brief digression to be precise in terminology
RFID = Radio Frequency Identification = “a” communication standard
  A ton through ~early 90’s; “EPC” ~= UPC, standardized; most now EPC Gen2
There are actually three types of “RFID” device
  Passive Tags - harvest power from reader & reflect
  Semi-Passive Tags - on-board power, but reflect data
  Active Tags - on-board power that transmit data
These are ”backscatter” — which describes any communication via reflected RF
Notes: The point: Papers misuse “RFID” to mean backscatter, and misuse “passive tag” to mean anything that doesn’t actively emit RF.
Most things that do backscatter don’t do the energy harvesting bit
Many papers that do backscatter describe themselves as RFID, but don’t follow any RFID communication standard

## Slide 19: The meaningful difference is in how the tag devices power themselves
Even on simple designs, need some power:
Let’s look at E-ZPass again:

## Slide 20: Let’s look at RFID standards to get a sense of the numbers
Low Frequency (~300 kHz) — mostly legacy
  ~10cm read range
High Frequency (3~30 MHz; often 13.56 MHz)
  Passive: 4~7 m max
  Semi-Passive: 10~30 m max
  Active: 30+ m
Ultra-High Frequency (300 MHz ~ 3 GHz)
  Passive: Up to 12 m
  Active: Up to 100 m

## Slide 21: Outline
Comparing networks
Backscatter and RFID
NFC

## Slide 22: Applications of NFC

## Slide 24: What is NFC?
NFC = Near Field Communication
A short-range wireless connectivity technology
  Operates at 13.56 Mhz
  Based on RFID technology
  Data transfer rate: up to 424 kbits/second
  < 20cm range
  Reader & Tag communicate
  Promoted by the NFC-Forum

## Slide 25: NFC History
Year | Event
1983 | The first patent to be associated with RFID was granted to Charles Walton
2002 | NXP Semiconductors and Sony co-invent NFC
2004 | Nokia, Phillips and Sony established the NFC forum
2006 | Initial specifications for NFC Forum Tags and “Smart Poster” records
2006 | Nokia launches the first NFC phone (Nokia 6131)
2009 | NFC Forum releases Peer-to-Peer standards
2010 | Samsung, Nexus 5: First Android NFC phone shown
2010 | AT&T, Verizon, T-Mobile announces Softcard mobile payment joint venture
2011 | Google I/O “How to NFC” demonstrates NFC to initiates a game and to share a contact, URL, app, video, …
2011 | RIM is 1st company for its devices is certified by Mastercard worldwide, the functionality of PayPass
2012 | Samsung introduces TecTile, a set of NFC stickers and a companion App for Android to read/write TecTile
2012 | Sony introduces “Smart Tags” using NFC technology to change modes and profiles on Sony smart phone
2012 | Wired US is the 1st mass market publication to feature NFC enable advertisements
2013 | Samsung and Vise announces major partnership to develop mobile payments
2014 | Apple introduces iPhone 6 with Apple Pay using NFC Technology

## Slide 26: NFC Operation
NFC communication between two devices is the same as traditional 13.56 MHz RFID.
The NFC network consists of two communication terminals:
  The NFC Initiator/Reader to start the communication.
  NFC initiator continuously emits RF carrier signals and keeps observing for modulation to occur. Detected modulation of the field would indicate of the presence of a target.
The Target/Tag receives the Initiator’s communication request and sends back a reply.
When the NFC target absorbs sufficient energy emitted by the reader, it starts sending modulated information back to the initiator.

## Slide 27: NFC Active and Passive Devices
Active NFC device is usually a microcontroller based like a NFC enabled smartphone, would not only be able to collect information from NFC tags, but it would also be able to exchange information with other compatible phones or devices and could even alter the information on the NFC tag if authorized to make such changes.
A passive device, such as an NFC tag, contains information that other devices can read but does not read any information itself. NFC tag does not have its own power source.

## Slide 28
DATA RATE & RANGE

## Slide 29: NFC RF signal coding
DATA RATE KBPS | ACTIVE DEVICE | PASSIVE DEVICE
106 | Modified Miller, 100%, ASK | Manchester, 10%, ASK
212 | Manchester, 10%, ASK | Manchester, 10%, ASK
424 | Manchester, 10%, ASK | Manchester, 10%, ASK
NFC employs two different coding systems on the RF signal to transfer data.
Modulation Index = (A-B)/(A+B) where A = Unmodulated signal amplitude B = Modulated signal amplitude Modulation Depth = B/A 10% ASK modulation means ASK modulation in which modulation index will range between 8% and 14%.
100% ASK means ASK modulation in which modulation and carrier amplitude are almost equal.

## Slide 30: NFC and Manchester coding
Manchester coding used for NFC data transfer
Manchester coding maps bits to transitions
  Bit 0  low to high
  Bit 1  high to low
Prevents long runs of high or low values

## Slide 31: NFC and Modified Miller coding
Modified Miller coding used for NFC data transfer used for 106 kbps active device transfers
Mapping bits to pulses
  1  Late low pulse
  0 
    Following a 0: Early low pulse
    Following a 1: Stay high
Mimics frequency modulation

## Slide 32: Manchester modulation NFC signal

## Slide 33: NFC Modes oh my!
There are three main operating modes for NFC:
  Card emulation mode (passive mode): the NFC device behaves like an existing contactless card conforming to one of the legacy standards
  Peer-to-peer mode: two NFC devices exchange information. The initiator device (polling device) requires less power compared to the reader/writer mode because the target (listener) uses its own power supply.
  Reader/writer mode (active mode): the NFC device is active and reads or writes to a passive legacy RFID tag.

## Slide 34: NFC Tags – Encoding data
NDEF (NFC Data Exchange Format) Structure
  Binary format for data
  Messages contains records
  Each record has header
NFC read returns the NDEF message

## Slide 35: NFC Forum NDEF record types
Record Type Definitions
  RTD Technical - Specifies the format and rules for building standard record types used by NFC Forum application definitions and third parties that are based on the NDEF data format.
  Text - Provides an efficient way to store text strings in multiple languages by using the RTD mechanism and NDEF format. An example of using this specification is included in the Smart Poster RTD.
  URI - Provides an efficient way to store Uniform Resource Identifiers (URI) by using the RTD mechanism and NDEF format. An example of using this specification is included in the Smart Poster RTD.
  Smart Poster - Defines an NFC Forum Well Known Type to put URLs, SMSs or phone numbers on an NFC tag, or to transport them between devices. The Smart Poster RTD builds on the RTD mechanism and NDEF format and uses the URI RTD and Text RTD as building blocks.
  Generic Control - withdrawn
  Signature - Specifies the format used when signing single or multiple NDEF records. Defines the required and optional signature RTD fields, and also provides a list of suitable signature algorithms and certificate types that can be used to create the signature. Does not define or mandate a specific PKI or certification system, or define a new algorithm for use with the Signature RTD.
  PHDC - Addresses a need for an openly-defined standard for the exchange of personal health data between devices using Near Field Communication technology.
Derived types
  Android Application NDEF Record
  Application NDEF Record
  Contact NDEF Record
  Email NDEF Record
  File NDEF Record
  Geolocation NDEF Record
  Phone NDEF Record
  SMS NDEF Record
  Website NDEF Record
  WiFi NDEF Record

## Slide 36: NDEF Format

## Slide 37: Let’s try it!
Install NFC tools
What NFC cards do you have?
I have a writeable NFC tag
  Write something to the tag and pass to the next table