## Slide 1: Wireless for the Internet of Things LoRa
CS/ECE 4501
Spring 2024
UVA
[Pannuto, Ghena, Campbell]
While we get started, take the quiz on canvas!

## Slide 2: Today’s Goals
Explore another point in the wireless design space
Introduce emerging protocol
Show how we are using LoRa

## Slide 3: Outline
Wide-Area Network Background
LoRA
LoRaWAN
Charlottesville Deployment
  The Things Network

## Slide 4: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 5: How do we collect data from MANY sensors?
Manually collect measurements
Connect it to WiFi (or Ethernet)
Pay for cellular access

## Slide 6: 2.4GHz protocols mostly used for indoor applications
Range for the wireless protocols we’ve looked at so far (best case)
  BLE: 100m (~300ft)
  802.15.4: 100m (~300ft)
  NFC: 20cm (~1ft)

## Slide 7: We need another network option
What requirements do we have?
  Wide area of coverage
    Deploy fewer gateways
  Low power
    So we can deploy on batteries
What requirements do we NOT have?
  Doesn’t need high throughput
    Sensor data is relatively small

## Slide 8: Wide area networks
Communication at the region/city scale rather than the building/residence scale
  Throughout cities
  Agricultural deployments
  Industrial facilities
City-scale sensing is one very popular domain
  What might we want to sense throughout a city?

## Slide 9: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
3G
4G
BLE
802.15.4
Low-Power Wide-Area Networks
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
2G
NFC
5G

## Slide 10: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate: 100 kbps or less
Range on the order of multiple kilometers
Simple ALOHA access control

## Slide 11: Outline
Wide-Area Network Background
LoRA
LoRaWAN
Charlottesville Deployment
  The Things Network

## Slide 12: LoRa (Long Range)
Proprietary LoRa physical layer
  Owned by Semtech
Low data rate (1-20 kbps) and long range (~5 km)
Most popular LPWAN protocol
  Target of academic research
  Industry involvement in hardware and deployments

## Slide 13: LoRa PHY uses a spread spectrum modulation technique
Chirp Spread Spectrum (CSS)
  Modulation technique where frequency is varied linearly from (to) lowest to (from) highest within a channel

## Slide 14: How does FSK, up-chirp, and down-chirp “sound” like?
Source: LoRa CHIRP by Richard Wenner

## Slide 15: Data Modulation in Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel
+
Input Binary Data

## Slide 16: Data Modulation in Chirp Spread Spectrum
In general,
n bits => divide BW to 2n initial frequencies
Remember, No. of symbols = 2n
Source: https://swarunkumar.com/slides/choir-sigcomm2017.pdf

## Slide 17: LoRa Modulated Signal
Source: https://youtu.be/lg0eZWZFKiE

## Slide 18: CSS has a Spreading Factor which determines bit rate
Spreading Factor is essentially the rate-of-change of frequency (sweep rate)
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision
LoRa has 6 spreading factors:
SF7 to SF12
Notes: https://www.thethingsnetwork.org/docs/lorawan/spreading-factors/

## Slide 19: LoRa channels (in the US)
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not used in practice)
Eight, 500 kHz downlink channels

## Slide 20: LoRa gateways
No synchronization with end devices
Instead listen to entire bandwidth simultaneously
  Only 12 MHz total
  Recognize preambles and allocate hardware to decode packet
    Cheap gateways: 8 decoders
    Good gateways: 64 decoders

## Slide 21: LoRa data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate options depend on channel in use
  Unbalanced uplink and downlink
64-channel uplink
  1-5 kbps data rate
Allowable rates based on US dwell time restriction (400 ms)
  Different in different regions
Notes: Dwell time (or transmit time) is the amount of time needed to transmit on a frequency

## Slide 22: LoRa link budget
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is about a kilometer in urban environments

## Slide 23: Outline
Wide-Area Network Background
LoRA
LoRaWAN
Charlottesville Deployment
  The Things Network

## Slide 24: LoRa vs. LoRaWAN
LoRa: physical layer protocol
LoRaWAN: MAC and network layer
(In practice we often conflate LoRa and LoRaWAN.)
https://lora-developers.semtech.com/documentation/tech-papers-and-guides/lora-and-lorawan/

## Slide 25: LoRaWAN MAC
Uplink: ALOHA - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: LoRaWAN has 3 types of device classes based on RX behavior (Class A, B, and C)
Notes: Aloha: send without sensing, if collision, wait for random delay and then send again

## Slide 26: LoRaWAN has Device Classes based on RX behavior
Listen-after-send (class A device)
  Two windows for RX on different channels
Periodic listening (class B device)
  Also has 2 RX windows after TX
  Synchronized with periodic beacons
  Has periodic ping slots (RX windows)
  Gateway can reach without waiting for TX
Continuous listening (class C device)
  Always-on receivers
Good Reference: https://www.thethingsnetwork.org/docs/lorawan/classes/

## Slide 27: LoRaWAN packet format
Frame header includes device address
MAC Payload maximum size depends on data rate
Data Rate Index | MAC Payload Size
0 | 19 bytes
1 | 61 bytes
2 | 133 bytes
3 | 250 bytes
4 | 250 bytes

## Slide 28: LoRaWAN star-of-stars topology
https://www.researchgate.net/publication/360965985_LoRaWAN_Communication_Protocols_A_Comprehensive_Survey_under_an_Energy_Efficiency_Perspective
Each gateway is a star network
Many gateways connect to a LoRaWAN backend

## Slide 29: LoRaWAN device abstraction
LoRaWAN Network
Application Server

## Slide 30: LoRaWAN network details

## Slide 31: LoRaWAN hardware
Numerous hardware modules and development kits
  Almost all use Semtech radio chips (Semtech owns LoRa PHY)
Recent addition: STM32WLE5 LoRa SoC
  Cortex-M4 + LoRa radio (analogous to nRF52840)

## Slide 32: Note about LoRa hardware
LoRa PHY is patented
Hardware controlled by Semtech
Good for interoperability
Openness?
Innovation?

## Slide 33: Joining a LoRaWAN network
Two modes:
  OTAA (Over the air activation): Dynamic join procedure that sets up security keys
  ABP (Activation By Personalization): Legacy approach with pre-shared security keys
OTAA Joining: two packets
  Join-request: from end device to the Network Server
  Join-accept: from Network Server to the end device

## Slide 34: OTAA Join Procedure
Device knows three things:
AppEUI: Identifier for the application the device uses on the application server
DevEUI: Device ID
AppKey: AES-128 bit secret registered with the network server
Join Request
Device sends (AppEUI, DevEUI, Nonce) and MIC using AppKey
Join Accept
Network server responds with AppNonce encrypted with AppKey
Device and network server compute the same AppSKey to encrypt all future payloads

## Slide 35: LoRaWAN network providers
You can always manage your own network
  Buy a gateway and run whatever backend software you want
Managed network providers
  The Things Network
  MachineQ from Comcast

## Slide 36: TTN Scale [Mar 2023]

## Slide 37: TTN Scale [Mar 2024]

## Slide 38: Outline
Wide-Area Network Background
LoRA
LoRaWAN
Charlottesville Deployment
  The Things Network

## Slide 39: Charlottesville TTN Network

## Slide 40: LoRa gateway operational at Rice Hall

## Slide 41: LoRaWAN Gateway Install – UVA Aerospace Research Lab

## Slide 42: Water Level Sensor Prototype

## Slide 43
LoRa gateway
335 m
55 m
Sensor nodes
Weather Station
CO2, Temperature, and Humidity Sensors

## Slide 44: LoRaWAN Sensors @ UVA
Temperature, Humidity, CO2

## Slide 45
Outdoor sensors @ UVA
Water depth sensing at Dell Pond

## Slide 46: RSSI values from the LoRaWAN field test

## Slide 47: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink

## Slide 48: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink
Outdoor small-sized sensing seems possibly achievable!
  With a low enough rate, it could support many devices
Code updates on devices could be tough

## Slide 49: Outline
Wide-Area Network Background
LoRA
LoRaWAN
Charlottesville Deployment
  The Things Network
Bonus: Research for Improving LoRaWAN

## Slide 50: Unlicensed LPWANs is a very active research area
Active work on:
  Better access control mechanisms
  Increasing bandwidth by utilizing other spectrums like TV white spaces
  Recover simultaneous transmissions
    Goal: reduce re-transmissions, increase end-device sleep and battery life
Let’s look at some tricks people have done to recover simultaneous transmissions!

## Slide 51: Resources
Swarun Kumar (CMU) - https://swarunkumar.com/lpwan.html
Choir
  https://swarunkumar.com/papers/choir-sigcomm2017.pdf
  https://swarunkumar.com/slides/choir-sigcomm2017.pdf
Charm
  https://swarunkumar.com/papers/charm-ipsn2018.pdf
Opportunistic Packet Recovery
  https://swarunkumar.com/papers/opr-mobisys2020.pdf

## Slide 52: Can we distinguish data from LoRa chirps that have collided?

## Slide 53: Choir concept
  Yes! By applying signal processing to the problem
Data in time domain
Data in frequency domain

## Slide 54: Background: Fast Fourier Transform (FFT)
Converts individual signal to its spectral components
https://www.nti-audio.com/en/support/know-how/fast-fourier-transform-fft
Interesting read: Cocktail Party Audio data separation using FFT

## Slide 55: What happens when LoRa chirps collide?

## Slide 56: What happens when LoRa chirps collide?

## Slide 57: Imperfections in hardware create offsets

## Slide 58: Decoding colliding packets

## Slide 59: Choir results
Recovering collided packets resolves losses due to Aloha transmission!
Increases maximum throughput on the network considerably!
Does require modifications to hardware on gateways though

## Slide 60: Can we recover weak LoRaWAN signals?

## Slide 61: Charm
Take advantage of multiple gateways in range of a device
Combine signals received at each gateway to recover packets that weren’t received cleanly

## Slide 62: Coherent combining
Signal received at each receiver is a combination of
  Signal
  Wireless channel
  Random noise
Signal and wireless channel are similar at all receivers
Noise is different though! Independent
When combined, signals are coherent (build in strength) whereas noise is incoherent (spreads out)

## Slide 63: Charm uses coherent combining across gateways
Gateways send signal data to the cloud
The cloud can perform combining on the data and recover signals
Challenges
  Only send the data when it’s needed
  Tight time synchronization on the data
  Gateway hardware changes

## Slide 64: Can we recover packets that have bad CRCs?

## Slide 65: Opportunistic Packet Recovery (OPR)
What if we have some information about where the interference might have occurred during the signal transmission?
OPR demonstrates that we can recover packets!
Process
  Receive bits even for bad packets
  Measure RSSI for each bit along the way
  Look for changes in RSSI that signals interference
  Try different values for the effected bits until the CRC succeeds!

## Slide 66: Detecting error bits in transmitted packets
Correctly identifies 83% of the corrupted bits with 17% false positives

## Slide 67: Multiple gateways do even better
If multiple gateways receive the packet, they can compare their received data
Common bits are likely correct, while differences are likely interference

## Slide 68: OPR total design
Bad packets are sent to the OPR Server for handling along with RSSI data
OPR server attempts to reconstruct the packet
In practice, system can correct up to 72% of CRC errors!
  Also completes correction in time for the ACK response (within 1 second)

## Slide 69: Resources
LoRaWAN
  LoRaWAN Specification version 1.1
  LoRaWAN Regional Parameters version 1.0.2