## Slide 1: Cinamin A Perpetual and Nearly Invisible BLE Beacon
Brad Campbell, Josh Adkins, and Prabal Dutta
University of Michigan
bradjc@umich.edu
NextMote Workshop
February 15, 2016
Graz, Austria

## Slide 2: What could we do with tiny Bluetooth Low Energy beacons that we could affix to everything?

## Slide 3: Existing BLE beacons are too big and have limited lifetimes
Size is dictated by the battery
Sufficient for certain applications
  Battery replacement OK in limited scale
Truly pervasive deployments will require smaller beacons with no maintenance needs

## Slide 4: Several trends are making miniature and pervasive BLE beacons possible
Beacon Requirements are Simple
Smart Dust is the Ultimate Goal
BLE Radios are Competing on Power
TX only
Repeated payload
Energy-Harvesting can Eliminate Batteries
COTS chips at 4.9 mA TX
Minimize size
Potential for perpetual operation
Not yet accessible

## Slide 5: Cinamin: A BLE Beacon in Under 100 mm3
Three main systems
  Solar Cell
  Power Supply
  BLE Radio
Radio/Antenna
PCB
Power Supply
Solar Cell
0.60 mm
0.50 mm
0.80 mm
1.50 mm
5 mm x 5 mm
≈85 mm3
CR2032 Battery for scale
COTS parts

## Slide 6: Operation: Charge capacitor to transmit a packet
BLE
Power Supply
Harvesting:
2.5-4.25 uW
Power Supply PQ:
60-990 nW
Leakage:
≈1 uW
TX: 13-34 uJ
Sleep: 1-3 uW
Startup: 6-58 uJ

## Slide 7: Between advertisements, is it better to sleep or shutoff and re-initialize?
(PHARVEST − PLOSS − PSLEEP) · tperiod
ESTARTUP + EADV
=
Incoming
Energy
Outgoing
Energy
In cold boot operation, we eliminate the PSLEEP cost.
In sleep-mode operation, we eliminate the ESTARTUP cost.

## Slide 8: At very low incoming energy levels, PSLEEP dominates
(PHARVEST − PLOSS − PSLEEP) · tperiod = ESTARTUP + EADV
Notes: Dialog DA14581: Cross: 5.8 uW
IcyTRX-65: Cross: 4.2 uW
Dialog DA14581: tperiod: 12 seconds
IcyTRX-65: tperiod: 6 seconds

## Slide 9: How to increase PHARVEST? Move the beacon closer to the light!
Irradiance ∝ 1/distance2

## Slide 10: At 100 mm3, the beacons just look like dirt

## Slide 11: Or bugs

## Slide 12: Let’s look further! What can we do with best-published technology?
Both very close to light
Best published results for Solar Cell, Supercap, and BLE Radio
Assume no losses
Notes: Da14581: 0.15 pkts/second, IcyTRY-65: 0.5 pkts/second
Best: Aluminum gallium arsenide solar cells + graphene super capacitor + BLE transciever = 1.5 pkts/second, near light: 3.3 pkts/second
Theoretical:
- no leakage, all power tx: 7 pkts/second
- perfect solar cell: 28 pkt/second
- next to light: 60 pkt/second

## Slide 13: Challenges in achieving this scale today
Need better power supply options
  Match voltage thresholds to BLE chip being used
  Minimize IC size and quiescent current
  Automatically switch between cold-boot and sleep
Need a suitable solar panel
  Ideally designed for indoor lighting
  Difficult to find in this form factor
Will a COTS antenna actually work?
  Can find small antennas, but have to violate keepout
  Short range may be acceptable

## Slide 14: Conclusion
Cinamin is a design for a BLE beacon that can [likely] be built today
Better enable applications that blend the physical and digital worlds
Further work needed to explore the tradeoffs in operating modes and hardware designs
Brad Campbell
University of Michigan

## Slide 15
Backup Slides

## Slide 16: Best-published technologies
Aluminum gallium arsenide solar cells
  “AlGaAs Photovoltaics for Indoor Energy Harvesting in mm-Scale Wireless Sensor Nodes”
  Alan S. Teran, Jamie D. Phillips, et al.
Graphene supercapacitors
  “Scalable fabrication of high-power graphene micro-supercapacitors for flexible and on-chip energy storage”
  Maher F. El-Kady & Richard B. Kaner
BLE Transceiver
  “13.2 A 3.7mW-RX 4.4mW-TX fully integrated Bluetooth Low-Energy/IEEE802.15.4/proprietary SoC with an ADPLL-based fast frequency offset compensation in 40nm CMOS”
  Yao-Hong Liu, et al.
  ISSCC 2015