## Slide 1: An Overflow-free Quantized Memory Hierarchy in General-purpose Processors
Marzieh Lenjani , Patricia Gonzalez ,
Elaheh Sadredini , M Arif Rahman, Mircea R. Stan
Notes: Hello eveyone, I am Marzieh, I am presenting my paper: An Overflow-free Quantized Memory Hierarchy in General-purpose Processors
1

## Slide 2: Characterization for design optimizations

## Slide 3: How about summarizing characterizations into an abstraction?
@characteristics
<…, …, ….>
OS and MMU

## Slide 4: Characteristics as abstractions for memory-intensive application
  What is different about memory-intensive applications?
  Few computations per loaded datum
Notes: Our work targets memory-intensive applications, because many of the modern applications are memory intensive
For example …..
So the question is what is different about memory-intensive applications
The main difference is that there few computations per loaded datum in memory-intensive applications

## Slide 5: Cost of data movement in memory-intensive applications
Cost of each data movement >> Cost of each computation
[1]. Han, Song, et al. "EIE" ISCA 2016.
Memory-intensive application
  Few computations per data movement
Memory to L1
>1000x more energy
>100x more latency
An ADD operation
  Data movement dominates the
  execution time and energy consumption

## Slide 6: Outline
Reducing the cost of data movement
  Approach1: Cache compression
  Approach2: Truncating LSBs
  Approach3: Quantization
Quantization in general-purpose processors
Characteristics as abstractions
Evaluation
Conclusion
Notes: Here is the outlie of this talk. First, I will talk about high cost of data movement in modern processors, and then explain how approximate computing can solve this and then introduce two major approach in approximate computing, then I will talk about the goal of this

## Slide 7: Approach1: Cache compression
L2
Compressor/
decompressor
A compressed cache block
A cache block
LLC
Memory
Processor

## Slide 8: Compressor/decompressor obliviously looks for value locality
L2
Compressor/
decompressor
A compressed cache block
A cache block
  Problem1: Complex compression/decompression
LLC
Memory
Processor

## Slide 9: Metadata per block
Compressor/
decompressor
A compressed cache block
A cache block
  Problem2: Significant metadata overhead
Metadata overhead

## Slide 10: Variable block size
  Problem3: Complex address translation
B3
B2
B1
Pointer to B1
Pointer to B2
Pointer to B2
L3:Data array
L3:Tag array
L2

## Slide 11: Low value locality
High variation in LSB
  Low value locality
Complex structures
  Low value locality
  Problem4: Low compression ratio
Sign
Exponent (8 bits)
Mantissa ( 23 bits)
Struct element{
float Price;
bool type;
float yield}
True
87.89
XXXXXXX
0.2
price
type
Unused
yield

## Slide 12: Approach2: Truncating LSBs
Approximate computing
  Many applications can tolerate imprecise variables
    [Example: image classification]
  Tolerate imprecise variables  Shorter variables
   Less data movement
Model
Cat✓
Dog ×
Notes: But we have approximate application which tolerate imprecise inputs. So, if we can tolerate imprecise inputs, lets eliminate some bits and make the variables shorter which results to having less data and

## Slide 13: Approach2: Truncating LSBs
Omitting Least Significant Bits (OLSB) [Jain et al., MICRO 2016]
  Complies with the exponent-mantissa format of the floating point standard
Sign
Exponent (8 bits)
Mantissa ( 23 bits)
Mantissa (14 bits)
Sign
Exponent (8 bits)
Eliminated bits
The shorter variable
Notes: So, prior works propose to eliminate least significant bits from mantissa to shorten the variables and they still follow the mantissa and exponent format format from the floating point format

## Slide 14: Problem 1: High cost with exponent
3 bits
1 bit
8 bits
Keeps the exponent intact to reduce error
High overhead
12 bits variables
4 bits
1 bit
7 bits
High error
X
Notes: But this approach has two problems. The first problem is that it has to keep the exponent almost intact because eliminating even one bits resultsa high error
And by having 8 bit for exponent, for short variable such as 12 bits variables, the overhead of 8 bits will be more 60 %

## Slide 15: Problem 2: Exponent’s impact on error
Mantissa (14 bits)
Sign
Exponent (8 bits)
Error=(M-M’)× 10+34
Error
Mantissa (14 bits)
Exponent =+127
Exponent =-126
Error= =(M-M’) × 10-43
  Error grows with the magnitude of value
HIGH
HIGH
LOW
LOW
Notes: The second problem is that because error depends on the exponent part, if exponent is large error is high and if expnent is small error is low, so , our error will be highly unpredictable

## Slide 16: Traditional reason for the exponent-mantissa format
0
3.4 × 1038
1.2 × 10-38
Maximum
Minimum positive
Minimum
-3.4 × 1038
Advantage: supporting a wide range of values
Notes: We know that The traditiona reason for having exponent is to support a wide range of value from + and – 3.4 by 10 raised to 38 and having minimum positive of 1.2 by 10 raised by -38

## Slide 17: Approach3: Quantization
Converting floating point numbers
to short integers
Shorter bit-width and limited error
1.25
2.75
Range of Values
2.0
-3
-2
-1
0
+1
+2
+3
∆=0.25
111
110
101
000
+001
+010
+011
Error=∆=fixed
Error=∆=fixed
Error=∆=fixed
Error=∆=fixed
Error=∆=fixed
Error=∆=fixed
Notes: So, we start to think about other approximation methods like Quantization. So what is quantization? Quantization can convert floating point numbers to integers. Assuming a limited range, quantization divides the ranges into few steps and and as assign an integer index to steps and a result represent values with few bits.

## Slide 18: Problem : Overflows
Maximum
Minimum
Values outside the supported range cause overflows
Notes: We know that The traditiona reason for having exponent is to support a wide range of value from + and – 3.4 by 10 raised to 38 and having minimum positive of 1.2 by 10 raised by -38

## Slide 19
Quantization is getting
very popular
Notes: The question here is that whether keeping the exponent and mantissa format is necessary or not

## Slide 20: Where to use quantization?
Applications that can tolerate overflows
Accelerators:
  Can exploit non-standard bit-width (e.g. 4-bit, 12-bit, 18-bit)

## Slide 21
How about overflow-free quantization in general-purpose processors?
Notes: The question here is that whether keeping the exponent and mantissa format is necessary or not

## Slide 22: Quantization for general-purpose processors
Software-based Implementation
  Can not exploit non-standard bit-width
    (e.g. 4-bit, 12-bit, 17-bit)
  Significant Programmer’s effort
  Significant performance overhead
    For conversions
  Prone to bugs and overflows

## Slide 23: Key observation
Significant portion of values lie within a narrow range
There are only few outliers outside the range
Notes: So, we observed that real applications operates on a limited range and conclude that the maybe this Mantissa and exponent format is not necessary

## Slide 24: Key observations
Deep learning
Financial apps
Signal processing
Financial apps
Chart: Net change
| -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3
Frequency | 2 | 3 | 7 | 12 | 33 | 132 | 812 | 809 | 121 | 37 | 13 | 9 | 7
Chart: Open price
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260 | 280 | 300 | 320 | 340 | 360 | 380 | 400
Frequency | 0 | 791 | 512 | 298 | 200 | 98 | 68 | 37 | 24 | 19 | 9 | 8 | 7 | 4 | 1 | 2 | 1 | 1 | 0 | 0 | 1
Chart: Sound amplitude
| -14 | -13.5 | -13 | -12.5 | -12 | -11.5 | -11 | -10.5 | -10 | -9.5 | -9 | -8.5 | -8 | -7.5 | -7 | -6.5 | -6 | -5.5 | -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | More
Frequency | 3 | 1 | 2 | 2 | 5 | 4 | 28 | 142 | 403 | 1026 | 1696 | 2370 | 3025 | 3495 | 3987 | 4490 | 5331 | 6356 | 8886 | 13823 | 21266 | 33614 | 54587 | 90063 | 119935 | 186551 | 339736 | 568978 | 690798 | 584462 | 274286 | 85305 | 32970 | 12609 | 4943 | 2001 | 964 | 443 | 270 | 144 | 74 | 25 | 9 | 5 | 15 | 16 | 8 | 4 | 3 | 1 | 2 | 1 | 3 | 1 | 2 | 1 | 3 | 0
Chart: Activation values
| -1.25 | -1 | -0.75 | -0.5 | -0.25 | 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25
Frequency | 0 | 0 | 20 | 347 | 5395 | 104783 | 73419 | 8654 | 2141 | 327 | 17
Significant portion of values
lie within a narrow range
There are only few outliers outside the range
Notes: So, we observed that real applications operates on a limited range and conclude that the maybe this Mantissa and exponent format is not necessary

## Slide 25
Quantization + overflow handling
can benefit a wide range of applications
Quantization + overflow handling
can be employed in
general-purpose processors

## Slide 26
Goals:
1. Support for overflow-free quantization in general-purpose processors
2. Hardware-accelerated conversions
3. Minimal programmer’s effort
4. Flexible bit-width

## Slide 27: Key mechanisms
Converting an array of values to a quantized bitstream
Representing values within the range with few bits
  Fixed bit-width, e.g., 4 bits
Assigning an outlier indicator with same bit-width
  E.g., “1111”
Replacing outliers with the indicator in the quantized bitstream
Storing the real value of outliers in a different dedicated space

## Slide 28: How to avoid overflows?
L1
Processor
Converter
A quantized block
Multiple
de-quantized
blocks
@quant <3, 0.25, 1.5>
float price [1000];
Memory
  1. Computation: Convert to float before computation
  2. Conversion: Retrieve outliers from the dedicated space
L2
Notes: So, The goal of this work is to provide a hardware support for quantization in general purpose processors. We want to minimize programmer’s effort, so tha tprogrammers only need to annotate the array that contains approximate values and corresponding quantization parametes. Then our converter module quantize and dequantized cache blocks when blocks move between a upper level cache and a lower level cache

## Slide 29: Quantization looks like cache compression
L1
Processor
Converter
A quantized block
Multiple
de-quantized
blocks
@quant <3, 0.25, 1.5>
float price [1000];
Memory
  How to avoid cache compression problems?
L2
Notes: So, The goal of this work is to provide a hardware support for quantization in general purpose processors. We want to minimize programmer’s effort, so tha tprogrammers only need to annotate the array that contains approximate values and corresponding quantization parametes. Then our converter module quantize and dequantized cache blocks when blocks move between a upper level cache and a lower level cache

## Slide 30: A high-level abstraction can help
  MMU transfers quantization parameters,
  array’s boundaries, and layout to hardware

## Slide 31: How do quantization parameters help?
A low-overhead compressor/decompressor
  Quantizer/dequantize
  Simple arithmetic-based conversions
    Instead of Obliviously looking for value locality
@quant <3, 0.25, 1.5>
float price [1000];

## Slide 32: How do array’s boundaries help?
Keep the metadata for the whole array
  Vs. keeping metadata per block (per page)

## Slide 33: How does layout help?
Higher compression ratio for arrays of structure
Struct element{
float Price;
bool type;
float yield}
True
87.89
XXXXXXX
0.2
price
type
Unused
yield
9
bits
1
bits
4
bit

## Slide 34: Address translation using precomputed (offline-computed) values
Precomputed values for low-overhead address translation
  Reciprocate of the number of quantized words that fit in a block
  Accumulated quantized bit-width of variables in a structure
B3
B2
B1

## Slide 35
Evaluation
Notes: The question here is that whether keeping the exponent and mantissa format is necessary or not

## Slide 36: Quantization vs LSB truncation
Quantization provides 3.5 times lower relative error
Chart: 
OLSB | 0.19858
Quantization | 0.055538
3.5

## Slide 37: Quantization vs LSB truncation
Quantization provides 16 times lower absolute error
Chart: 
OLSB | 9671.3441
Quantization | 604.8391
16

## Slide 38: Quantization vs LSB truncation
For a specified error,
quantization requires fewer bits

## Slide 39: Quantization vs OLSB
  Up to 31% performance improvement over OLSB

## Slide 40: Quantization vs OLSB
  Up to 31% performance improvement over OLSB

## Slide 41: Performance Evaluation
Chart: 
4 Cores | 4.5233
8 Cores | 5.7834
16 Cores | 7.4467
Performance improvement increases as the number of cores increases

## Slide 42: Performance Evaluation
Chart: 
4 Cores | 6.8786
8 Cores | 7.8243
16 Cores | 9.541
Performance improvement increases as the number of cores increases

## Slide 43: Quantization vs cache compression
  Latency of access to the decoupled tag and data array nullifies the higher compression rate by Qnt+Comp

## Slide 44: Conclusion
Most values lie within a narrow range
  No need to have exponent and mantissa format except for outliers
General-purpose processors can exploit quantization
Quantization can be a low-overhead compression technique
  Simpler compressor/decompressor
  Less metadata
  Low-overhead address translation
  Higher compression ratio
    For floating point variables and arrays of structures