## Slide 1: Fermi
A Complete GPU Compute Architecture by NVIDIA
Tamal Saha, Abhishek Rawat, Minh Le
{ts4rq, ar8eb, ml4nw}@virginia.edu

## Slide 2: GPU Computing
Unprecedented FP performance
Ideal for data parallel applications
Programmability
Nov 2006: G80
Jun 2008: GT200
Sep 2009: Fermi
1999:
GPU

## Slide 3: Overview
3G Streaming Multiprocessor
3 bn transistors
512 CUDA cores
384(6 * 64)-bit memory interface

## Slide 4: Top Innovations in Fermi
Improve Double Precision Performance – 256 FMA ops/clock
ECC support – 1st time in a GPU
True Cache Hierarchy – L1 cache, shared memory and global memory
More Shared Memory – 3x more than GT200; configurable
Faster Context Switching – under 25 µs
Faster Atomic Operations – 20x faster than GT200

## Slide 5: High Performance CUDA Cores
512 CUDA cores
  32 Cores/SM
  16 SM
4x more core/SM than GT200

## Slide 6: Dual Warp Scheduler
Each SM has
  2 warp scheduler
  2 instruction dispatch unit
Dual – issue in each SM
Most instructions can be dual issued
  Exception: Double Precision
Warp Scheduler | Warp Scheduler
Inst Dispatch Unit | Inst Dispatch Unit
… | …
Warp 8 inst 11 | Warp 9 inst 11
Warp 2 inst 42 | Warp 3 inst 33
Warp 14 inst 95 | Warp 15 inst 95
: | :
Warp 8 inst 12 | Warp 9 inst 12
Warp 14 inst 96 | Warp 3 inst 34
Warp 2 inst 43 | Warp 15 inst 96
time

## Slide 7: Load/Store Units
16 load/store units/SM
Source and destination address calculated by load/store unit

## Slide 8: Improved Arithmetic Capability
Full IEEE 754-2008 support
16 double precision FMA ops/SM
8x the peak double precisi0on floating point performance over GT200
4 Special Functional Units(SFU)s/SM for transcendental instructions, such as, sin, cosine, reciprocal and square root.

## Slide 9: Parallel Thread eXecution ISA
Fermi is the first architecture to support PTX 2.0.
  PTX 2.0 greatly improves GPU programmability, accuracy, and performance.
Primary goals of PTX 2.0
  stable ISA that can span multiple GPU generations.
  provide a machine-independent ISA for C, C++, Fortran, and other compiler targets.
  provide a common ISA for optimizing code generators and translators which map PTX to specific target machines.

## Slide 10: ISA Improvements
Full IEEE 754-2008 32-bit and 64-bit precision.
  support for Fused Multiply-Add for all FP precision (prior generations used MAD for single precision FP).
  support for subnormal numbers, and all four rounding modes (nearest, zero, positive infinity and negative infinity).
Unified Address Space
  1 TB continuous address space for local (thread private), shared (block shared) and global address spaces.
  unified pointers can be used to pass objects in any memory space.

## Slide 11: ISA Improvements (cont..)
Full support for object oriented C++ code, not just procedural C code.
Full 32-bit integer path with 64-bit extensions.
  Load/store ISA supports 64-bit addressing for future growth.
Improved Conditional Performance through Predication.

## Slide 12: ISA Improvements (cont..)
Optimized for OpenCL and DirectCompute.
  Shares key abstractions like threads, blocks, grids, barrier synchronization, per-block shared memory, global memory, and atomic operations.
  new append, bit-reverse and surface instructions.
Improved efficiency of “atomic” integer instructions. (5x-20x times prior generations)
  atomic instructions handled by special integer units attached to L2 cache controller.

## Slide 13: Parallel Datacache
64 KB on-chip configurable memory/SM
  16 KB L1 cache + 48 KB Shared memory
  48 KB L1 cache + 16 KB Shared memory
3x more Shared memory than GT200.
Unified L2

## Slide 14: Configurable Shared Memory & L1 Cache
64 KB on-chip memory/SM
  16 KB L1 cache + 48 KB Shared memory
  OR
  48 KB L1 cache + 16 KB Shared memory
3x more Shared memory than GT200.
  Significant performance gain for existing apps using Shared memory only
  Apps using software managed cache can be stream lined to use hardware managed cache

## Slide 15: Error Correcting Code
Single error correction – Double error detection
  DRAM
  Chip’s register files
  Shared memories
  L1 and L2 cache

## Slide 16: GigaThread Thread Scheduler
Two-level thread scheduler.
  Chip level: thread blocks => SMs
  SM level: Warps (32 threads) => execution unit
24,576 simultaneously active threads
10x faster app context switching ( < 25 μs )
Concurrent Kernel Execution
Serial Kernel Execution
Concurrent Kernel Execution
time
time

## Slide 17: So, what’s next?
The Relatively Small Size of GPU Memory
Inability to do I/O directly to GPU Memory
Managing application level parallelism

## Slide 18
Q?

## Slide 19: References
http://www.nvidia.com/object/fermi_architecture.html
Fermi Compute Architecture White Paper - http://www.nvidia.com/content/PDF/fermi_white_papers/NVIDIA_Fermi_Compute_Architecture_Whitepaper.pdf
The Top 10 Innovations in the New NVIDIA Fermi Architecture, and the Top 3 Next Challenges by Dave Patterson, Co-author of Computer Architecture: A Quantitative Approach

## Slide 20
Thank You