## Slide 1
RISC / CISC Architectures’ Performance comparison assuming similar H/W Organization
Qiuhua Cao William Greenwell
Chengdu Huang Kumar Manvendra

## Slide 2: Outline
Differences between RISC / CISC
Quantitative performance analysis
    Number of Instructions
    Cache Behaviour
    Case study of one(two ??) benchmarks(fp behaviour)
Factors favoring RISC , CISC
Critique / Conclusion

## Slide 3: What the paper suggest?
RISC has many performance advantages over CISC
  Single cycle L/S instruction (faster,low overhead)
  Hardwired control ; vastly reduced chip complexity
  more registers/less MEM references
  Fixed INST format,fewer instructions
  MEM accesses are not tightly bound to INSTS

## Slide 4: Experimental Framework
Paper looks at MIPS M/2000(from RISC) and VAX 8700(from CISC)
Most recent compilers were used for each of the two machines
Cycle time determined through machine independent features but its same
Spec 1 Release benchmarks used
-same underlying organization

## Slide 5
CPU Pipeline Abstractions MIPS and VAX
MIPS instruction fetch stage matches with VAX micro- instruction fetch stage
    Large set of general purpose registers
    Single cycle instructions
    Delayed branches

## Slide 6: About MIPS and VAX
Strong organizational similarities
  Ex: CPU Pipeline abstractions match up closely
VAX Microinstruction stage features a lot of RISC features
MIPS has split I-Cache and D-Cache unlike VAX which has same I+D Cache
MIPS has larger page size
Same Cycle time -- A COINCIDENCE ??
MIPS has much faster MEM access ,FP ops

## Slide 7: Spec Benchmarks used
We have used 3 integer (in C) benchmarks
    Espresso
    Eqntott
    Li
And 7 floating point (in fortran )benchmarks
    Spice2g6
    Matrix300
    Nasa7
    Fpppp
    Tomcatv
    doduc
Compiled using VAX Cv3.1 , CCv2.0
Compiled using VAX Fortran V5.0-1 ,
MIPS f77 v2.0

## Slide 8
Tools used to generate benchmarks
VAX 8700
    Hardware monitor
        Every microinstruction count is kept
        Data / instruction accesses can be studied
MIPS M/2000
    Pixie/pixstats
        Division into basic blocks and counting instruction in each basic blocks

## Slide 9
Instructions and CPI

## Slide 10
Instructions and CPI
MIPS < VAX

## Slide 11
Instructions and CPI
MIPS exe/ VAX exe
G mean = 2.17

## Slide 12
Instructions and CPI
VAX CPI/ MIPS CPI
G mean = 5.77

## Slide 13
Instructions and CPI
Net Effect on Performance
cycles per program ratio

## Slide 14
Instructions and CPI
SPICE is the best

## Slide 15
Instructions and CPI
Three integer compilers
have biggest RISC
Lowest inst ratio

## Slide 16
Instructions and CPI
Three lowest RISC
three lowest CPI ratio

## Slide 17
Operation Counts

## Slide 18
Operation Counts
MIPS per inst < VAX per inst
MIPS also equals VAS count

## Slide 19
Operation Counts
MIPS < VAX

## Slide 20
Operation Counts
MIPS mem< VAX mem
exception

## Slide 21
Cache behavior

## Slide 22
Cache behavior
D highest miss ratio
Lowest RISC factor

## Slide 23
Cache behavior
some MIPS > some VAX

## Slide 24
MIPS = 2.66 × VAX

## Slide 25: Case Study
fpppp benchmark
  Highest CPI Ratio, Highest INST Ratio, High RISC factor
  High number of FP L/S ops on MIPS; High density of double precision operand specifiers on VAX
  MIPS has fast FP operations
  VAX has no instruction overlapping

## Slide 26: Architecture Factors Favoring MIPS
Operand specifier decoding
  e.g. Three-register integer add
    VAX: 4 cycles ; MIPS: 1 cycle
Number of Registers
  VAX: 15 32-bit general regs
  MIPS: 32 32-bit general regs and 16 64-bit FP regs

## Slide 27: Architecture Factors Favoring MIPS
FP Hardware/Instruction Overlap
  Data movement between chips
  MIPS has register destination FP ops only
Simple Jump/branches
  VAX Condition codes

## Slide 28: Architecture Factors Favoring MIPS
Fancy VAX Instructions
  Unnecessary functionality and unnecessary overhead
  e.g. VAX procedure call and return inst
Instruction Scheduling
  MIPS can fill delay slots

## Slide 29: Architecture Factors Favoring MIPS
Translation Buffer
  MIPS has a larger page size
Branch Displacement Size
  VAX: 8 bits
  MIPS: 16 bits

## Slide 30: Architecture Factors Favoring VAX
Big I-stream Constants
Not-taken Branches

## Slide 31: Variance of the RISC Factor
Loose correlation with D-cache misses
Highest RISC factor: li
  Lowest D-cache miss ratio
  Lots of function call overhead for VAX
  Address unaligned mem refs for VAX
Lowest RISC factor: spice

## Slide 32: Future of CISC & RISC
VAX may be able to catch up to current RISC architectures.
  Figure 4 from paper
RISC will incorporate advanced implementation techniques.
VAX will always play “catch up.”

## Slide 33: Summary Table
3.7
2.7
1.8
RISC-F
3.9
2.2
1.1
Inst. Ratio
10.4
5.8
3.5
CPI Ratio
3.1
1.7
1.1
MIPS CPI
17.4
9.9
5.4
VAX CPI
Max
Geometric Mean
Min
Source: Bhandarkar & Clark. “Performance from Architecture: Comparing a RISC and a CISC with Similar Hardware Organization”

## Slide 34: Caveats
Compiler influence may skew results.
Small sample size with respect to benchmark programs
Application-level vs. system-level comparison
  Effect of operating system primitives