## Slide 1: McPAT: An Integrated Power, Area, and Timing Modeling Framework for Multicore and Manycore Architectures
Runjie Zhang
Dec.3
S. Li et al. in MICRO’09

## Slide 2: Motivation
“Tools both limit and drive research directions”
New demands
  Multicore/manycore
  Evaluate power, timing and area
  Different source of power dissipation
  Deep-submicron

## Slide 3: Related Work
Wattch:
  Enabling a tremendous surge in power-related research
Orion:
  Combined Wattch’s core power model with a router power model
CACTI:
  First tool in rapid power, area, and timing estimation
Notes: Wattch: widely-used processor power estimation tool. Calculates dynamic power dissipation from switching events obtained from an architectural simulation. It uses some models from CACTI
Orion is a tool for modeling power in NoC

## Slide 4: What’s wrong with previous work?
Wattch
  No timing and area models
  Only models dynamic power consumption
  Use simple linear scaling model
Orion2
  No short circuit power or timing
  “Incomplete”
CACTI
  ???

## Slide 5: Contributions
First integrated power, area, and timing modeling framework
Model all three types of power dissipation
Complete, integrated solution for multithreaded and multicore processor power
Deep-submicron tech. that no longer linear

## Slide 6: Overview

## Slide 7: Integrated Approach
Power | Dynamic: Similar to Wattch Short Circuit: IEEE TCAD’00 Leakage: MASTAR & Intel
Timing | CACTI with extension
Area | CACTI Empirical modeling for complex logic

## Slide 8: Hierarchical Approach

## Slide 9: Architecture Level
Core | Divided into several main units: e.g. IFU, EXU, LSU, OOO issue/dispatch unit
NoC | Signal links and routers
On-Chip Caches | Coherent cache
Memory Controller | 3 main hardware structure Empirical model for physical interface (PHY)
Clocking | PLL and clock distribution network Empirical model for PLL power

## Slide 10: Circuit Level
Wires | Short wires as one-section Pi-RC model Long wires as a buffered wire model
Arrays | Based on CACTI with extensions
Logic | Highly regular: CACTI Less regular: Model from Intel, AMD and Sun Highly customized: Empirical, from Intel and Sun
Clock Distribution Network | Separate circuit model Global, Domain, and Local

## Slide 11: Validation
Notes: 4 processors, include in-order and OOO, single-threaded and multithreaded processor
Peak power

## Slide 12: Validation
 | Average error | 1st Contributor Error / % in total pwr
Niagara | 1.47W / 23% | 74% / 1%
Niagara2 | 1.87W / 26% | 47% / 5%
Alpha 21364 | 3.4W / 26% | 45% / 3%
Xeon Tulsa | 4.2W / 17% | 29% / 3%
Notes: What is the definition of biggest contributor?
The biggest contributor in Niagara2 is not I/O power

## Slide 13: Scaling & Clustering
New generation:
Double # of cores
Keep the same micro-architecture

## Slide 14: Parameters and Benchmarks

## Slide 15: Area and Power

## Slide 16: Performance and Efficiency

## Slide 17: Performance and Efficiency

## Slide 18: In-order vs. OOO with M5