## Slide 1: Wireless for the Internet of Things BLE Connections
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Nasir]

## Slide 2: Today’s Goals
Explore how connections work
  What does the link layer look like?
  How do higher layers interact to share data?
Investigate network questions about connections
Overview of additions in BLE 5.0

## Slide 3: Recall: BLE advertisements lead to connections
Central
Advertisement:
“I’m the Living Room Light”
Peripheral
Connection Request
Connected (stops advertising)
“Set light brightness to 50%”
(note: this is highly simplified)
We’ll explore what happens here!
Notes: Advertiser
Scanner
Central
Peripheral
https://community.nxp.com/t5/Wireless-Connectivity/A-view-on-Bluetooth-Low-Energy-stack-roles/m-p/380310

## Slide 4: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 5: BLE Connections: A 10,000ft view
Higher throughput than advertisements
Supports bi-directional communication
Half-duplex (“one person talks at a time”)
During a connection both devices act like servers
  Can read/write fields available on other device
Roles – simple view
  Peripheral: can be advertising/in connection
  Central: scanning / in 1 or more connections
  Not quite accurate: devices can have many roles simultaneously
Central
Peripheral
Phone: Hey, please set brightness
to 75%.
Light: Sure thing!
Phone: What’s the current color?
Light: It’s blue.
Advertisement:
“I’m the Living Room Light”
(write)
(read)
Notes: Simple view
  A peripheral is either advertising or in a connection
  A central is scanning and in one or more connections
  (Remember: actually false, devices can have many roles simultaneously)

## Slide 6: Once connected, BLE has PHY options with more throughput
LE 1M (default)
  Symbol rate: 1 Msym/s (Mega symbols / second)
  BLE encodes 1 bit / symbol, so this is also 1 Mbit/s
LE 2M
  2 Msym/s
LE Coded
  1 Msym/s + Forward Error Correction (FEC)
    S = 2 (2 symbols correspond to 1 bit)
      ½ effective data rate – 500 Kbit/s goodput (~2x range)
    S = 8 (8 symbols correspond to 1 bit)
      125 Kbits/s goodput (~4x range)
FSK Example
0
0
1
1
1
Each of these are symbols
Notes: The mandatory symbol rate is 1 megasymbol per second (Msym/s), where 1 symbol represents 1 bit therefore supporting a bit rate of 1 megabit per second (Mb/s), which is referred to as the
LE 1M PHY. The 1 Msym/s symbol rate may optionally support error correction
coding, which is referred to as the LE Coded PHY. This may use either of two
coding schemes: S=2, where 2 symbols represent 1 bit therefore supporting a
bit rate of 500 kb/s, and S=8, where 8 symbols represent 1 bit therefore
supporting a bit rate of 125 kb/s. An optional symbol rate of 2 Msym/s may be
supported, with a bit rate of 2 Mb/s, which is referred to as the LE 2M PHY. The
2 Msym/s symbol rate supports uncoded data only. LE 1M and LE 2M are
collectively referred to as the LE Uncoded PHYs. Section 3.2.2 describes this
terminology in more detail
Binary frequency shift keying encodes digital data by selecting a central frequency known as the carrier and then shifting it up by a given frequency deviation to represent a 1 or
down by the same frequency deviation to represent a 0. The minimum size of the
frequency deviation that is permitted is specified in the Bluetooth® Core Specification and depends on the selected symbol rate, which is either 1 or 2 mega-symbols per second (Msym/s) in Bluetooth LE. For the 1 Msym/s symbol rate, a minimum frequency deviation of 185 kHz is specified, whereas for the faster symbol rate, the minimum frequency deviation is 370 kHz. These values were chosen carefully, to help make the recognition of encoded 1s and 0s in a signal reliable.

## Slide 7: BLE uses 2.4 GHz ISM Band with Data and Advertisement Channels
Recall: Each BLE channel is 2 MHz wide, 40 channels (0-39)
  3 channels for advertising (37, 38, 39)
  37 channels for connections (0 - 36)
Notes: Source: https://i0.wp.com/embeddedcentric.com/wp-content/uploads/2019/03/bluetooth_ble_spectrum.png?ssl=1

## Slide 8: Connection Timeline
Peripheral advertises
Central sends a connection
request packet on advertising
channel just after receiving
advt
Peripheral stops advertising
Central and peripheral switch
to a data channel
Notes: - Animate
- Change text to annotations

## Slide 9: Choosing a data channel for communication
Why do you switch from advertising channel to data channel?
How to pick a channel out of the 37 data channels?
What if two pairs pick same channel?

## Slide 10: Choosing a data channel for communication
Why do you switch from advertising channel to data channel?
  For better reliability and to improve quality of service
How to pick a channel out of the 37 data channels?
  Randomize for reduced chance of collision
What if two pairs pick same channel?
  Higher chance of collision occurring
  Some way to not be tied to the same data channel is needed

## Slide 11: Connected devices hop through channels to improve reliability
BLE is a Frequency Hopping Spread Spectrum (FHSS) technology
Central and peripheral “hop” among data channels in a pre-agreed fashion
  Why? To avoid bad channels and reduce collisions
Next hop channel cn+1 = (cn + hop) mod 37
Exact channels used in hopping and in
what order might vary

## Slide 12: How does the Central and Peripheral agree on things?
For a packet to be received:
  Central and peripheral should be listening and sending on same data channel
For the hopping to be successful, both must:
  Follow same hop sequence
    Which channels to use and the order to follow
  Hop at a given time schedule
  Agree on when to schedule their first communication
Some synchronization is needed!

## Slide 13: Send synchronization information in the Connection Request packet
Notes: Note: CONNECT_IND is used in BLE 5.0, replaces CONNECT_REQ in BLE 4.x
https://www.silabs.com/documents/public/presentations/ew-2019-bluetooth-low-energy-beacon-next-generation.pdf

## Slide 14: Connection request parameters examined
Specifies parameters of the connection
  Peripheral must either agree or totally reject the connection
  Peripheral can later propose a change to the connection parameters
Interval is how frequently connection events occur (7.5ms – 4s)
Notes: Figure from video would be good

## Slide 15: Steady-state connection timing
Some data can be exchanged at each interval
  Might just be acknowledgements
  Additional packets can be sent if there is a lot to transmit
  Each interval is on the next channel in the hopping sequence
Peripheral can skip a number of intervals to save energy
  Defined by the Latency connection request parameter
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Connection Interval
Hop to next data channel
Optional packets

## Slide 16: BLE connection “events” happen at periodic intervals
Hop to next data channel
(Central)
(Peripheral)
Notes: Source: https://embeddedcentric.com/introduction-to-bluetooth-low-energy-bluetooth-5/
During a connection
  Central sends a packet each “connection interval”
  Peripheral immediately responds with a packet
  Multiple packets may be exchanged this way until done
  Repeat at next connection interval
Ending a connection
  Either device sends termination packet
  Timeout occurs on either device

## Slide 17: How do you schedule the very first connection event?
WinSize and WinOffset specify start of the first connection event
  First connection event: first exchange after CONNECT_REQ packet)
WinOffset: Time from now until first event
  Analogy: “Hey let’s meet 2 hours from now”
WinSize: Flexible window of time to expect first transmission
  Analogy: “I might be upto 15mins late”
Notes: Figure from video would be good

## Slide 18: WinSize, WinOffset, and Interval define TDMA schedule
Place an “anchor” point that defines the TDMA schedule for this device
Interval specifies duration between connection events starting at “anchor”
Central to Peripheral
Peripheral to Central
Central to Peripheral

## Slide 19: How do you agree on hopping pattern?
Channel Map (ChM) and Hop define the FHSS pattern
Channel Map (ChM): Map of which channels to use
Hop: next hop increment
  Next hop channel cn+1 = (cn + hop) mod 37
Notes: Figure from video would be good

## Slide 20: Connection messages are sequenced for additional reliability
LLID – link layer ID
Empty data / Fragment
Data
Control
MD – more data (continues connection event)
[Next Expected] Sequence Number – acknowledgements

## Slide 21: LL uses acknowledgments to handle packet loss and corruptions
Case 1: Successful exchange of packets
SN: Sequence Number
  Only two SN used: 0, 1
NESN: Next Expected Sequence Number
  Equivalent to Acknowledgement
Case 2: Re-transmission of missing packet
Case 3: Handling CRC failures
Notes: Source: https://www.bluetooth.com/bluetooth-resources/understanding-reliability-in-bluetooth-technology/

## Slide 22: Next steps in a connection
Control packets
  Version
    Bluetooth version, Company ID of Software Stack
  Features
    Various connection features supported by the device
    Encryption, Ping, Channel selection algorithms, Various 5.0 features
  Etc.
    Extended packet length, Various 5.0 features (change PHY)
    Various “procedures” for setting up changes in the connection
Data packets
  Attribute discovery
  Attribute reading

## Slide 23: Control payloads
Examples:
Request update to connection parameters like interval (by peripheral)
Begin encrypting communication
Terminate a connection

## Slide 24: Data payloads
Length (16 bits) | Channel ID (16 bits) | L2CAP SDU Length* (16 bits) | Information Payload (0 to 249 octets)
SDU – Service Data Unit
Logical packet that may be split into several physical packets
Channel ID
Destination for data
ATTributes or Security
Can also make custom endpoints

## Slide 25: Ending connections
Termination control packet
Timeout is how long since hearing from a device before the connection breaks
  Human-based devices may just wander away from each other
  Or be shut off, or reprogrammed, etc.

## Slide 26: Very briefly: security in connections
Excellent TI resource here for more details: https://dev.ti.com/tirex/explore/node?node=AOPOY.GDApakIOYjiwoY6A__pTTHBmu__LATEST
Either side can request secure connection [central -> Pairing; peripheral -> Security Req]
“Bonding” saves pairing info between connections

## Slide 27: Very briefly: security in addresses
All devices have a unique, hardware “Identity Address”, but may not share it
  Public Address - Use the Identity Address. (The BDA never changes.)
  Random Static Address - Generate a random address per power cycle. The address cannot be regenerated at any other time. Can be used as an Identity Address.
  Resolvable Private Address (RPA) - Generate a random address with a given time interval. Generated using Identity Resolving Key (IRK) which can also be used by trusted peers (bonded devices) to resolve the Random Address to the Identity Address.
  Non-resolvable Private Address - Generate a random address with a given time interval. Generated randomly. Cannot be resolved to an Identity Address.

## Slide 28: Check your understanding
What makes connections more reliable than advertisements?
How does a Peripheral send data to a Central in a connection?
Why is a “termination” control packet useful?

## Slide 29: Check your understanding
What makes connections more reliable than advertisements?
  TDMA schedule and FHSS means less likely to collide
  Each packet sent is acknowledged or resent
How does a Peripheral send data to a Central in a connection?
  Wait until next connection interval
  Respond to packet from Central with a data payload
Why is a “termination” control packet useful?
  Timeout could delay for a while
  Enables re-connection if desired

## Slide 30: Break
xkcd.com/612/

## Slide 31: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 32: Questions about how a connection “network” works
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
How much throughput can a device have?

## Slide 33: How is the TDMA schedule created/managed?
Only the central needs to know the schedule
  It controls interactions with the peripheral(s) it is connected to
Anchor point and connection interval determines the schedule for a specific device
Central to Peripheral
Central to Peripheral
Peripheral to Central

## Slide 34: How is synchronization managed?
Central sends first packet at each connection interval
  So peripheral must be synchronized to central
  Resynchronization can occur on each received packet
Specification describes how a peripheral must widen its listening window based on “Source Clock Accuracy”

## Slide 35: Clock drift is an energy burden due to large guard bands and energy cost of precise timekeeping
Wall time
Device time
CC2520 Radio + AM18xx RTC:
300s * 2ppm * 2 = 1.2 ms guard
1.2 ms * 60 mW = 36 μJ (RF loss)
300s * 150nW = 45 μJ (RTC loss)
≈ 100 μJ loss / packet @ 300 s
300 s
Guard
1200 μs
@ 2ppm
Static Power:
100 nW+
(CC2520 is a 15.4 radio, but same idea applies) Max connection interval in BLE is 4 seconds

## Slide 36: How many devices can be connected?
We can schedule with granularity of at least 1.25 ms (offset steps)
  That’s at least 800 devices per second
Intervals go up to 4 seconds, so multiply by four
  That’s 3200 devices per max interval
Plus central can skip intervals on occasion without dropping the connection
  And really the offset defines a window. More granularity is available
Answer: thousands of devices
  Although each is sending minimum-sized packets each interval

## Slide 37: How many devices can be connected in the real world?
The limit is much much lower on real devices
  Example: Android sets a limit at around 4-15
  nRF52 s140 softdevice allows up to 20
Connection management is often done in firmware
  Softdevice for nRF, firmware on the radio chip in smartphones
Limited by memory and complexity

## Slide 38: How much throughput can a device have?
1 Mbps?

## Slide 39: How much throughput can a device have?
1 Mbps? Not even close. Packet overhead plus timing delays
Step 1: decrease connection interval as much as possible
  More connection events per second mean more data
  Range: 7.5 ms to 4.0 s
  Somewhat device-specific configuration
    Android allows 7.5 ms
    iOS allows 15 ms

## Slide 40: How much throughput can a device have?
Step 2, increase packet size
Use Data Length Extension (DLE) supported by BLE v4.2+
Notes: https://punchthrough.com/maximizing-ble-throughput-part-3-data-length-extension-dle-2/
Connection event length = time duration where tx happens (different from connection interval)

## Slide 41: How much throughput can a device have?
488 bytes per connection event
  Maximum sized packets, discounting headers and timing delays
  7 bytes of overhead / headers in the 251 bytes
Result: 520 kbps (65 kB per second)
  iOS result 260 kbps
  Original BLE 4.1 result on Android: 128 kbps
  Lower in practice due to lost packets

## Slide 42: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 43: How is data actually exchanged between central and peripheral?
Attribute Protocol (ATT) and Generic Attribute Profile (GATT) used for this!
ATT is the underlying framework for GATT
  Two roles: Client and Server
Data that the server exposes is structured as attributes
ATT Client
ATT Server
Attribute Protocol
Central
Peripheral

## Slide 44: Attribute Server Keywords
Characteristic
  A field with properties and a value
  Descriptor: metadata about the characteristic
  eg: Light Brightness
Service
  Collection of characteristics
Profile
  Collection of services
Each attribute has a type, permissions, and a value
Operations on attributes: Read, Write, Notify, Indicate

## Slide 45: Overview of Generic Attribute Profile (GATT)
Attribute Type is specified as a UUID
Notes: https://novelbits.io/bluetooth-gatt-services-characteristics/
A Notification is an unacknowledged message or update while an Indication is an acknowledged message or update. These Notifications and Indications are sent any time the relevant data in the GATT table on the GATT Server is updated. (You must "subscribe" to the data that you would like to be Notified or Indicated of) In a way Indications and Notifications are much like TCP and UDP packets. TCP requires that when data is sent, the receiver acknowledges that the data has been received by sending back an ACKnowledgement packet. UDP just sends off data without any concern whether it is actually confirmed to be received or not. In this sense Indications are akin to TCP and Notifications are akin to UDP.

## Slide 46: UUIDs and handles
Universally Unique Identifiers
  128-bit, mostly random with a few bits for versioning
  Example: 00000000-0000-1000-8000-00805F9B34FB
    This is the default BLE UUID for known services
    You can generate your own UUID for custom services
Handles
  Too long to pass around all the time, so pick 16 bits that mean that UUID
    Must be unique among services/characteristics on that device
  Taken from UUID: 0000xxxx-0000-1000-8000-00805F9B34FB
  Handle often sequentially incremented for each new characteristic within a service
Resource: Useful post on identifying handles in the wild

## Slide 47: How would our Smart Light expose its data?
ATT Client
ATT Server
Attribute Protocol
Central
Peripheral
Generic Access Profile Service (UUID: 0x1800)
Name (UUID: 0x2a00)
Properties: Read
Value: Living Room Light
Appearance (UUID: 0x2a01)
Properties: Read
Value: 0x4142
Light Service (UUID: 0bd51666-e7cb-469b-8e4d-2742f1ba77cc )
Brightness (UUID: 0xe7add780-b042-4876-aae1-112855353cc1)
Properties: Read, Write
Value: 0.65
service
characteristic
Color (UUID: 0xe7add780-b042-4876-aae1-112855353cc2)
Properties: Read, Write
Value: 00FFFF

## Slide 48: Discovery
When a connection first occurs, each device can query the other for a list of services
  And can further query for a list of characteristics in that service
  Gets a list of handles/UUIDs
Standardized UUIDs can be interpreted immediately
  Custom services/characteristics need documentation from the manufacturer

## Slide 49: How would our smart light advertise its services?
Central
Peripheral
Advertisement:
“I’m the Living Room Light”
Advertisement:
“I’m the Living Room Light. I have a GAP Service (0x1800), and a Light Service (…)”
Notes: Simple view
  A peripheral is either advertising or in a connection
  A central is scanning and in one or more connections
  (Remember: actually false, devices can have many roles simultaneously)

## Slide 50: Now you know how this interaction happens!
Higher throughput than advertisements
Supports bi-directional communication
Half-duplex (“one person talks at a time”)
During a connection both devices act like servers
  Can read/write fields available on other device
Roles – simple view
  Peripheral: can be advertising/in connection
  Central: scanning / in 1 or more connections
  Not quite accurate: devices can have many roles simultaneously
Central
Peripheral
Phone: Hey, please set brightness
to 75%.
Light: Sure thing!
Phone: What’s the current color?
Light: It’s blue.
Advertisement:
“I’m the Living Room Light”
(write)
(read)
Notes: Simple view
  A peripheral is either advertising or in a connection
  A central is scanning and in one or more connections
  (Remember: actually false, devices can have many roles simultaneously)

## Slide 51: Example: Time Profile

## Slide 52: Current time characteristic
The Bluetooth SIG are pedantic people

## Slide 53: Interacting with characteristics
Depends on their permissions
  Readable, Writable, Notify-able, etc.
Notify
  Automatically get a message sent whenever the characteristic value updates
  Note: have to enable this on both sides, it’s not the default behavior
Long characteristics are automatically fragmented across multiple packets and/or connection events
  L2CAP is in charge of this

## Slide 54: Break + Example Services
https://btprodspecificationrefs.blob.core.windows.net/assigned-values/16-bit%20UUID%20Numbers%20Document.pdf

## Slide 55: Documentation of GATT standards
https://www.bluetooth.com/specifications/gatt/
  Various profiles and services that have been standardized
GATT Specification Supplement
  Various characteristic definitions that have been standardized
Both incredibly specific and woefully inexhaustive

## Slide 56: Break
xkcd.com/1892

## Slide 57: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 58: Changes in BLE 5
Major changes
  Multiple physical layers
  Advertising extensions
Minor changes
  Various quality of life improvements
  Examples:
    Advertise on channels in any order
    Better data channel hopping algorithm
Notes: Hopping algorithms:
https://www.mathworks.com/help/bluetooth/ug/bluetooth-le-channel-selection-algorithms.html

## Slide 59: Revised physical layers
2 Mbps PHY
  Transmit data faster
  Transmit more data in the same time
Coded PHY
  Forward Error Correction in the data stream
    1 bit -> 2 symbols or 8 symbols
  Makes bits more reliable -> longer distance
  500 kbps and 125 kbps modes
Connections can switch to these PHYs after creation
Advertisements can use these with extensions only

## Slide 60: Coded PHY mixes physical and link layers
Different PHY settings at different times
  Make beginning headers extra-reliable
  Data might be slightly less reliable as a trade for faster speed
Packet sent with coded PHY

## Slide 61: Revised processing path

## Slide 62: Extended advertising
Regular advertisements point to extended advertisements
  Uses Data Channels to do so. Why?

## Slide 63: Extended advertising
Regular advertisements point to extended advertisements
  Uses Data Channels to do so. Why? Packet Collisions

## Slide 64: Procedure for scanning extended advertisements
Scan on 3 primary channels for advertising packets.
If ADV_EXT_IND is scanned, record the secondary channel information (which channel and when etc.)
Scan the specific secondary channel at the given time.

## Slide 65: Extended advertisement train on data channels
Use case: long advertisements that need to be fragmented

## Slide 66: Periodic advertising on data channels
Use case: publicly-available localized audio sources
TV in a bar
Commentary in a museum
Broadcast analogy of a connection
Downside:
how many of these can a gateway follow at a time?

## Slide 67: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 68: Useful documentation
[5.2 specification] [4.2 specification] (link to PDF download)
https://www.novelbits.io/deep-dive-ble-packets-events/
Thinking about BLE connection data transfer rates
  https://punchthrough.com/maximizing-ble-throughput-on-ios-and-android/
  https://punchthrough.com/maximizing-ble-throughput-part-2-use-larger-att-mtu-2/
  https://punchthrough.com/maximizing-ble-throughput-part-3-data-length-extension-dle-2/