## Slide 1: Wireless for the Internet of Things WiFi (IEEE 802.11)
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
Introduce the ins and outs of WiFi
Think about how WiFi (IEEE 802.11) has managed to keep up over 25 years
https://www.wevolver.com/article/the-evolution-of-wi-fi-networks-from-ieee-80211-to-wi-fi-6e

## Slide 3: Characterizing WiFi
Plot BLE, 802.15.4, and WiFi on each set of axes
Range
Throughput
Power
Throughput
Wireless Spectrum
Channel Size

## Slide 4: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
IoT + WiFi

## Slide 5: What is WiFi?
Most successful wireless protocol (family)
Small Area (~35m), high performance (up to 9,600 Mbit/s)
~25 years young
  We’ll do some history
  Note the parallels in technology development
    First: Maximize the performance of a single channel
    Now: Improve performance through parallelism (more channels working together)

## Slide 6: IEEE 802.11 timeline
1985 – US FCC rules ISM band for unlicensed use
1990s – WaveLAN (NCR Corporation, Netherlands)
  Wireless ethernet for cashier systems
1997 – 802.11 specification
1999 – 802.11b and 802.11a amendments
1999 – WiFi Alliance formed for certification of devices
1999 – Apple iBook is the first consumer WiFi product

## Slide 7: Major amendments
802.11b was very popular but is now usually unsupported
802.11a never saw major deployment
WiFi Alliance rebranded 802.11ac as “WiFi 5” and backported scheme
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO (downlink only) | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.4/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.4/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 8: Resources
Peter Steenkiste – Carnegie Mellon University
  https://www.cs.cmu.edu/~prs/wirelessS18/handouts/L11-AdHoc.pdf
  https://www.cs.cmu.edu/~prs/wirelessS18/handouts/L12-LAN.pdf
Raj Jain – Washington University in Saint Louis
  https://www.cse.wustl.edu/~jain/cse574-14/ftp/j_05lan.pdf
  https://www.cse.wustl.edu/~jain/cse574-14/ftp/j_06lan.pdf
Honestly
  https://en.wikipedia.org/wiki/IEEE_802.11

## Slide 9: Outline
WiFi Overview
WiFi PHY
  802.11/802.11b
  802.11a/802.11g
  802.11n/802.11ac
  802.11ax
WiFi MAC and Packets
IoT + WiFi

## Slide 10: Goal: improve throughput
In twenty years, WiFi has gone from 2 Mbps to 9.6 Gbps
How does a network PHY improve its throughput?
More capable modulation and/or bit transmission
  Better radios
  New modulation schemes: 64-QAM, 256-QAM, etc.
Better spatial use
  MIMO techniques
More bandwidth
  OFDM techniques
  Increased channel width at 2.4 GHz and bigger 5 GHz channels

## Slide 11: Walking through PHY changes by amendment
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.5/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.5/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 12: Original WiFi specification (1997)
Legacy WiFi
  Frequency Hopping Spread Spectrum (FHSS)
  GFSK (Gaussian Frequency-Shift Keying)
    Relatively simple radio design
  Frequency hopping over 80 channels (1 MHz each)
  Actually supports an Infrared PHY as well!!

## Slide 13: 802.11b (1999)
802.11b
  Direct Sequence Spread Spectrum (DSSS)
  DBPSK and DQPSK (Differential Binary/Quadrature Phase-Shift Keying)
Translate data into “codes”
  Each data bit corresponds to several code bits (Chips)
  Chips are what is actually modulated over the air
  Data can be recovered by knowing the code patterns
Phase-shift Keying (of the Chips)
Modulation

## Slide 14: 802.11b channels
14 channels total
  1-11 for US
  1-13 for most of the rest of the world
  1-14 for Japan (but 14 only for 802.11b)
22 MHz channels
  5 MHz spacing -> significant channel overlap
  Channels 1, 6, and 11 can be used without overlap

## Slide 15: Question
If the majority of channels overlap, why even have them?
  Different options for different regions
  Inside US use three channels: 1, 6, 11
  Outside of North America can use four channels: 1, 5, 9, 13
  Historical: avoid other 2.4 GHz users
    If they’re at the low end of the band, you could switch to channel 2 or 3

## Slide 16: Walking through PHY changes by amendment
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.5/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.5/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 17: Increase performance with more bandwidth: OFDM
Replace DSSS with Orthogonal Frequency Division Multiplexing (OFDM)
OFDM idea
  Split band into a number of narrow subcarriers
  Subcarriers are spaced so that they don’t interfere
  Transmit on multiple subcarriers at once to increase throughput
  Intuition: easier to send/receive N simpler transmissions than one complex (wide bandwidth) transmission. Analogy:
    Chinese: 电脑
    English: Computer
OFDM enables higher throughput
Recall DSSS

## Slide 18: 802.11a channels
802.11a did promote the use of 5 GHz band
  Several 20 MHz channels with no overlap (9ish in the US)
    Big increase from “three” channels of 2.4 GHz
  Various regional rules on a number of different channels
    Needs to avoid frequencies in use by existing radar deployments
    Orange channels aren’t usually used in the US at least

## Slide 19: 802.11g (2003)
Applies OFDM to 2.4 GHz band
  Increases throughput from 11 Mbps to 54 Mbps
Same 2.4 GHz channels as 802.11b, but 20 MHz bandwidth
  Still 1, 6, 11 in US
  1, 5, 9, 13 in other regions
Backwards compatible with 802.11b
  Capable of DSSS communication when required

## Slide 20: Improved WiFi hardware is in high demand
Typically, standards lead hardware by several years
  BLE 5.2 is out, but 5.0 is just being adopted in phones
Development of 802.11g hardware started before finalization of standard
  Demand for increased performance was already high in 2003
Phenomena continues in modern WiFi and Cellular protocols
  Hardware supports some features as soon as it’s clear they’ll exist

## Slide 21: Walking through PHY changes by amendment
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.5/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.5/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 22: How do we increase throughput?
Wired world
  Add more wires in parallel
Wireless world
  Add more antennas?

## Slide 23: How do we increase throughput?
Water world
  Fatter pipes
Wireless world
  Fatter channels (with more bandwidth)
802.11.n — WHY NOT BOTH?

## Slide 24: MIMO – Multiple In Multiple Out
N x M subchannels can be used to send data simultaneously
  Huge boost in data throughput
  Antenna diversity adds to reliability as well
The signals may interfere with each other
  But receiving all of them allows the data to be recovered
Beamforming
  Use interactions between array of antennas to focus energy on the receiver
  Way outside of the scope of this class

## Slide 25: Expandable bandwidth
OFDM allows many subcarriers within a channel to be used at once
  Throughput scales with the amount of bandwidth available
  Allow larger 40 MHz channels to be used

## Slide 26: 802.11n (2009)
Supports OFDM and MIMO on 2.4 GHz and 5 GHz
Supports 20 MHz and 40 MHz channels
  Easier to create large channels in 5 GHz band
Backwards compatible with 802.11g (tries not to be with 802.11b)
Wildly successful
  Still the 2.4 GHz band protocol (802.11ac is 5 GHz only)
  A little less than half of the networks visible to me are still 802.11n

## Slide 27: 802.11n modulation and coding schemes
MCS – Modulation and Coding Scheme
GI – Guard Interval: delay between transmitted symbols

## Slide 28: Break + Open Question
How much bandwidth is acceptable to use?
  Is it okay for a WiFi network to use the entire 2.4 GHz spectrum?
  Maybe. At least the range is pretty short!
    Only next-door neighbor’s network interfere with your network
    Someone further away isn’t affected at all
  Need to share with neighbors nearby though
    Theoretically better to have separate allocations than to overlap and deal with the collisions

## Slide 29: Walking through PHY changes by amendment
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.5/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.5/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 30: “The MIMO Gap”
Access points have 3-4 [or more now] antennas
Client devices have 1-2 [or more now] antennas
  While absolute numbers keep going up, trend holds
  Asymmetric design pattern again: More complexity in the AP than clients
Original MIMO was one device at a time
No expand to be multiple device simultaneously

## Slide 31: Multi-user Multiple In Multiple Out (MU-MIMO)
Multi-user MIMO uses the same techniques to send in parallel to multiple devices

## Slide 32: 802.11ac (2013)
Update for 5 GHz band only
  Supports Downlink MU-MIMO (from AP to device)
  Supports channels widths up to 160 MHz
  Engineering updates: up to 256-QAM
Routers apply 802.11ac to 5 GHz and 802.11n to 2.4 GHz
Still in wide use (as of 2023)
  Eduroam is 802.11ac

## Slide 33: 802.11ac channels

## Slide 34: 802.11ac modulation and coding schemes
4 spatial streams is also allowed, getting up to 3466 Mbps

## Slide 35: Walking through PHY changes by amendment
 | Protocol | Year | Frequency | PHY | Max Rate | Range
- | 802.11 | 1997 | 2.4 GHz | DSSS/FHSS | 2 Mbps | 20 m
1 | 802.11b | 1999 | 2.4 GHz | DSSS | 11 Mbps | 35 m
2 | 802.11a | 1999 | 5 GHz | OFDM | 54 Mbps | 35 m
3 | 802.11g | 2003 | 2.4 GHz | OFDM | 54 Mbps | 38 m
4 | 802.11n | 2009 | 2.4/5 GHz | OFDM + MIMO | 600 Mbps | 70 m
5 | 802.11ac | 2013 | 5 GHz | OFDM + MU-MIMO | 3.4 Gbps | 35 m
6 | 802.11ax | 2021 | 2.5/5/[6] GHz | OFDMA + MU-MIMO | 9.6 Gbps | 35 m
7 | 802.11be | TBA | 2.5/5/6 GHz | OFDMA + MU-MIMO | 40 Gbps | 35 m

## Slide 36: New directions in WiFi focus: Aggregate throughput across all devices
For point-to-point, WiFi is “(more than) fast enough”
Now the problem is the quantity of devices in a single space
  Desktop, laptop, tablet, smartphone, smartwatch, IoT devices, etc.
Insight: Bring established cellular techniques to WiFi

## Slide 37: Orthogonal Frequency Division Multiple Access
OFDM: split channel into subcarriers and transmit on those
OFDMA: allocate subcarriers to a device for an amount of time
  Turns OFDM into an access control mechanism
  Complicated question: which device gets which subcarriers at which time?

## Slide 38: OFDM vs OFDMA Orthogonal Frequency Division Multiplexing vs. Orthogonal Frequency Division Multiple Access
Net spectrum usage ~the same
In same time slot, assign sub-carriers to different users
  Effect: Lower bandwidth per user, but more simultaneous users
This is the same strategy cellular “resource blocks” use
  Called “Resource Units” in WiFi

## Slide 39: 802.11ax (2021)
Standard approved on February 9th 2021
  First devices started supporting it in 2019 (WiFi 6)
6 GHz band (WiFi 6E)
  1.2 GHz of bandwidth (5.925-7.125 GHz)
  2020: US FCC made band available for unlicensed use!!!
  EU followed by June 2021
OFDMA
  MAC scheduling variant of OFDM
  AP schedules devices based on time and subcarrier allocations

## Slide 40: 6 GHz band is an enormous amount of bandwidth

## Slide 41: Less bandwidth in the 6 GHz band in Europe

## Slide 42: WiFi 6 Hardware
Two varieties:
  WiFi 6
    Most of the features, but NOT the new frequencies
  WiFi 6E
    Includes the extra 6 GHz channels
    Basically entirely unused as of 2023
WiFi 6E is the stuff you want for future proofing

## Slide 43: What’s coming next: 802.11.be
Still in flux, “WiFi 7” aka “Extremely High Throughput” (EHT)
Adds…
  More channel bonding / wider bandwidth: up to 320 MHz
  Up to 4096-QAM
  Up to 16-stream MIMO
  AP coordination for non-enterprise networks
  Lots of fancy timing estimation stuff (802.1Q)
    Primary focus seems to be AV-streaming Quality-of-Service (QoS)

## Slide 44: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
  802.11 Access Control
  802.11 Frame format
  802.11e Improvements to MAC
IoT + WiFi

## Slide 45: Basic WiFi network
Star topology network
Basic Service Set (BSS)
  Access point(s)
  Multiple connected clients
Service Set ID (SSID)
  Identifies network
  Broadcast by access point in beacons

## Slide 46: WiFi superframe structure
Beacon followed by contention-free period followed by contention
  Repeats periodically (default ~100 ms)
  802.15.4 adopted a similar superframe
This is more hypothetical than real

## Slide 47: WiFi superframe in practice
Continuous contention access period
  Any device may send at any time
  PCF is unused in practice
Periodic beacons
  Which also use CSMA and therefore may be delayed
Time
Delayed Beacon
Beacon
Contention
Based Access

## Slide 48: 802.11 beacons
Transmitted periodically (~100 ms by default)
  Enable discovery of network
    Contain capabilities and SSID for the network (802.11b/g/n/ac/ax…)
  Assign contention-free slots if used
  Notify devices of waiting packets
    Traffic Indication Map (TIM) has a bitmap specifying which devices data is for
    Enables devices to sleep, skipping a number of beacons
  Handles broadcast/multicast messages
    Every N beacons includes a notation of available broadcast messages
    Messages are transmitted during next contention access period using normal CSMA
    Defines maximum sleep period for devices (must listen to these beacons)

## Slide 49: Contention-free access
Known as Point Coordination Function (PCF)
  Allocates a contention-free period for specific devices
  Access Point decides when to grant based on requests
Drawbacks
  Latency depends on beacon intervals
  Mechanism for explicit Quality of Service is unclear
PCF is not used in practice

## Slide 50: Contention-based access
Known as Distributed Coordination Function (DCF)
  Base communication method for WiFi (essentially always)
  All packets are immediately ACK’d by receiving device
  Uses CSMA/CA to determine when it can send
    With random backoff
  Problem: packets can be very long (up to 20 milliseconds)
  Solution: Network Allocation Vector (NAV)
    Packets include a notation of their duration
    Sensing the beginning of a packet allows backoff to skip the whole packet duration before continuing

## Slide 51: Reminder: hidden terminal problem
Two devices communicating with Access Point may not be able to hear each other
  CSMA fails and Access Point losses both messages
A solution: RTS/CTS (Request/Clear To Send)

## Slide 52: Drawbacks of RTS/CTS
Four packets per data (RTS, CTS, Data, Ack)
  Could have just sent data instead of RTS
Significant portion of traffic are application-layer Acks
  Probably better to just have it fail and try again later
RTS/CTS only used for very large packets in practice
  *It’s mentioned still in 802.11n and 802.11ac, so not entirely unused

## Slide 53: Backoff in WiFi
Listen for activity
  If free
    Wait for Inter Frame Spacing (IFS)
    If still free, transmit
  If busy
    Randomly select a number of backoff Slots
    Count down slots whenever medium is not busy
    If busy when backoff completes:
      Increase maximum backoff Slots
      Repeat
Slot time: basic time unit for protocol
  Total time of: switch from Rx to Tx, plus processing time, plus propagation delay

## Slide 54: Prioritizing packets with varying IFS
Tiered Contention Multiple Access (TCMA)
  Idea: assign different inter-frame spacing based on traffic class
  Inherently prioritizes communication
Acknowledgements sent with Short IFS (SIFS)
  Will always transmit before new data clears CSMA check
New data sent with DCF IFS (DIFS)

## Slide 55: Putting backoff together
Two variables
  Contention Window (CW) – maximum backoff amount
  Backoff Count (BO) – current remaining backoff
When attempting to send, if busy Backoff selected in [0, CW]
  Countdown Backoff slots whenever medium is not busy
  At 0, attempt to transmit if not busy
  If busy, double Window and select Backoff again
802.11g values:
  Slot time= 20 us, CWmin= 15 slots (300 us), CWmax= 1023 slots (20 ms)
  SIFS= 10 us, DIFS= 50 us

## Slide 56: 802.11 backoff example
A and B want to send and see the medium is busy
  Followed by an Acknowledgement after SIFS
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B

## Slide 57: 802.11 backoff example
Each chooses a random backoff [0, CW] (we’ll say CW is 32)
  Start counting down backoff slots
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8

## Slide 58: 802.11 backoff example
C wants to send, waits DIFS, and can send immediately
  No other traffic is going on
  A and B pause backoff for packet duration
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic

## Slide 59: 802.11 backoff example
A and B used NAV to pause backoff for entire traffic plus ACK
  After DIFS, resume backoff count from its previous value
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
SIFS
ACK
DIFS

## Slide 60: 802.11 backoff example
B reaches zero backoff, finds channel empty, transmits
  A pauses its backoff again for duration plus ACK
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
B Traffic
SIFS
ACK
DIFS

## Slide 61: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
IoT + WiFi

## Slide 62: Why, why not, talk WiFi in a wireless for IoT class
Pros
  Ubiquitous
  High-performance
Cons
  Complex configuration
  And security requirements
    Device-Northwestern anyone?
  Expensive in energy and money

## Slide 63: WiFi capability in microcontrollers
ESP32
  Microcontroller plus WiFi radio in single chip
  (Same idea as nRF52840)
Capabilities
  802.11b/g/n 2.4 GHz only
  20 MHz or 40 MHz channels
  Single antenna only (no MIMO)
  MCS0-7
    7 Mbps – 150 Mbps
  Tx power up to 20.5 dBm

## Slide 64: Low power WiFi
Question: should a microcontroller stay connected or reconnect?
  Light sleep: stay connected always, only listening to beacons
  Deep sleep: reconnect to network each time data is ready
Answer for ESP32 depends on security and data interval
  Resecuring during connection takes lots of energy
    Crossover point is about 60 seconds
  Insecure transmissions have a crossover of 5-15 seconds
https://blog.voneicken.com/2018/lp-wifi-esp-comparison/#conclusions

## Slide 65: Bonus: MQTT – answer to the “where do you send data” question

## Slide 66: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
IoT + WiFi

## Slide 67: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
  802.11 Access Control
  802.11 Frame format
  802.11e Improvements to MAC
IoT + WiFi

## Slide 68: 802.11 frame
Frame control (various bits)
  Type of packet (Control, Management, Data)
  Subtype (Association, RTS, CTS, Ack, etc.)
  Indication of to/from “distribution system” (Internet rather than intranet)
Duration
  Specifies on-air time of full packet in microseconds
  Note: no actual length field 😱
Surprising, but smart!
Recall modulation schemes vary — but everyone needs to be able to parse header (for duration, for NAV)
Length can be very large (e.g. in ac: 5.5 ms max duration is 4.5 MB length!); sent at full data rate

## Slide 69: 802.11 frame
Sequence control
  4-bit fragment number
  12-bit sequence number
Quality of Service control
  Identifies traffic category
High Throughput Control
  Configurations for selecting best data rate
Frame body
  Max size depends on PHY
    ~2000 for lower rates
    ~8000 for 802.11n
    ~11000 for 802.11ac
Frame check sequence
  32-bit CRC

## Slide 70: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
2
2
Devices filter on Address 1

## Slide 71: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
3
3
Devices filter on Address 1

## Slide 72: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
1
Devices filter on Address 1

## Slide 73: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
4
4
Devices filter on Address 1

## Slide 74: Sending frames in WiFi
Frame bursting
  Transmit multiple frames in a row
Frame fragmentation
  Split service data over multiple frames
Frame aggregation
  Multiple service data in a single frame
  Allows multiple packets to reach Access Point in a single transmission

## Slide 75: Calculating packet durations
Example duration for a 1500 byte 802.11g packet
  6 Mbps for header
  24 Mbps for payload
  566 μs for total packet
    Plus 10 μs for SIFS
    Plus 34 μs for ACK
https://sarwiki.informatik.hu-berlin.de/Packet_transmission_time_in_802.11

## Slide 76: Implementation Drives Specification Sometimes
SIFS nominally defined by processing time
  Aside: Big challenge for SDRs
Convolutional decoders need(ed) 16 µs to finish processing
  For highest-rate MCS (ERP-OFDM)
  SIFS is 10 μs, so extension needed
Processing must finish before next packet starts
  To be able to decode NAV in header
Notes: https://www.electronics-notes.com/articles/connectivity/wifi-ieee-802-11/802-11g.php

## Slide 77: Break + xkcd
https://xkcd.com/2199/

## Slide 78: Outline
WiFi Overview
WiFi PHY
WiFi MAC and Packets
  802.11 Access Control
  802.11 Frame format
  802.11e Improvements to MAC
IoT + WiFi

## Slide 79: 802.11e improves MAC layer
Hybrid Coordination Function (HCF)
  Modifies contention-free access (still no one uses it)
  Modifies contention-based access: Enhanced Distributed Channel Access (EDCA)
Modifies Quality of Service based on application
  Example of breaking layering for an optimization
  Categories (lowest to highest priority):
    Background
    Best Effort
    Video
    Voice

## Slide 80: Different priority for different application category
Expand to more IFS lengths for different traffic categories
  Smallest AIFS (equal to DIFS) goes to Voice, Largest to Background
  Contention Window min and max also change for each category
    Selects a probability that most important category goes first

## Slide 81: Multiple queues within a single device

## Slide 82: 802.11e also adds maximum durations
802.11e also defines duration a device can transmit for
  Based on PHY in use and Application category
  Background/Best Effort: one frame per contention win
  Example, up to 11 ms for Voice on 802.11ac
    Could be one really big frame at a low data rate
    Could be multiple frames in a row separated by SIFS