## Slide 1: Wireless for the Internet of Things LPWAN and LoRa
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Nasir]

## Slide 2: Housekeeping
Don’t forget to take mini quiz on WiFi now!
Assignment 4 is out
  Based on Lab 5 (WiFi)
  Sorry about the numbering scheme! 😓
Overview about assignment + Q&A during my OH at 2pm tomorrow
  I’ll try to book a bigger meeting room!
PollEverywhere: PollEv.com​/wiot23nn

## Slide 3: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
Research for Improving LoRaWAN

## Slide 4: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 5: How do we collect data from MANY sensors?
Manually collect measurements
Connect it to WiFi (or Ethernet)
Pay for cellular access

## Slide 6: 2.4GHz protocols mostly used for indoor applications
Range for the wireless protocols we’ve looked at so far (best case)
  BLE: 100m (~300ft)
  802.15.4: 100m (~300ft)
  WiFi: 70m (~230ft)

## Slide 7: We need another network option
What requirements do we need?
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small
Notes: what should the end device requirements be?
- power
data requirements
what about the receiving device requirements?
  coverage range

## Slide 8: Wide area networks
Communication at the region/city scale rather than the building/residence scale
  Throughout cities
  Agricultural deployments
  Industrial facilities
City-scale sensing is one very popular domain
  What might we want to sense throughout a city?

## Slide 9: Long-range, low-data needs haven’t historically been met
Data
Throughput
Range
WiFi

## Slide 10: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
802.15.4
Data
Throughput
Range

## Slide 11: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
802.15.4
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 12: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
2G
3G
4G
BLE
802.15.4
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
3G

## Slide 13: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
3G
4G
BLE
802.15.4
Low-Power Wide-Area Networks
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
2G

## Slide 14: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 15: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
Research for Improving LoRaWAN

## Slide 16: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Low rate (1-20 kbps) and long range (~5 km)
  Shorter range than Sigfox but much higher bit rate
Most popular LPWAN protocol
  Target of academic research
  Industry involvement in hardware and deployments

## Slide 17: LoRa PHY uses a spread spectrum modulation technique
Chirp Spread Spectrum (CSS)
  Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 18: How does FSK, up-chirp, and down-chirp “sound” like?
Source: LoRa CHIRP by Richard Wenner

## Slide 19: Data Modulation in Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel
+
Input Binary Data

## Slide 20: Data Modulation in Chirp Spread Spectrum
In general,
n bits => divide BW to 2n initial frequencies
Remember, No. of symbols = 2n
Source: https://swarunkumar.com/slides/choir-sigcomm2017.pdf

## Slide 21: LoRa Modulated Signal
Source: https://youtu.be/lg0eZWZFKiE

## Slide 22: CSS has a Spreading Factor which determines bit rate
Spreading Factor is essentially the rate-of-change of frequency (sweep rate)
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision
LoRa has 6 spreading factors:
SF7 to SF12
Notes: https://www.thethingsnetwork.org/docs/lorawan/spreading-factors/

## Slide 23: LoRaWAN channels (in the US)
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not used in practice)
Eight, 500 kHz downlink channels

## Slide 24: LoRaWAN gateways
No synchronization with end devices
Instead listen to entire bandwidth simultaneously
  Only 12 MHz total
  Recognize preambles and allocate hardware to decode packet
    Cheap gateways: 8 decoders
    Good gateways: 64 decoders

## Slide 25: LoRaWAN data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate options depend on channel in use
  Unbalanced uplink and downlink
64-channel uplink
  1-5 kbps data rate
Allowable rates based on US dwell time restriction (400 ms)
  Different in different regions
Notes: Dwell time (or transmit time) is the amount of time needed to transmit on a frequency

## Slide 26: LoRaWAN link budget
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is about a kilometer in urban environments

## Slide 27: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: LoRaWAN has 3 types of device classes based on RX behavior (Class A, B, and C)
Notes: Aloha: send without sensing, if collision, wait for random delay and then send again

## Slide 28: LoRaWAN has Device Classes based on RX behavior
listen-after-send (class A device)
  Two windows for RX on different channels
Periodic listening (class B device)
  Also has 2 RX windows after TX
  Synchronized with periodic beacons
  Has periodic ping slots (RX windows)
  Gateway can reach without waiting for TX
Continuous listening (class C device)
  Always-on receivers
Good Reference: https://www.thethingsnetwork.org/docs/lorawan/classes/

## Slide 29: LoRaWAN packet format
Frame header includes device address
MAC Payload maximum size depends on data rate
Data Rate Index | MAC Payload Size
0 | 19 bytes
1 | 61 bytes
2 | 133 bytes
3 | 250 bytes
4 | 250 bytes

## Slide 30: LoRaWAN network details

## Slide 31: LoRaWAN hardware
Numerous hardware modules and development kits
  Almost all use Semtech radio chips (Semtech owns LoRa PHY)
Recent addition: STM32WLE5 LoRa SoC
  Cortex-M4 + LoRa radio (analogous to nRF52840)

## Slide 32: LoRaWAN network providers
You can always manage your own network
  Buy a gateway and run whatever backend software you want
Somewhat-managed network providers
  The Things Network (predominantly in Europe)
    But available in the US too!
  Helium
    Anyone can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 33: TTN Scale [Mar 2023]

## Slide 34: Helium Scale [Mar 2023]

## Slide 35: Helium Scale [Jan 2022]

## Slide 36: Quick reality check: Verizon?
And this is just crowd-sourced data…

## Slide 37: UVA Example: Smart Water Infrastructure Project
Sensor
Gateway
Server
Interface
Sensor
Gateway
Project led by Victor Sobral
Working with Prof. Jon Goodall and Prof. Brad Campbell

## Slide 38: Water Level Sensor Prototype

## Slide 39: Gateway Deployment Planning

## Slide 40: Currently one LoRa gateway operational at Rice Hall

## Slide 41: RSSI values from the LoRaWAN field test

## Slide 42: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink

## Slide 43: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink
Outdoor small-sized sensing seems possibly achievable!
  With a low enough rate, it could support many devices
Code updates on devices could be tough

## Slide 44: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
Research for Improving LoRaWAN

## Slide 45: Unlicensed LPWANs is a very active research area
Active work on:
  Better access control mechanisms
  Increasing bandwidth by utilizing other spectrums like TV white spaces
  Recover simultaneous transmissions
    Goal: reduce re-transmissions, increase end-device sleep and battery life
Let’s look at some tricks people have done to recover simultaneous transmissions!

## Slide 46: Resources
Swarun Kumar (CMU) - https://swarunkumar.com/lpwan.html
Choir
  https://swarunkumar.com/papers/choir-sigcomm2017.pdf
  https://swarunkumar.com/slides/choir-sigcomm2017.pdf
Charm
  https://swarunkumar.com/papers/charm-ipsn2018.pdf
Opportunistic Packet Recovery
  https://swarunkumar.com/papers/opr-mobisys2020.pdf

## Slide 47: Can we distinguish data from LoRa chirps that have collided?

## Slide 48: Choir concept
  Yes! By applying signal processing to the problem
Data in time domain
Data in frequency domain

## Slide 49: Background: Fast Fourier Transform (FFT)
Converts individual signal to its spectral components
https://www.nti-audio.com/en/support/know-how/fast-fourier-transform-fft
Interesting read: Cocktail Party Audio data separation using FFT

## Slide 50: What happens when LoRa chirps collide?

## Slide 51: What happens when LoRa chirps collide?

## Slide 52: Imperfections in hardware create offsets

## Slide 53: Decoding colliding packets

## Slide 54: Choir results
Recovering collided packets resolves losses due to Aloha transmission!
Increases maximum throughput on the network considerably!
Does require modifications to hardware on gateways though

## Slide 55: Can we recover weak LoRaWAN signals?

## Slide 56: Charm
Take advantage of multiple gateways in range of a device
Combine signals received at each gateway to recover packets that weren’t received cleanly

## Slide 57: Coherent combining
Signal received at each receiver is a combination of
  Signal
  Wireless channel
  Random noise
Signal and wireless channel are similar at all receivers
Noise is different though! Independent
When combined, signals are coherent (build in strength) whereas noise is incoherent (spreads out)

## Slide 58: Charm uses coherent combining across gateways
Gateways send signal data to the cloud
The cloud can perform combining on the data and recover signals
Challenges
  Only send the data when it’s needed
  Tight time synchronization on the data
  Gateway hardware changes

## Slide 59: Can we recover packets that have bad CRCs?

## Slide 60: Opportunistic Packet Recovery (OPR)
What if we have some information about where the interference might have occurred during the signal transmission?
OPR demonstrates that we can recover packets!
Process
  Receive bits even for bad packets
  Measure RSSI for each bit along the way
  Look for changes in RSSI that signals interference
  Try different values for the effected bits until the CRC succeeds!

## Slide 61: Detecting error bits in transmitted packets
Correctly identifies 83% of the corrupted bits with 17% false positives

## Slide 62: Multiple gateways do even better
If multiple gateways receive the packet, they can compare their received data
Common bits are likely correct, while differences are likely interference

## Slide 63: OPR total design
Bad packets are sent to the OPR Server for handling along with RSSI data
OPR server attempts to reconstruct the packet
In practice, system can correct up to 72% of CRC errors!
  Also completes correction in time for the ACK response (within 1 second)

## Slide 64: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
Research for Improving LoRaWAN

## Slide 65: Resources
LoRaWAN
  LoRaWAN Specification version 1.1
  LoRaWAN Regional Parameters version 1.0.2