## Slide 1: Wireless for the Internet of Things IoT Cellular, Backscatter, Matter
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
Wrap up cellular discussion
  Understand how cell companies want to support the IoT market
Introduce backscatter
  RF-based technique for low power communication
Discuss Matter
  Future of smart home?

## Slide 3: Outline
IoT Cellular
Backscatter
  RFID
  IoT Backscatter
Matter

## Slide 4: Reminder: the cell in cellular technologies
Place towers at corners of cells
  Directional antennas send three different frequency bands, one per cell
  Each cell gets three tower and three bands
Density of cells varies based on expected number of users
  Change cell size using Power Control

## Slide 5: 3GPP (aka: the actual answer for what stuff is really doing)
3rd Generation Partnership Project (3GPP)
Industry alliance for development of telecoms standards
  Established around 1998
  Makes “Releases” which are roughly analogous to IEEE standards/versions
    Release 8 (2008) LTE ~4G
    Release 15 (2018) NR (New Radio) ~5G
Focused on the practical
  ITU post-hoc defined “4G”, 3GPP defined LTE

## Slide 6: Mapping ”4G”, “LTE”, “LTE Advanced”, etc onto actual technologies
This Qualcomm presentation is great: https://www.qualcomm.com/media/documents/files/demystifying-3gpp-and-the-essential-role-of-qualcomm-in-leading-the-expansion-of-the-mobile-ecosystem.pdf

## Slide 7: LTE Categories
Different equipment supports different “categories” of LTE
  Maximum MCS index supported
Examples
  iPhone 6 (2015): Cat 4
  Pixel 3 (2018): Cat 16
Notes: MCS = Modulation Coding Scheme
https://mcsindex.com/ looks like all the tables for WiFi; not clear whether this is the same for cell

## Slide 8: Additional low-end categories for IoT
LTE-M (LTE Cat M1)
  375 kbps uplink, 300 kbps downlink (for the actually implemented mode)
  Reduced power and maximum bandwidth
  Increased range
NB-IoT (LTE Cat NB1)
  65 kbps uplink, 26 kbps downlink
  Reduced power and greatly reduced bandwidth
  Greatly increased range

## Slide 9: Why do we need “special categories” for IoT on cell?
Pragmatic for the end device
  Lower power
  Allow for long-off periods
Pragmatic for network operators
  Allows for scale: network no longer needs to assume that devices could always be on in each cell

## Slide 10: LTE-M and NB-IoT were developed in parallel

## Slide 11: LTE-M and NB-IoT downlink and uplink
OFDMA downlink
  Put the more complicated hardware in the cell tower [simple FFT demodulator]
SC-FDMA (single carrier FDMA) uplink
  Blocks of subchannels combined into one signal
  Similar concept, but simpler for end devices to implement

## Slide 12: LTE resource allocation
Cellular uses OFDMA to schedule
  Time + Frequency -> “2D Scheduling”
Cellular uses single channels up to 20 MHz
  Further divides these into 100 Resource Blocks
Resource Block
  12 subcarriers for OFDM in frequency (15 kHz each)
  7 symbols in time (0.5 ms)
Devices are allocated frequency and time based on what they are sending
  Allocated in units of Resource Blocks

## Slide 13: Resources used by LTE-M and NB-IoT
LTE-M uses up to 6 resource blocks
  1.4 MHz of bandwidth (1.080 MHz)
  Can co-exist with other normal LTE traffic, scheduled by cell tower
  Limited to only some capability of LTE
NB-IoT uses up to 1 resource block
  200 kHz of bandwidth (180 kHz)
  Multiple deployment options
    Guard-band in practice

## Slide 14: Reducing power for IoT devices
Reduce max Tx power to 20 dBm
  Increased receive sensitivity at tower will cover it
Extended Discontinuous Reception (eDRX)
  Allow devices to reduce paging period and still stay on network
  Cell tower will hold messages
What does this get to?
  “For a LTE-M1 device that transmits data once per day, and wakes up every 60 hyper frames to check for commands (this would be about every 10 minutes), a life of 4.7 years is achievable on 2 AA batteries.”
Graphics, quote from https://www.link-labs.com/blog/lte-e-drx-psm-explained-for-lte-m1

## Slide 15: Further power reduction for simple devices
Power Saving Mode (PSM)
  For very simple, uplink-focused devices, allow them to turn off entirely but stay connected
  Minutes to days in duration
  Notify tower before sleeping, listen for packets after each transmission
Graphics from https://www.link-labs.com/blog/lte-e-drx-psm-explained-for-lte-m1

## Slide 16: Some numbers from an actual telecom: Aeris [n.b. Aeris has been a leader in cellular M2M since the 90’s]
PSM has two timers, devices request values, tower chooses actual:
  Extended Timer (“sleep” timer)
    3GPP max is 35,712,00s [413.33 days]
    Aeris timer range: Min 240m [4h]; Max 413 days
    “Aeris Fusion” timer range: Max: 12.9 days
  Active Timer (how long will the device stay in idle after communication?)
Numbers from https://aeriscom.zendesk.com/hc/en-us/articles/360049848254-Understanding-LTE-M-Power-Management-Modes
Notes: Really hard to tell difference between Aeris and Aeris Fusion. I think Aeris Fusion is a new product that allows devices (same SIM?) to dynamically switch between an IoT profile and a full-fledge voice / high-bw data profile. My guess then is that Aeris network is all their own owned infra, and Fusion is them acting as an MVNO [thus limited to others for wakeup range]

## Slide 17: Improved range for LTE-M and NB-IoT
LTE defines a Maximum Coupling Loss (MCL) a.k.a Link Budget
  Traditional cellular: 144 dB (~2.5 km)
  LTE-M: 160 dB (~5 km)
  NB-IoT: 164 dB (~10 km)
  Sigfox: ~155 dB
  LoRaWAN: ~143 dB
Note that many cellular bands are often on higher frequencies
  Example: 1900 GHz

## Slide 18: Coarsely, lower frequency -> longer range
This was the picture circa 2019
Why else might T-Mobile have really wanted to buy Sprint…

## Slide 19: Cellular deployments
Originally unclear which would be dominant
  Verizon and AT&T focused on LTE-M
  T-Mobile focused on NB-IoT
  All rolled out services nationwide in the 2018-2019 timeframe
Networks are expanding to provide both capabilities
  LTE-M: AT&T, T-Mobile, US Cellular, Verizon
  NB-IoT: AT&T, T-Mobile
Pricing models still very uncertain
  NB-IoT example: $5 per device per year up to 12 MB, 10 packets per hour
  Future adoption will greatly depend on these

## Slide 20: Outline
IoT Cellular
Backscatter
  RFID
  IoT Backscatter
Matter

## Slide 21: Resources
This Bell Labs instructional video from 1959 is excellent background:
  https://www.youtube.com/watch?v=DovunOxlY1k

## Slide 22: What does an antenna do?
Loosely: Converts between electric and magnetic waves
Animation by Chetvorno - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=40789783

## Slide 23: What generates electric waves?
RF front end
  can be done with high-speed digital components (e.g. fast DACs)

## Slide 24: What receives electric waves?
Could be a high-speed ADC, more often with analog pieces in front:
Graphics from Analog Devices whitepaper: https://www.analog.com/media/en/technical-documentation/tech-articles/480501640radio101.pdf — significantly more detail here

## Slide 25: What happens if nothing ‘receives’ the wave?
From: https://www.flippingphysics.com/standing-waves.html

## Slide 26: “Fixed end” and “Free end” in electronic transmission
~
~
Short Circuit = “Free End”
- Reflects wave
Open Circuit = “Fixed End”
- Inverts wave
~
Matched Load
- Absorbs wave (no reflection)

## Slide 27: Backscatter systems reflect waves rather than generate waves — significant (10,000x or more) power savings
Simple versions just ‘reflect or don’t reflect’
Modern designs can do more advanced modulation as well
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=8368232

## Slide 28: Backscatter is an old idea — history in spycraft!
1945: Leon Theremin* creates “The Thing” (aka Great Seal Bug)
  *Yes, same guy who invented the instrument
  Discovered when a British embassy radio operator heard recorded conversations

## Slide 29: Outline
IoT Cellular
Backscatter
  RFID
  IoT Backscatter
Matter

## Slide 30: RFID is everywhere nowadays
Fundamental design principle is asymmetry
  Extremely simple, cheap tags
  Complex readers

## Slide 31: A brief digression to be precise in terminology
RFID = Radio Frequency Identification = “a” communication standard
  A ton through ~early 90’s; “EPC” ~= UPC, standardized; most now EPC Gen2
There are actually three types of “RFID” device
  Passive Tags - harvest power from reader & reflect
  Semi-Passive Tags - on-board power, but reflect data
  Active Tags - on-board power that transmit data
These are ”backscatter” — which describes any communication via reflected RF
Notes: The point: Papers misuse “RFID” to mean backscatter, and misuse “passive tag” to mean anything that doesn’t actively emit RF.
Most things that do backscatter don’t do the energy harvesting bit
Many papers that do backscatter describe themselves as RFID, but don’t follow any RFID communication standard

## Slide 32: The meaningful difference is in how the tag devices power themselves
Even on simple designs, need some power:
Let’s look at E-ZPass again:

## Slide 33: Let’s look at RFID standards to get a sense of the numbers
Low Frequency (~300 kHz) — mostly legacy
  ~10cm read range
High Frequency (3~30 MHz; often 13.56 MHz)
  Passive: 4~7 m max
  Semi-Passive: 10~30 m max
  Active: 30+ m
Ultra-High Frequency (300 MHz ~ 3 GHz)
  Passive: Up to 12 m
  Active: Up to 100 m

## Slide 34: Sidebar: What’s NFC?
Near Field Communications is a subset of the RFID protocol
  10-20cm range (usually <10)
  Inductively coupled loop antennas
    Communicates via local magnetic field rather than electromagnetic waves
      This is the “near-field” part
    (Basically a transformer)
Note, does still emit RF, just weakly (i.e. can be eavesdropped on from afar)

## Slide 35: Outline
IoT Cellular
Backscatter
  RFID
  IoT Backscatter
Matter

## Slide 36: “Embedded” sensors
How do you change batteries in a device that’s inside a wall or inside someone’s body?

## Slide 37: Backscatter for sensor networks
Backscatter allows transmissions at up to 10000x lower power than conventional radios
  Makes it very attractive for low-energy sensing devices
Backscatter
Transmissions
Conventional
Radio
Backscatter Tag

## Slide 38: RFID sensors
First iterations were literally RFID sensors
  Limited by cost and range of RFID readers (only a few meters)
WISP 5.0
University of Washington
Moo 1.0
University of Massachusetts

## Slide 39: Backscatter + LPWAN = usable?
Idea:
  Backscatter is about low energy operation
  LPWANs are about long-range operation
  Can we combine them for low energy and medium-long range?
LoRea: long-range transmissions at μW
Varshney et al. ”LoRea: A Backscatter architecture that achieves a long communication range” SenSys 2017

## Slide 40: Design element #1: LoRea decouples the carrier signal generation and reception
Bi-static setup spatially separates carrier generation from the receiver
Use devices that surround us for providing the necessary carrier signal
Self-interference reduced due to path loss suffered by carrier signal
Bi-static configuration
Monostatic configuration
Notes: + If we look into a RFID reader's configuration, there is a single device that both receives the backscatter transmissions and generates the necessary carrier signal. This is called a monostatic configuration.
+ In LoRea, we decouple the task of carrier signal generation and the reception of the backscatter transmissions. We adopt a bistatic configuration as we show in the slide. We have a dedicated device for carrier signal generation and reception.
+The advantage of the bistatic configuration is two-fold: First, we can attenuate the carrier signal arriving at the receiver due to the path loss suffered due to the propagation of the wireless signal. This helps us reduce interference from stronger carrier signal to much weaker backscatter transmission. Second, it also enables us to use the devices that surround us, such as smartphones or wifi router, as sources for providing the necessary carrier signal to support backscatter transmissions. In fact, in lorea, we demonstrate the use of these devices to provide the carrier signal.’

## Slide 41: Design element #2: LoRea backscatters at a frequency offset from the carrier signal
Backscatter is a mixing process
Transceivers attenuate interference at adjacent frequency channels
Frequency separation reduces interference from carrier to backscatter signal
No complex self-interference mechanisms required at reader
Notes: + The second design element that we incorporate in the design of LoRea is that we create separation in frequency between the carrier signal and the reflected transmissions. We transmit the backscattered signal at a particular offset from the carrier signal. This is unlike systems such as RFIDs that transmit at the same frequency as the carrier signal, requiring complex and expensive self-interference cancellation mechanisms.
+ To backscatter at an offset from the carrier signal, we take advantage of the property that the backscatter is a mixing process. If a carrier signal is incident on the backscatter tag, and if we toggle the antenna, i.e., change the antenna's state between absorption and reflection state at a frequency delta f, we can now create backscatter transmissions at a frequency offset of Fc+delta F due to the mixing property.
+ Most modern radio transceivers have bandpass filters present in adjacent frequency bands. They support these to enable co-existence on the shared wireless spectrum to suppress interference from adjacent traffic. We use these filters to our advantage; we place the carrier signal in the bandpass filter and significantly attenuate the carrier signal.
+ By incorporating the decoupling in space and frequency, we can reduce the interference to the weak backscatter transmissions from stronger carrier signal by up to 50-70 dB. We do not need to employ any complex self-interference cancellation mechanisms that are used on existing RFID readers. We use off-the-shelf commodity transceivers that just cost a few usd to carrier generation and the reception, thus significantly lowering the infrastructure's cost and complexity to support backscatter transmissions.

## Slide 42: Ran out of space while performing experiments
State-of-art few meters. We achieved kilometers, was difficult to anticipate
Initial experiments conducted near the university and a river
Experiment Setup
Receiving transmissions 1km away from the setup

## Slide 43: LoRea outperforms state-of-the-art systems
System name | Communication range
LoRea – 868 MHz (SENSYS 2017) | 3400 m
LoRea – 2.4 GHz (SENSYS 2017) | 225 m
RFID | < 18 m
BackFi (SIGCOMM 2015) | 5 m
Passive WiFi (NSDI 2016) | 30 m
HitchHike (SENSYS 2016) | 54 m
Interscatter (SIGCOMM 2016) | 30 m
LoRa Backscatter (UBICOMP 2017) | 2800 m
Range reported are line of sight, with backscatter tag co-located with carrier source

## Slide 44: Future research directions for backscatter sensor communication
Improve capabilities for “ambient” backscatter
  Reuse existing RF signals rather than relying on carrier generation
MAC layers for backscatter
  Need ability to communicate with very low power
  How do you manage access to the medium?
Real-world usable backscatter stacks and hardware
  Needs to be deployable and usable by non-experts

## Slide 45: Backscatter as a sensor: soil moisture
Idea: bury backscatter tags in soil
  Measure round-trip-time for signal to reflect
  Ts (time signal travels through ground) changes based on the moisture in the soil
Josephson, Colleen, et al. "Low-cost In-ground Soil Moisture Sensing with Radar Backscatter Tags.“ COMPASS 2021

## Slide 46: Outline
IoT Cellular
Backscatter
  RFID
  IoT Backscatter
Matter

## Slide 47
The foundation for connected things
A seal of approval that devices will work seamlessly together today & tomorrow
Simplifying development for manufacturers and increasing compatibility for consumers.
CES 2023

## Slide 48: How We Stack Up
Common application layer + data model Interoperability, simplified setup & control
IP-based Convergence layer across all compatible networks
Secure AES-128-CCM encryption with 128-bit AES-CBC
Open-source development approach Based on market-proven technologies
Common protocol across device and mobile Extensible to cloud
Common data model Core operational functions, multiple device types
Low overhead MCU-class compute, <128KB RAM, <1MB Flash

## Slide 49: Creating Experiences that Matter
Consumers
More consistent set up experience
Multi –Admin works across & with multiple ecosystems
Developers
Develop once / deploy everywhere
Secure-by-design approach
Community of support
Retailers
Simplified purchasing experience
Minimized returns
Commercial / Builders
Future proofed ecosystem compatibility
Flexibility for users

## Slide 50: Target Device Types
Lighting, Electrical
Access Control
Blinds/Shades
Safety & Security
HVAC Controls
Access Points, Bridges
TVs
Matter controllers can be implemented in a variety of devices and interfaces
Scoping exercises for additional device types and use cases underway and continual.

## Slide 51: Open Source
Matter open source project:
github.com/project-chip/connectedhomeip
Collaborative, open-source development
Accessible, transparent, robust, and secure. Code examples showing interactions on multiple transports.
Built on market-proven technologies
Companies from across the industry are contributing market-proven technologies and best practices.
Implementation-first approach
Growing to implement the overall architecture. Not just a technical spec, but deployable code.

## Slide 52: Matter communication architecture
Multiple Phy/Link layers: Ethernet, WiFi, or Thread
IPv6 networking
Multiple transport layers
  TCP or UDP. Custom BLE layer for device setup only

## Slide 53: Matter networks
Use border routers to communication across networks

## Slide 54: Interoperability between devices
Always an IoT challenge!
Matter uses Zigbee device library
  Akin to BLE GATT device standards
BLE Profile
BLE Service
BLE Characteristic
ZigBee Profile + Device Type
ZigBee Cluster
ZigBee Attribute
Also ~ZigBee Commands

## Slide 55: Security: major emphasis for Matter
Promote security by default
Standard and software stacks handle
  Commissioning
  Setting up security certs
“Fabric”: logical set of devices that share a security domain and can communicate
Devices in Matter can support “multi-fabric”
  This would enable connecting device ecosystems together
  Does have to be implemented though…

## Slide 56: Matter Commissioning – User View
Device is manufactured and shipped
User brings Device to Smart Home
User intros Device to Commissioner (Tablet, Phone, Smart Speaker, etc.)
User initiates commissioning
Device is commissioned
Device operates smoothly in Smart Home
Light Switch
Thread Border Router
Commissioner
Wi-Fi Router
Store
Factory

## Slide 57: More on Matter
https://www.youtube.com/watch?v=v_285vCHifw
https://www.nordicsemi.com/products/matter
https://xkcd.com/927/