## Slide 1: CS6501 – Embedded OS
TinyOS and nesC
TinyOS
nesC

## Slide 2: TinyOS and nesC
TinyOS: operating system for sensor networks
nesC: Programming language for sensor networks

## Slide 3: Why TinyOS?
Traditional OSes are not suitable for networked sensors
Characteristics of networked sensors
  Small physical size & low power consumption
    Software must make efficient use of processor & memory, enable low power communication
  Concurrency intensive
    Simultaneous sensor readings, incoming data from other nodes
    Many low-level events, interleaved w/ high-level processing
  Limited physical parallelism (few controllers, limited capability)
  Diversity in design & usage
    Software modularity – application specific

## Slide 4: TinyOS solution
Support concurrency
  event-driven architecture
Software modularity
  application = scheduler + graph of components
  A component contains commands, event handlers, internal storage, tasks
Efficiency: get done quickly and then sleep
Static memory allocation

## Slide 5: TinyOS computational concepts
Events
  Time critical
  Caused by interrupts (Timer, ADC, Sensors)
  Short duration
Commands
  Request to a component to perform service (e.g, start sensor reading)
  Non-blocking, need to return status
  Postpone time-consuming work by posting a task (split phase w/ callback event)
  Can call lower-level commands
Tasks
  Time flexible (delayed processing)
  Run sequentially by TOS Scheduler
  Run to completion with respect to other tasks
  Can be preempted by events

## Slide 6: TinyOS Execution Model

## Slide 7: Concurrency
Two threads of execution
  Tasks
    deferred execution
    tasks cannot preempt other tasks
  Hardware event handler: respond to interrupts
    Interrupts can preempt tasks
Scheduler
  Two level scheduling
    interrupts (vector) and tasks (queue)
  Task queue is FIFO
  Scheduler puts processor to sleep when no event/command is running and task queue is empty

## Slide 8: TinyOS Execution Model (revisited)

## Slide 9: TinyOS Theory of Execution: Events & Tasks
Consequences of an event
  Runs to completion
  Preempt tasks
What can an event do?
  signal events
  call commands
  post tasks
Consequences of a task
  No preemption mechanism
  Keep code as small execution pieces to not block other tasks too long
  To run a long operations, create a separate task for each operation, rather than using on big task
What can initiate (post) tasks?
  Command, event, or another task

## Slide 10: TinyOS summary
Component-based architecture
  Provides reusable components
  Application: graph of components connected by “wiring”
Three computational concepts
  Event, command, task
Tasks and event-based concurrency
  Tasks: deferred computation, run to completion and do not preempt each other
  Tasks should be short, and used when timing is not strict
  Events: run to completion, may preempt tasks
  Events signify completion of a (split-phase) operation or events from the environment (e.g., hardware, receiving messages)

## Slide 11: nesC: A programming language for sensor networks
Main features
  Support and reflect TinyOS’s design
    Support components, event-based concurrency model
  Extending C with support for components
    Components provide and use interfaces
    Application: wiring components using configurations
  Whole-program analysis & optimization
    Detect race conditions
  Static language
    No dynamic memory allocation, call-graph fully known at compilation
No multiprogramming
  Each mote runs a single application

## Slide 12: nesC model
Application: graph of components
  Main component
    init, start, stop
    first component executed
  Other components
Components
  modules
  configurations
Interfaces: point of access to components
  uses
  provides
Component
A
Component
B
Component D
Component
C
Application
configuration
Component
E
Component F

## Slide 13: nesC Component Types
Components
Configurations
Modules
A collection of other components put together by “wiring” syntax.
Does not use C-like code
Can also provide and use interfaces
Provides, uses, and implements interface(s)
Contains C-like code

## Slide 14: Why modules and configurations?
Allow a developer to “snap together” applications using pre-build components without additional programming.
For example, a developer could provide a configuration that simply wires together one or more pre-existing modules.
The idea is for developers to provide a set of components, a “library,” that can be re-used in a wide range of applications.

## Slide 15: nesC Component
Specification
  Identified by the keyword configuration or module
  List of interfaces that component
    uses, provides
    Alias interfaces as new name
Implementation
  Identified by the keyword implementation
  Defines internal workings
  May include other components and associated “wiring”
Generalized component
Frame
Functions
implementation
provides
uses
Interface_A
Interface_B
NOTE: This model applies to both modules and configurations
configuration|module

## Slide 16: nesC Configuration – A Bare Minimum Configuration
configuration ConfigurationName {
provides interface …;
uses interface …
}
implementation {
// wiring
……
}
Component
provides
configuration
implementation
uses
Interface_A
Interface_B

## Slide 17: nesC Module – A Bare Minimum Module
module ModuleName {
provides interface StdControl;
}
implementation {
// ========== FRAME =========
// ========== FUNCTIONS =====
command result_t StdControl.init() {
return SUCCESS;
}
command result_t StdControl.start() {
return SUCCESS;
}
command result_t StdControl.stop() {
return SUCCESS;
}
}
Component
Frame
Functions
provides
module
implementation
uses
Interface_A
Interface_B

## Slide 18: Example: Blink Configuration
configuration Blink {
}
implementation {
components Main, BlinkM, SingleTimer, LedsC;
Main.StdControl -> SingleTimer.StdControl;
Main.StdControl -> BlinkM.StdControl;
BlinkM.Timer -> SingleTimer.Timer;
BlinkM.Leds -> LedsC;
}

## Slide 19: Example: Blink Module
module BlinkM {
provides {
interface StdControl;
}
uses {
interface Timer;
interface Leds;
}
}
implementation {
command result_t StdControl.init() {
call Leds.init();
return SUCCESS;
}

## Slide 20: Example: Blink Module (cont’d)
command result_t StdControl.start() {
// Start a repeating timer that fires every 1000ms
return call Timer.start(TIMER_REPEAT, 1000);
}
command result_t StdControl.stop() {
return call Timer.stop();
}
event result_t Timer.fired() {
call Leds.yellowToggle();
return SUCCESS;
}
}

## Slide 21: nesC Interface
define “public” methods that a component can use
contain one or more commands and/or events
group functionality, e.g.,
  Standard control interface
  Split-phase operation
interface Send {
command void send(TOS_Msg *m);
event void sendDone();
}
interface StdControl {
command void init();
command void start();
command void stop();
}

## Slide 22: Interface : provides & uses
Provides: Exposes functionality to others
Uses: Requires another component
Interface provider must implement commands
Interface user must implement events
Interface_A
Interface_B
Interface_C
Frame
Functions
Uses
configuration|module
Commands
Event
Events
Command
Provides
Event
Commands

## Slide 23: nesC Interface Examples
module MyAppM {
provides interface StdControl;
uses interface ADC;
uses interface Timer;
uses interface Send;
}
implementation {
…
}
interface StdControl {
command void init();
command void start();
command void stop();
}
interface ADC {
command void getData();
event void dataReady(int data);
}
interface Timer {
command void start(int interval);
command void stop();
event void fired();
}
interface Send {
command void send(TOS_Msg *m);
event void sendDone();
}
Questions: what need to be implemented by MyApp?

## Slide 24: Interfaces: in /MoteWorks/tos/interfaces/

## Slide 25: nesC Module Implementation
Frame
  Global variables and data
  One per component
  Statically allocated
  Fixed size
Functions
  Implementation of:
    Commands, events, tasks
  Commands and Events
  are simply C function calls
Component
Frame
Functions
provides
module
implementation
uses
Interface_A
Interface_B

## Slide 26: Frame
Modules maintain local and persistent state
  Module states or variables are statically allocated
  Each Module has a separate variable name space
  Variables declared in Command and Event are local and allocated on the stack
module fooM {
provides interface I1;
uses interface I2;
}
implementation {
uint8_t count=0;
command void I1.increment() {
count++;
}
event uint8_t I2.get() {
return count;
}
}
Call I1.increment(); //first call
Call I1.increment(); //second call
signal I2.get(); //return 2

## Slide 27: What can a module do?
Calling commands
& signaling events
module MyAppM {
provides interface StdControl;
uses interface Clock;
…
}
implementation {
command result_t StdControl.init(){
call Clock.setRate(TOS_I1PS, TOS_S1PS);
}…
}
Posting tasks
module MyAppM {
…
}
implementation {
task void processing(){
if(state) call Leds.redOn();
else call Leds.redOff();
}
event result_t Timer.fired()
{
state = !state;
post processing();
return SUCCESS;
}…
}

## Slide 28: nesC Configuration
wiring together other components
  No code, just wiring
GenericConfiugration.nc
provides
configuration
uses
Interface_A
Interface_B
configuration D {
provides interface_A;
uses interface_B;
}
implementation {
components C1, C2;
X = C1.X;
X = C2.X;
}
implementation
C1
D
C2
GenericConfiguration.nc

## Slide 29: nesC Wiring Syntax
Binds (connects) the User to an Provider’s implementation
  User.interface -> Provider.interface
  Example
  MyApp_Timer.Timer -> TimerC.Timer[unique("Timer")];
Connected elements must be compatible
  Interface to interface, command to command, event to event
  Example: you can only wire interface Send to Send, but cannot connect Send to Receive

## Slide 30: Three nesC Wiring Statements
Alias or pass through linkage
endpoint1 = endpoint2
Direct linkage, style 1
endpoint1 -> endpoint2
Direct linkage, style 2
endpoint1 <- endpoint2
which is equivalent to: endpoint2 -> endpoint1
configuration C {
provides interface X as Xprovider;
uses interface X as Xuser;
}
implementation {
Xuser = Xprovider;
}
C.nc
C1
D
C2
D1
D2
C

## Slide 31: How mote application starts?
int main() {
call hardwareInit(); //init hardware pins
TOSH_sched_init(); //init scheduler
call StdControl.init(); //init user app
call StdControl.start(); //start user app
while(1) {
TOSH_run_task(); //infinite spin loop for task
}
}

## Slide 32: nesC Filename Convention
nesC file suffix: .nc
C is for configuration (Clock, ClockC)
  “C” distinguishes between an interface and the component that provides it
M is for module (Timer, TimerC, TimerM)
  “M” when a single component has both configuration and module

## Slide 33: Dealing with Concurrency in nesC
TinyOS two execution threads: Tasks and interrupts
  Tasks cannot preempt other tasks
  Interrupts can preempt tasks
Race condition
  Concurrent update to shared state
Any update to shared state that is reachable from asynchronous code is a potential race condition
  Asynchronous code
    Code that is reachable from at least one interrupt handler
  Synchronous code
    Commands, events, or tasks only reachable from tasks

## Slide 34: atomic Keyword
atomic: denote a block of code that runs uninterrupted (interrupts disabled)
  Prevents race conditions
When should it be used?
  Required to update global variables that are referenced in async event handlers
  Must use atomic block in all other functions and tasks where variable is referenced
nesC compiler generates warning messages for global variables that need atomic blocks, e.g.,
SensorAppM.nc:44: warning: non-atomic
accesses to shared variable ‘voltage’

## Slide 35: atomic Keyword (cont’d)
Disables all interrupts, therefore use with caution and intention
Affects code block within {…} that follows it
Useful for locking a resource
Example
Compiles to:
  cli(); // disable interrupts
  lda r1, busy // load busy to register
  jnz r1, inUse // check busy
  str busy, 1 // set busy to true
  inUse:
  sbi(); // enable interrupts
No interrupts will disrupt code flow
  atomic {
    if (!busy)
    busy = TRUE;
  }

## Slide 36: atomic Syntax Example
From MoteWorks/tos/system/TimerM.nc

## Slide 37: async Syntax
async event result_t Clock.fire() {
post HandleFire();
return SUCCESS;
}
tinyos-1.x/tos/system/TimerM.nc
Post task “decouples” the async event
async attribute used to indicate that command or event is part of an asynchronous flow
async processes are “decoupled” by posting a task (to return quickly)

## Slide 38: nesC Features for Concurrency
post
  Puts a function on a task queue
  Must be void foo(void)
atomic
  Turn off interrupts
async
  Use async to tell compiler that this code can be called from an interrupt context – used to detect potential race conditions
norace
  Use norace to tell compiler it was wrong about a race condition existing (the compiler usually suggests several false positives)
task void do-work() { //declares a task that does work}
post do-work();

## Slide 39: Concurrency Example
module SurgeM {…}
implementation {
bool busy;
norace unit16_t sensorReading;
event result_t Timer.fired() {
bool localBusy;
atomic {
localBusy = busy;
busy = TRUE;
}
if(!localBusy) call ADC.getData();
return SUCCESS;
}

## Slide 40: Concurrency Example (cont’d)
task void sendData() {
adcPacket.data = sesnorReading;
call Send.send(&adcPacket, sizeof adcPacket.data);
return SUCCESS;
}
event result_t ADC.dataReady(unit16_t data) {
sensorReading = data;
post sendData();
return SUCCESS;
}
…
}

## Slide 41: nesC Keywords
Keyword | Description
component | Building blocks of a nesC application. Can be a module or a configuration
module | A basic component implemented in nesC
configuration | A component made from wiring other components
interface | A collection of event and command definitions
implementation | Contains code & variables for module or configuration
provides | Defines interfaces provided by a component
uses | Defines interfaces used by a module or configuration
as | Alias an interface to another name
command | Direct function call exposed by an interface
event | Callback message exposed by an interface

## Slide 42: Appendix: TinyOS Programming Tips
  By Phil Levis guide to TinyOS 2.0 Programming Guide
    Note: Not all TinyOS 2.0 concepts apply to MoteWorks
  Last update: June 28, 2006

## Slide 43: TinyOS Programming Hints – Condensed (1 of 4)
Programming Hint 1: It’s dangerous to signal events from commands, as you might cause a very long call loop, corrupt memory and crash your program.
Programming Hint 2: Keep tasks short.
Programming Hint 3: Keep code synchronous when you can. Code should be async only if its timing is very important or if it might be used by something whose timing is important.
Programming Hint 4: Keep atomic sections short, and have as few of them as possible. Be careful about calling out to other components from within an atomic section.
Programming Hint 5: Only one component should be able to modify a pointer’s data at any time. In the best case, only one component should be storing the pointer at any time.

## Slide 44: TinyOS Programming Hints – Condensed (2 of 3)
Programming Hint 6: Allocate all state in components. If your application requirements necessitate a dynamic memory pool, encapsulate it in a component and try to limit the set of users.
Programming Hint 7: Conserve memory by using enums rather than const variables for integer constants, and don’t declare variables with an enum type.
*Programming Hint 8: In the top-level configuration of a software abstraction, auto-wire init to MainC. This removes the burden of wiring init from the programmer, which removes unnecessary work from the boot sequence and removes the possibility of bugs from forgetting to wire.
*Programming Hint 9: If a component is a usable abstraction by itself, its name should end with C. If it is intended to be an internal and private part of a larger abstraction, its name should end with P. Never wire to P components from outside your package (directory).
*TinyOS 2.0 specific

## Slide 45: TinyOS Programming Hints – Condensed (3 of 4)
Programming Hint 10: Use the as keyword liberally.
Programming Hint 11: Never ignore combine warnings.
Programming Hint 12: If a function has an argument which is one of a small number of constants, consider defining it as a few separate functions to prevent bugs. If the functions of an interface all have an argument that’s almost always a constant within a large range, consider using a parameterized interface to save code space. If the functions of an interface all have an argument that’s a constant within a large range but only certain valid values, implement it as a parameterized interface but expose it as individual interfaces, to both minimize code size and prevent bugs.
Programming Hint 13: If a component depends on unique, then #define a string to use in a header file, to prevent bugs from string typos.
*TinyOS 2.0 specific

## Slide 46: TinyOS Programming Hints – Condensed (4 of 4)
*Programming Hint 14: Never, ever use the “packed” attribute.
*Programming Hint 15: Always use platform independent types when defining message formats.
*Programming Hint 16: If you have to perform significant computation on a platform independent type or access it many (hundreds or more) times, then temporarily copying it to a native type can be a good idea.
*TinyOS 2.0 specific