## Slide 1
Tock: A Secure Operating System for Microcontrollers
Amit Levy
Octopi Workshop 10/29/18

## Slide 2: Limitations of Microcontroller Software
USB authentication keys have multiple functions
Sensor networks run several experiments at once
Fitness watches support different activities
Low memory: ~64 kB RAM
No virtual memory
Can’t use Linux!
No isolation
Notes: Linux + Windows entrenched
Microcontrollers totally different beast
So, mismatch, for example

## Slide 3: Multi-User Device: Signpost
Currently deployed @ U.C. Berkeley
Modular city-scale sensing
Tracking Ambient conditions
Pedestrian density
Noise monitoring
8 pluggable modules
Microcontroller + Sensors
Several applications per module

## Slide 4: OTA Updates: Helium
End-to-end IoT “solution”
Programmable module
  Long-range radio
  MCU runs customer services + applications
Abandoned a previous version that used Lua
Next version uses Tock

## Slide 5: Security Sensitive Device: Google Titan
Google’s Titan chip: security hardened MCU
Server root-of-trust, authentication
Without Tock: a handful of experts audit all code
Open source port of Tock started during internship

## Slide 6: Thesis: Embedded Devices are Multiprogrammed
Multiple users running applications concurrently
Applications updated dynamically
  Small payloads better
  Buggy updates shouldn’t brick devices
Security sensitive devices want least privilege

## Slide 7: Tock Embedded OS
Growing open-source community
  883 GitHub followers, >100 mailing list subscribers
  54 contributors (so far) to main project
  ~20 contributors to out-of-tree HW ports
  >100 developers trained at Tock tutorials
Growing HW support
  ARM Cortex-Ms: Atmel SAM4L, Nordic NRF5x, TI CC26xx & TM4C129x, NXP MK66, STM32
  RISC-V port at a secret facility outside Boston

## Slide 8: Multiprograming a Microcontroller
Memory & Performance Isolation
Power & Clock Control
Peripheral communication busses
Future work

## Slide 9: Example: USB Authentication Key
Multiple independent applications
No programmability in favor of security
Result: Handful of programmers control software stack

## Slide 10: Platform (~10 developers)
Build the hardware
Responsible for TCB: core kernel, MCU-specific code
Trusted: complete control over firmware & hardware
Goal: possible to correctly extend TCB

## Slide 11: OS Services (~1000 developers)
Most OS services come community
  Device drivers, networking protocols, timers...
Platform provider can audit but won’t catch all bugs
Goal: protect kernel from safety violations

## Slide 12: Applications (~20M developers)
Implement end-user functionality
“Third-party” developers: unknown to platform provider
Potentially malicious
Goal: end-users can install 3rd-party apps

## Slide 13: Need New Isolation Techniques
With 64 kB, malloc a serious threat to system stability
No virtual memory
Still need to solve driver isolation
  GC’d languages & hardware isolation too resource heavy

## Slide 14: New Tools Available
Memory Protection Unit (MPU)
Protection bits for 8 memory regions
Isolate processes for applications
Rust
Non-GC'd type-safe systems language
Prevent safety violations in kernel at very low cost

## Slide 15: Tock: A Microcontroller OS
Processes: Use the Memory Protection Unit
Capsules: Type-safe Rust API for safe driver development
Grants: Bind dynamic kernel resources to process lifetime

## Slide 16: Tock’s Isolation Mechanisms
Capsules
Rust code linked into kernel
Isolation enforced at compile-time
Lower overhead
Used for device drivers, protocols, timers...
Processes
Standalone executable in any language
Isolation enforced at runtime
Higher overhead
Applications
Trusted for liveness, not safety
Totally untrusted

## Slide 17: Processes
Hardware-isolated concurrent programs in any language
  MPU to protect memory regions without virtualization
  Independent stack, heap, static variables
Run dynamically, compiled with position independent code
Scheduled preemptively
System calls & IPC for communication
Notes: * Similar to processes in other systems
* Each process has dedicated block of memory for…
* Enforced with the hardware
* scheduled preemptively
* Unlike capsules, Instead of methods & references…
* Nice property
* Compared to capsules...

## Slide 18: Process Overhead
Dedicated memory region (at least a stack)
Context switch for communication (340 cycles)
Notes: For operations, like quickly toggling a I/O pin, non-starter
For others, like sending a large string over serial, no biggie
11ms vs. 100us

## Slide 19: Capsules
A Rust module and structs
Single-threaded event-loop with asynchronous I/O
Single stack
No heap
Communicate via references & method calls, often inlined

## Slide 20: Capsule Resource Overhead
 | ROM size (B) | RAM size (B)
Tock | 41744 | 9704
TinyOS | 39604 | 10460
Example 1: “blink”
Example 2: Networked sensor
 | ROM size (B) | RAM size (B)
Tock | 3208 | 916
TinyOS | 5296 | 72

## Slide 21: Capsule Isolation
struct DMAChannel {
length: u32,
base_ptr: *const u8,
}
impl DMAChannel {
fn send_buffer(&self, buf: &'static [u8]) {
self.length = buf.len();
self.base_ptr = buf.as_ref();
}
}
Exposes the DMA base pointer and length as a Rust slice
Type-system guarantees user has access to memory
Won’t be deallocated before DMA completes
Notes: * Example of pretty rich isolation semantics
* From DMA capsule for one of the MCUs
* DMAChannel capsule sets length and base pointer in MMIO registers.
* Don’t want to expose this to clients
* Instead, fields are private, and clients sets buffer through a method that takes a Rust slice.
* Getting the developer to express what they want through types

## Slide 22: Working Example: Software Timer
Software Timer
HW Alarm
Kernel

## Slide 23: Statically allocate timer state?
Software Timer Driver
FAIL
Static allocation must trade off memory efficiency and maximum concurrency
No memory available to handle this request.

## Slide 24: What About Dynamic Allocation?
Software Timer Driver
AES Driver
Bluetooth Driver
FAIL
Can lead to unpredictable shortages.
One process’s demands impacts capabilities of others.
Notes: Lead to unpredictable shortages. Worse, the fault could happen anywhere, including…
Haven’t gotten the right information from developer
Who should be charged for allocation?
When is it safe to free?

## Slide 25: Grants: Per-Process Kernel Heaps
Allocations for one process do not affect others
System proceeds if one grant section is exhausted
All process resources freed on process termination
Grant section
Heap
Data
Stack
Code
RAM
Flash
Process
Accessible
Memory
Notes: Grants solve this problem by…
Kernel heap, called grant section, allocated in process memory, but can’t access

## Slide 26: Grants: Per-Process Kernel Heaps
Software Timer Driver
Grants balance safety and reliability of static allocation with flexibility of dynamic allocation
Notes: * Process requests for timer => new grant allocated
* More than one request? more grants are allocated.
* Memory exhausted? kill the process, no affect on the rest of the system.
* And can restart process immediately
Recall, grant sections live in… but contain kernel data, so… need to make sure...

## Slide 27
Grants use the type-system to ensure references only accessible when process is live
fn enter<'a, F>(&'a self, pid: ProcId, f: F) →
where F: for<'b> FnOnce(&'b mut T)
// Can’t operate on timer data here
timer_grant.enter(process_id, |timer| {
// Can operate on timer data here
if timer.expiration > cur_time {
timer.fired = true;
}
});
// timer data can’t escape here
Notes: Capsules can’t store direct references to granted memory
Instead, the enter the grant section by passing in the id of the process.
Enter checks process is still alive, and executes a closure provided by capsule, passing in a reference to the actual data.
It’s important that this reference not escape, so use a feature of Rust, lifetimes, to enforce this property.

## Slide 28: Grants: No Cross-Process Structures
Shared Heap
Software Timer Driver
Process 2
Process 1

## Slide 29: Grants: No Cross-Process Structures
μS

## Slide 30: Multiprograming a Microcontroller
Memory & Performance Isolation
Power & Clock Control
Peripheral communication busses
Future work

## Slide 31: Power State & Clock Control
Power draw combo of duty cycle and active draw
  What’s the deepest sleep state we can drop to?
  Which clock should drive active peripherals?
Multiprogramming makes both harder!
RCSYS
RCFAST
Impact of Active Clock Selection
Duty Cycle a Function of Workload

## Slide 32: Multiprograming a Microcontroller
Memory & Performance Isolation
Power & Clock Control
Peripheral communication busses
Future work

## Slide 33: Multiprogramming a Peripheral
A platform must support all possible applications
  Efficient protocols may not be so efficient anymore
Peripheral communication not designed for multiprogramming
  How to restart individual components?
  How to isolate services?
  Virtualizing vs. Multiplexing

## Slide 34: Multiprograming a Microcontroller
Memory & Performance Isolation
Power & Clock Control
Peripheral communication busses
Future work

## Slide 35: Future Work
Writing & Enforcing security policies
  For the kernel: language-based capability system?
  For processes: permissions without a file system?
  For networked applications: cryptographic tokens?
Debugging embedded applications
  Security implications
  Logging
More applications, more hardware
  RISC-V, x86
  Wearables, sensor networks, security devices

## Slide 36: Tock: A Secure Operating System for Microcontrollers
Embedded devices are multiprogrammable
  Security, Software Updates, Multi-tenancy
Tension between isolation and resources
  Traditional approaches insufficient for low memory
  New programming languages & hardware features help
Must also rethink: power management, networking, security policies...

## Slide 37: Evaluating with Practitioners
Researchers working with Tock
Half-day tutorials (~100 people)
Open source community (45+ contributors)
Embedded Systems class at Stanford

## Slide 38: Security is an End-to-End Property
Is threat model realistic?
Can system builders extend TCB safely?
Can developers build applications?

## Slide 39: Realistic Threat Model?
 | Signpost | Helium | Titan
Applications | Researchers | Customers | App Developers
Capsules | Module builders | Community, Helium Inc. | Product developers
Platform | Signpost authors | Helium Inc. | Titan team

## Slide 40: Security is an End-to-End Property
Is threat model realistic?
Can system builders extend TCB safely?
Can developers build applications?
✓

## Slide 41: Safely Extend the TCB?
Rule out common errors by design:
Synchronization with interrupt handlers
Untrusted user pointers
Use-after-free

## Slide 42: Tock on Signpost
 | Ambient Module | Audio Module
Process LoC | 6990 | 6688
Capsules LoC | 4479 | 3985
Platform LoC | 3252 | 3244
 | 405 “unsafe” | 381 “unsafe”
Each Signpost module runs a Tock kernel

## Slide 43: Security is an End-to-End Property
Is threat model realistic?
Can system builders extend TCB safely?
Can developers build applications?
✓
✓

## Slide 44: Writing Applications?
Energy consumption on Signpost applications*
*Adkins et al., IPSN’18

## Slide 45: Future Work with Tock
Efficient Clock Management
Can’t statically choose clock domains
Idea: Hide clock choices from app
Low-power wireless networking
6lowpan implementation overheads
Multi-application Bluetooth Low-Energy peripherals
Security Policies
Specify access rights for processes/apps
Enforce high-level policies on capsules
Tagline: An “App Store” for embedded systems

## Slide 46: Teensy (Embedded Systems Class)
Platform LoC | 4055
Unsafe LoC | 170

## Slide 47: Rust Features
Type and memory safe
  No buffer overflows, dangling pointers, type confusion, use-after-free…
Compile-time enforced type system
  No type artifacts at run time
No garbage collection
  Control over memory layout and execution
Runtime behavior similar to C

## Slide 48: Rust’s Ownership
Key Property: Deallocate memory as soon as owner out of scope
{
let x = Resource::new();
}
When the scope exits, x is no longer valid and the memory is “freed”
{
let x = Resource::new();
let y = x;
println!(“{}”, y); // OK: value moved
println!(“{}”, x); // compilation error!
}

## Slide 49: Borrowing
fn transform(x: &mut Resource) {
// the borrow is implicitly released.
}
let mut my_resource = Resource::new();
transform(&mut my_resource);
// my_resource still valid here
Just a pointer at runtime
Mutable references (&mut) must be unique
Shared references (&) cannot mutate the value
Notes: Rust uses this property to get things like thread-safety
But more fundamental requirement

## Slide 50: What About Circular Data-Structures?
SoftwareTimer
VirtualAlarm
Alarm
HWAlarm

## Slide 51: Sum Types vs. Shared Mutability
enum NumOrPointer {
Num(u32),
Pointer(&mut u32)
}
// n.b. will not compile
let external : &mut NumOrPointer;
if let Pointer(internal) = external {
*external = Num(0xdeadbeef);
*internal = 12345;
// Kaboom: we’ve just written ‘12345‘
// to the address ‘0xdeadbeef‘
}
$ rustc test.rs
error[E0506]: cannot assign to ‘external‘
because it is borrowed
Existential types for imperative languages, Dan Grossman, ESOP’02

## Slide 52: Interior Mutability
Safe if we avoid mutability + aliasing concurrently
Examples from Rust core library:
Cell: Copy-in/out or replace, no direct references
Mutex: mutual-exclusion on internal reference
Can write our own with different semantics:
TakeCell: non-blocking mutual-exclusion
  Used in Tock for storing large buffers
Developer expresses: Which part of data is mutable?

## Slide 53
pub struct SoftwareTimer {
alarm: &VirtualAlarm,
...
}
pub struct VirtualAlarm {
next_alarm: Cell<u32>,
alarm: &HWAlarm,
client: &SoftwareTimer,
...
}
pub struct HWAlarm {
regs: [VolatileCell<u32>; 16],
client: &VirtualAlarm,
...
}
SoftwareTimer
VirtualAlarm
Alarm
HWAlarm