## Slide 1: Class 24: Storage
cs4414 Fall 2013
University of Virginia
David Evans

## Slide 3: Why is storage complicated?

## Slide 4: Delay Lines

## Slide 5: Mercury Delay Lines
0/1

## Slide 8: Why Mercury?
0/1
Speed of Sound
Air 343 m/s
Mercury 1450 m/s (40° C)
Water 1500 m/s (25° C)

## Slide 9: Magnetic Core Memory
MIT Project Whirlwind, 1951
2K 16-bit words
with “no waiting”!

## Slide 10: SRAM
NOT
NOT

## Slide 11: Four-Transistor SRAM Bit

## Slide 12
Modern DRAM

## Slide 13: After Turning off Power
5 seconds
30 seconds
5 minutes

## Slide 14
cycles (at 800MHz) to read a particular row = 13.75ns
= 185° F

## Slide 15: Storage Systems
Device | Example | Time to Access | Cost per Bit
Mercury (Gin) Delay Line | UNIVAC (1951) | 220,000ns (average) | $ 0.38 (1968) (a bazillion n$)
DRAM | Kingston KVR16N11/4 4GB DDR3 ($40) | 13.75ns | 1.16 n$
UNIVAC 1968 (Core memory): $823,500 for 131 K 16-bit words

## Slide 16: Cheaper, More Persistent Storage

## Slide 17: How big is a TB?

## Slide 18: Storage Systems
Device | Example | Time to Access | Cost per Bit
Mercury (Gin) Delay Line | UNIVAC (1951) | 220,000ns (average) | $ 0.38 (1968) (a bazillion n$)
DRAM | Kingston KVR16N11/4 4GB DDR3 ($40) | 13.75ns | 1.16 n$
Hard Drive | Seagate Desktop HDD 4 TB SATA 6Gb/s NCQ 64MB | ? | 0.0046 n$

## Slide 19: Accessing a Hard Drive
5900 rpm spindle
“seek time”
~ 0.1ms
rotate time:
1/5900rpm ~ max 10ms

## Slide 20: Passing the Drop Test

## Slide 21: Passing the Drop Test

## Slide 22: Storage Systems
Device | Example | Time to Access | Cost per Bit
Mercury (Gin) Delay Line | UNIVAC (1951) | 220,000ns (average) | $ 0.38 (1968) (a bazillion n$)
DRAM | Kingston KVR16N11/4 4GB DDR3 ($40) | 13.75ns | 1.16 n$
Hard Drive | Seagate Desktop HDD 4 TB SATA 6Gb/s NCQ 64MB | 5ms (ave) | 0.0046 n$

## Slide 23: Storage Abstractions

## Slide 26: Storage Abstractions
Memory Location
File
What about: database, URI?
Do we really need both?

## Slide 27: Unix File Abstraction

## Slide 28: Which are files?
class24.pptx
/Users/dave/OS/classes/
OS-provided random numbers

## Slide 29: “Everything is a File”
class24.pptx
/Users/dave/OS/classes/
OS-provided random numbers
/mnt/cdrom
/dev/tty0
/dev/random

## Slide 30: inode represents a file
Size of File (bytes)
Device ID
User ID
Group ID
File Mode (permission bits)
Link count (number of hard links to node)
…
Diskmap

## Slide 31
include/linux/fs.h

## Slide 32
> stat -x class24.pptx
File: "class24.pptx"
Size: 5855495 FileType: Regular File
Mode: (0644/-rw-r--r--) Uid: ( 501/ dave) Gid: ( 20/ staff)
Device: 1,2 Inode: 6706357 Links: 1
Access: Wed Nov 20 15:00:41 2013
Modify: Wed Nov 20 14:23:13 2013
Change: Wed Nov 20 14:23:13 2013
Size of File (bytes)
Device ID
User ID
Group ID
File Mode (permission bits)
Link count (number of hard links to node)
…
Diskmap
stat

## Slide 33
> ln class24.pptx todays-class.pptx
> stat -x class24.pptx
File: "class24.pptx"
Size: 5855495 FileType: Regular File
Mode: (0644/-rw-r--r--) Uid: ( 501/ dave) Gid: ( 20/ staff)
Device: 1,2 Inode: 6706357 Links: 2
Access: ..
> stat -x todays-class.pptx
File: "todays-class.pptx"
Size: 5855495 FileType: Regular File
Mode: (0644/-rw-r--r--) Uid: ( 501/ dave) Gid: ( 20/ staff)
Device: 1,2 Inode: 6706357 Links: 2
> rm class24.pptx
> stat -x class24.pptx
stat: class24.pptx: stat: No such file or directory
> stat -x todays-class.pptx
File: "todays-class.pptx"
Size: 5855495 FileType: Regular File
Mode: (0644/-rw-r--r--) Uid: ( 501/ dave) Gid: ( 20/ staff)
Device: 1,2 Inode: 6706357 Links: 1

## Slide 34
Removing a linked file like this is very confusing for PowerPoint…

## Slide 35
Size of File (bytes)
Device ID
User ID
Group ID
File Mode (permission bits)
Link count (number of hard links to node)
…
Diskmap
Diskmap
(Unix System 5)
0
1
2
…
9
10
11
12
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)

## Slide 36
Diskmap
(Unix System 5)
0
1
2
…
9
10
11
12
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Indirect
Disk Block (1K bytes)
4 bytes for each = 256 pointers
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)

## Slide 37
Diskmap
(Unix System 5)
0
1
2
…
9
10
11
12
Indirect
Disk Block (1K bytes)
4 bytes for each = 256 pointers
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Double
Indirect
Disk Block
Indirect
Disk Block (1K bytes)
Indirect
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)

## Slide 38
Diskmap
(Unix System 5)
0
1
2
…
9
10
11
12
Indirect
Disk Block (1K bytes)
4 bytes for each = 256 pointers
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Double
Indirect
Disk Block
Indirect
Disk Block (1K bytes)
Indirect
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
How would you determine if your file system has this structure?

## Slide 39
Diskmap
(Unix System 5)
0
1
2
…
9
10
11
12
Disk Block (1K bytes)
Indirect
Disk Block (1K bytes)
4 bytes for each = 256 pointers
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Double
Indirect
Disk Block
Indirect
Disk Block (1K bytes)
Indirect
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)
Disk Block (1K bytes)

## Slide 40: Directories are Files Too!
Filename | Inode
. | 494211
.. | 494205
.DS_Store | 494212
class0 | 6565946
class1 | 6565826
class10 | 1467012
class11 | 2252968
… | …
class19 | 5649155
class2 | 494218
… | …
ls -ali

## Slide 41
> brew install tree # needed on MacOS X, but builtin to most Unixes

## Slide 42: How to create a new file?

## Slide 43: Finding a Free Block
Data
I-List (inodes)
Superblock
Boot block
Not to scale!
0
1
…
98
99
List of free disk blocks
0
1
…
98
99

## Slide 44: Finding a Free inode
Data
I-List (inodes)
Superblock
Boot block
Not to scale!
0 | 0
1 | 1
2 | 0
3 | 0
… | …
Superblock keeps a cache of free inodes

## Slide 45: Modern File Systems

## Slide 46: What should a modern file system do that Unix S5FS doesn’t?

## Slide 47: Handling Failures
ZFS
Developed for Solaris, 2005
Now open source:
http://open-zfs.org/
“MacZFS is free data storage and protection software for all Mac OS users. It's for people who have Mac OS, who have any data, and who really like their data. Whether on a single-drive laptop or on a massive server, it'll store your petabytes with ragingly redundant RAID reliability, and it'll keep the bit-rotted bleeps and bloops out of your iTunes library.”

## Slide 48: Block Checksums
0
1
2
…
9
10
11
12
Disk Block (1K bytes)
S5FS
Block | Checksum (SHA-256)
0 | 40a3dc…
1 | 2c5829d…
2 | 955d253…
… | …
ZFS
How do you check the checksums?

## Slide 49: Hashing the Hashes
Block 1
Block 2
Block 3
Block 4
Hash(B1)
Hash(B2)
Hash(B2)
Hash(B2)

## Slide 50: Merkle Tree
Ralph Merkle
Block 1
Block 2
Block 3
Block 4
Hash(B1)
Hash(B2)
Hash(B2)
Hash(B2)

## Slide 51: Recovery
copies = 2
One Copy
Copy 1
Copy 2
Keep 2 copies of every block: if checksum fails for first copy read, try reading second copy.

## Slide 52
copies = 3
One Copy
Copy 1
Copy 2
For the truly paranoid…
Copy 3

## Slide 53: RAID
For the fairly paranoid but cheap…
Redundant Arrays of Inexpensive Disks
ACM SIGMOD 1988
whitehouse.gov

## Slide 54: Case for RAID

## Slide 56: Redundancy

## Slide 58: Improving Performance
Cache (64MB DRAM)
Adaptive Replacement Cache

## Slide 59: Adaptive Replacement Cache
T1: Recent Cache Entries
Accessed Again
T2: Frequently-Used Blocks
Size of T1 adapts
B1: Evicted from T1 (LRU)
B2: Evicted from T2 (LRU)
How should relative size of T1 and T2 be adjusted?
Blocks in Cache
“Ghost” Entries

## Slide 60: Adaptive Replacement Cache
T1: Recent Cache Entries
Accessed Again
T2: Frequently-Used Blocks
Size of T1 adapts
B1: Evicted from T1 (LRU)
B2: Evicted from T2 (LRU)
Blocks in Cache
“Ghost” Entries
Hit in B1: should increase size of T1, drop entry from T2 to B2
Hit in B2: should increase size of T2, drop entry from T1 to B1

## Slide 61
IBM Almaden Research Center

## Slide 62: Do you actually have a disk like this on your main computing device?
Cache (64MB DRAM)

## Slide 63: Flash Memory
Solid State Drive

## Slide 64: Storage Systems
Device | Example | Time to Access | Cost per Bit
Mercury (Gin) Delay Line | UNIVAC (1951) | 220,000ns (average) | $ 0.38 (1968) (a bazillion n$)
DRAM | Kingston KVR16N11/4 4GB DDR3 ($40) | 13.75ns | 1.16 n$
Hard Drive | Seagate Desktop HDD 4 TB SATA 6Gb/s NCQ 64MB | 5,000,000ns | 0.0046 n$
SSD | Samsung 500GB ($300) | ? | 0.075 n$

## Slide 68: Storage Systems
Device | Example | Time to Access | Cost per Bit
Mercury (Gin) Delay Line | UNIVAC (1951) | 220,000ns (average) | $ 0.38 (1968) (a bazillion n$)
DRAM | Kingston KVR16N11/4 4GB DDR3 ($40) | 13.75ns | 1.16 n$
SSD | Samsung 500GB ($300) | ~10,000 ns (for random read) | 0.075 n$
Disk Drive | Seagate Desktop HDD 4 TB SATA 6Gb/s NCQ 64MB | 5,000,000ns | 0.0046 n$
Modern Hard Drive

## Slide 69: Charge
Storage systems should be designed around hardware capabilities and workload
  Today’s OSes mostly use filesystems designed around 1990s disks and 1960s workloads!
  But, with lots of clever hacks to make them work okay on today’s hardware and workloads
More from Wilkes 1967: