## Slide 1: Understanding and Mitigating Supply Chain Risks for Computing and Communications (or: Who’s Driving Your Missiles?)
David Evans
DSSG Think Piece
University of Virginia

## Slide 2
Federal prosecutors said the three contracted this year to provide integrated circuits to the U.S. Navy and other government agencies. They shipped such circuits to the Navy.
They obtained the counterfeit circuits by importing them from China, the indictment alleges. Prosecutors said they imported more than 10,000 such chips.
Notes: "MVP Micro has added an extra layer of inspection to protect its customers," said MVP Micro Holdings Ceo, Mustafa Aljaff. "We are determined to go above and beyond what our competitors are doing and this x-ray inspection system does just that. This system is the Nexus of our QC process and it allows us to extend the OEM warranty by one full year. You are what you ship and MVP Micro refuses to send out anything that is not to OEM specifications."

## Slide 4: Defense Examples
Cold War Technology Trojans
  Soviets tried to purchase pipeline software from Canadian company, request was denied
  KGB then stole the software – but CIA learned of this and “updated” software
  Trojan software created largest non-nuclear explosion ever, disrupted Soviet gas supply
  Thomas Reed, “At the Abyss: An Insider’s History of the Cold War”
IBM Typewriters delivered to the US Embassy in Moscow
Israel / Syria

## Slide 5: Integrated Circuit Supply Chain (simplified)
Design
Fabrication
Assembly
Deployment
Modern fab: ~$2B
Useful lifetime: ~3 years
Mostly overseas
1964: USAF Minuteman II ICBM – 2-4000 ICs, 40% of cost is electronics
95% of US production of ICs are for DoD
2002: DoD is < 0.5% of world IC market (~$0.5B direct per year)
[Brian Cohen, IDA]
ASIC: Application-Specific Integrated Circuit

## Slide 6: Verifying Ics?
Design
Fabrication
Assembly
Deployment
DARPA: Trust in ICs Program
Verifier

## Slide 7: Impossibility of Black Box Verification
~2100000 possible states, can design malicious logic that is triggered by one specific input

## Slide 8: White Box Verification: DARPA-Hard++
Typical ASIC:
Millions of gates
Only need a few hundred to hide malicious logic
Known and trusted design: automated reverse engineering and inspection

## Slide 9: Trusted Foundry Program
Trusted Foundry
Design
Fabrication
Assembly
Deployment
NSA/DoD program created in 2003
~12 accredited foundries: IBM, Northop Grumman, Sandia, etc.
personnel with access to foundry are cleared
same foundry can produce untrusted ICs
Guidance: all systems of Mission Assurance Category I must use Trusted Foundry (“Systems handling information that is determined to be vital to the operational readiness or mission effectiveness”)
Notes: Systems handling information that is determined to be vital to the operational readiness or mission effectiveness of deployed and contingency forces in terms of both content and timeliness. The consequences of loss of integrity or availability of a MAC I system are unacceptable and could include the immediate and sustained loss of mission effectiveness.

## Slide 10: Issues with Trusted Foundry
Trusted Foundry
Design
Fabrication
Assembly
Deployment
Libraries
Design Tools
Even trusted design relies on libraries, design software, etc. from possibly untrusted sources

## Slide 11: Issues with Trusted Foundry
Trusted Foundry
Design
Fabrication
Assembly
Deployment
How do you know chip is the one that came from the trusted foundry?

## Slide 12: Validating Trusted ICs
Trusted Foundry
Design
Fabrication
Assembly
Deployment
Record properties of trusted chip
Secure Database
interrogate chip

## Slide 13: Chip Verification: Physically Unclonable Functions (PUFs)
Edward Suh (Cornell), Srinivas Devadas (MIT); Verayo
0 1
x0
Challenge
bits
1 0
0 1
1 0
...
...
x1
Challenge bits: which delay path to take
Signals “race” through circuit: outputs 1 if top path is faster, 0 otherwise.

## Slide 14: Using PUFs to Validate Trusted IC
Trusted Foundry
Design
Fabrication
Assembly
Deployment
interrogate chip with set of random PUF challenges
Secure Database
<chipID, <challenge1, response1>
<challenge2, response2>
...
<challengen, response>>
interrogate chip with known challenge and check response

## Slide 15: PUF Security Issues
How hard is it for an attacker to model the PUF?
  More complex PUF designs
  Cryptographic protections (one-way hash) on output
How hard is it for an attacker to tamper with the rest of the chip without effecting the PUF?
  Integrate PUF into circuit (design complexity)
Deployment issues: when and how to validate
Opportunity for continuous end-to-end validation from foundry to deployment.

## Slide 16: Alternate Direction: FPGAs
Custom ASICs
High Cost (application-specific)
High Performance
Fixed logic (not programmable)
General-Purpose Processors
Low Cost (mass market)
Low Performance
Fully programmable
Field-Programmable Gate Arrays

## Slide 17: Secure FPGA
Field-Programmable
Logic
Control Core
Public Key
Bitstream
Encrypted and signed with
Private Key
Trusted Designer
Private Key
Generic, secure FPGA produced by Trusted Foundry

## Slide 18: Advantages of FPGAs
Mass produced FPGA
  One Trusted FPGA design could support many applications
  Performance gap is shrinking (close to ASICs)
Core is simple compared to General-Purpose Processor
  Limit size, can verify small core
Custom logic can be protected
  Removed from chip when vulnerable
Protect and verify bitstream cryptographically
  Public key stored in FPGA core

## Slide 19: Using COTS Equipment
Counterfeit Cisco Routers
Operation “Cisco Raider”: $76M in fake Cisco routers
Top Secret

## Slide 20
Two brothers entered guilty pleas on Tuesday for selling counterfeit “Cisco” products to federal agencies, the U.S. military and others….
Edman’s customers included the Marine Corps, Air Force, FBI, Federal Aviation Administration, Department of Energy, as well as defense contractors…

## Slide 21: Strategies for Using COTS
Limited interface
  Network device to monitor untrusted device
    But how do you trust the monitoring device?
Redundancy
  Multiple devices from disjoint supply chains
  Monitor that they behave “identically”
Avoid targeted attacks
  Sales channel should not know it is going to DoD
  What are the risks for embedding Trojan in design?
Software updates
  Protected by digital signatures…but how are internal processes protected?

## Slide 22: Good News/Bad News?
“It’s certainly possible for the world’s major espionage services to secretly plant vulnerabilities in our microprocessors, but the threat is overblown. Why would anyone go through the effort and take the risk, when there are thousands of vulnerabilities in our computers, networks and operating systems waiting to be discovered with only a few hours work?”
  Bruce Schneier (CTO of BT Counterpane)

## Slide 23: Summary
Trusting ICs is essential: all of our computing and communications depends on them
This is a hard problem: Sophisticated attacker can easily hide a Trojan in IC, cannot be detected by testing
Trusted Foundry: control the supply chain
  Impossible to completely isolate
  Need ways to verify end-to-end trust
  Minimize costs and size of trusted components: generic trusted FPGA, trusted bitstream
COTS equipment
  Avoid targeted attacks

## Slide 24: Thanks!
IDA Mike Adams, Brian Cohen,
Katie Gliwa, Anil Joglekar, Lee Hirsch
NSA Denise Peake, Jeri Selinger
Sandia Chuck Oien, Keith Vanderveen
LLNL Ron Kane, Debbie May
DSSG Mentors and Members