## Slide 1
Liuhua Chen, Haiying Shen and Karan Sapra
Department of Electrical and Computer Engineering, Clemson University
({liuhuac, shenh, ksapra}@clemson.edu)
Background and Motivation
Design Details
Future Work
Distributed Autonomous Virtual Resource Management in Datacenters Using Finite-Markov Decision Process
Experimental Results
To provide robust infrastructure as a service (IaaS), clouds currently perform load balancing by migrating virtual machines (VMs) from heavily loaded physical machines (PMs) to lightly loaded PMs. Previous load balancing methods have the following disadvantages:
A delay to achieve load balance;
No long-term load balance;
High overhead.
To overcome these problems, we propose a proactive Markov Decision Process (MDP)-based load balancing algorithm.
Make our algorithm fully distributed to increase its scalability.
We conducted trace-driven experiments on CloudSim. We implemented two versions: MDP uses the MDP model for identifying VMs to migrate; and MDP* uses the model for both VM selection and PM selection. We compared them with Sandpiper [1] and CloudScale [2].
To handle challenge 2, we carried out experiments to study the transition probability and show that the transition probability matrix remains stable.
Overview:
MDP classifies the resource utilization degree of a PM to states, and treats VM migrations as actions. MDP learns the probabilities of PM state transitions from traces, and computes the optimal polity that PMs should perform in order to achieve maximum rewards.
The optimal policy π is a mapping from states to actions. Following a policy π , every PM:
Determines its current state s;
Executes action π(s);
Periodically go to step 1.
Acknowledgments
Result: MDP*<MDP<CloudScale<Sandpiper
Result: MDP*<MDP<Sandpiper<CloudScale
U.S. NSF grants NSF-1404981, IIS-1354123, CNS-1254006, CNS-1249603, Microsoft Research Faculty Fellowship 8300751.
Challenges:
MDP components must be well designed for low overhead;
Transition probabilities in the MDP must be stable.
Advantages of MDP-based load balancing:
Reduces SLA violations and achieves long-term load balance;
Reduces the overhead and delay;
Build one MDP used by all PMs.
MDP components:
State: classification of resource uti-lization of a PM.
Action: a migration of VM in a certain state (VM-State).
Probability: the probability that state s will transit to state s’ after taking action a.
Reward: given after transition to state s’ from state s by taking action a in order to encourage PMs to become lightly loaded.
Result: MDP*<MDP<Sandpi per<CloudScale
Result: MDP*<MDP<Sandpiper<CloudScale
Chart: Threshold
| 0.7 | 0.8 | 0.9
VM-high | 0.013607 | 0.01 | 0.013889
VM-medium | 0.80695 | 0.77359 | 0.75022
VM-low | 0.39475 | 0.47844 | 0.55429
Figure 2 Probability of state transitions.
Transition Probability
Reward
PM State
PM Action
MDP Model
Optimal Policy π
Check State
Take Action
Periodically
Resource Utilization Monitor
Refer to π
Periodical Update
Figure 1 Overview of MDP-based load balancing.
CPU
MEM
Low
Med
High
Low
Med
High
s9
s6
s3
s8
s5
s2
s7
s4
s1
s1
s2
a1
a2
a2
a1
0.2
0.8
6
-1
0.5
0.5
0.3
0.7
0.4
0.6
-5
8
-2
-3
4
2
Figure 3 Example of a simple MDP.
Chart: VM/PM ratio
| 2.5 | 3 | 3.5
MDP | 479053 | 1524562 | 2900811
MDP* | 241885 | 803167 | 1743471
Sandpiper | 766420 | 2017521 | 3296104
CloudScale | 1625206 | 2300914 | 3946651
Figure 6 The CPU time consumption.
Chart: Totlal number of migrations
| 1.5 | 2 | 2.5
MDP | 17 | 25 | 35
MDP* | 13 | 21 | 31
Sandpiper | 27 | 36 | 47
CloudScale | 31 | 40 | 51
Figure 4 The number of VM migrations
Chart: 
| 1.5 | 2 | 2.5
MDP | 17 | 21 | 24
MDP* | 13 | 17 | 21
Sandpiper | 24 | 29 | 33
CloudScale | 21 | 25 | 28
Figure 5 The number of overloaded PMs.
Chart: VM/PM ratio
| 2.5 | 3 | 3.5
MDP | 2.4244 | 2.9143 | 3.559
MDP* | 2.3133 | 2.5763 | 3.0168
Sandpiper | 2.5591 | 3.1452 | 3.7442
CloudScale | 2.9614 | 3.278 | 4.049
Figure 7 Energy consumption.
To handle challenge 1, our designed MDP intelligently uses a PM load state as a state and records the transitions between PM load states by moving out a VM in a specific load state.
A PM-high has similar probabilities to transit to state medium under slightly varying threshold, when it migrates VM-high, VM-medium and VM-low.
References:
[1] T. Wood, P. J. Shenoy, A. Venkataramani, and M. S. Yousif. Black-box and gray-box strategies for virtual machine migration. In Proc. of NSDI, 2007.
[2] Z. Shen, S. Subbiah, X. Gu, and J.Wilkes. CloudScale: Elastic resource scaling for multi-tenant cloud systems. In Proc. Of SOCC, 2011.